## Slide 1
ECEN 461
Advance Embedded Systems
Real Time Operating Systems – A Review

## Slide 2: Advanced Embedded Systems
Here are the topics we’ll cover
Review RTOS
IOT – Connecting to “the Man”
Signal Processing
Robot Operating System – Example of a large scale System.

## Slide 3: Advanced Embedded Systems
Grading
10 Labs – 40%
5 Quizzes – 20%
Project – RCW Conference – 40%

## Slide 4: Real Time Operating Systems
What is the key aspect of any Operating System?
What does a scheduler do?
  A set of code and data structures that decide which task/process/thread gets time on the processor.
What is a task/process/thread?
  A set of code and data structures that is designed to do “something”. Each task/process/thread has its own Program Counter/Stack Pointer/Register set – this is a execution context.
Scheduler

## Slide 5: Real-Time Operating System (RTOS) Features
What is the difference between a Scheduler and a Round-Robin with Interrupt architecture?
  RR w/Int
    Work is split between ISRs and main thread
    Two contexts – One for the main thread, the other for the ISR. ISRs are non-prememptive.
  RTOS
    Work is split between ISRs and tasks
    Tasks are run in an organized fashion (we can introduce the idea of priority)

## Slide 6: Real-Time Operating System (RTOS) Features
Tasks are run by a scheduler program
  Highest priority task is always the “running” task
    If higher priority task becomes ready to run, other tasks are preempted
  Tasks can block when they are waiting for events
    ISRs can cause tasks to become unblocked
    Tasks can delay themselves for fixed time intervals
RTOS contains code to
  Create tasks
  block and unblock tasks
  schedule tasks
  allow tasks and ISRs to communicate
  etc

## Slide 7: RTOS Application Code: Example
RTOS is essentially a set of objects (data and functions) that can be called from the application code
void vTask1( void *pvParameters );
void vTask2( void *pvParameters );
int main( void )
{
Serial.begin(9600);
/* Create one of the two tasks. */
xTaskCreate( vTask1, "Task 1", 200, NULL, 1, NULL );
/* Create the other task in exactly the same way. */
xTaskCreate( vTask2, "Task 2", 200, NULL, 1, NULL );
/* Start the scheduler so our tasks start executing. */
vTaskStartScheduler();
for( ;; );
return 0;
}

## Slide 8: RTOS Application Code: Example
RTOS is essentially a set of objects (data and functions) that can be called from the application code
void vTask1( void *pvParameters );
void vTask2( void *pvParameters );
int main( void )
{
Serial.begin(9600);
/* Create one of the two tasks. */
xTaskCreate( vTask1, "Task 1", 200, NULL, 1, NULL );
/* Create the other task in exactly the same way. */
xTaskCreate( vTask2, "Task 2", 200, NULL, 1, NULL );
/* Start the scheduler so our tasks start executing. */
vTaskStartScheduler();
for( ;; );
return 0;
}
xTaskCreate ()
  Tasks are the main functions of the
  application software
  Tasks run independently from each other
  The RTOS determines which task will run next
  Each task has its own private context:
    register values
    program counter
    stack
  All other data is shared by all tasks
  Tasks are like Windows/Unix threads

## Slide 9: RTOS Application Code: Example
RTOS is essentially a set of objects (data and functions) that can be called from the application code
void vTask1( void *pvParameters );
void vTask2( void *pvParameters );
int main( void )
{
Serial.begin(9600);
/* Create one of the two tasks. */
xTaskCreate( vTask1, "Task 1", 200, NULL, 1, NULL );
/* Create the other task in exactly the same way. */
xTaskCreate( vTask2, "Task 2", 200, NULL, 1, NULL );
/* Start the scheduler so our tasks start executing. */
vTaskStartScheduler();
for( ;; );
return 0;
}
What do you think vTaskStartScheduler does?

## Slide 10
Heap Memory
Stack Memory
Program Memory
BIOS
Registers
Processor
main()
{
xTaskCreate(1, task1Function);
xTaskCreate(2, task2Function);
vTaskStartScheduler();
}
PC = 000000000
task1Function()
{
while(1)
getValue;
}
task2Function()
{
while(1)
getValue;
}
What happens when you press the power key?
Program Counter goes to 00000000
Processor executes BIOS (Boot Code)
Establishes variables for hardware
- Heap Location
- Stack Location
- HW drivers

## Slide 11
Heap Memory
Stack Memory
Program Memory
BIOS
Registers
Processor
BIOS Variables
main()
{
xTaskCreate(1, task1Function);
xTaskCreate(2, task2Function);
vTaskStartScheduler();
}
PC = main
task1Function()
{
while(1)
getValue;
}
task2Function()
{
while(1)
getValue;
}
xTaskCreate(priority, function pointer)
{
}
After the BIOS the PC goes to main

## Slide 12
Heap Memory
Stack Memory
Program Memory
BIOS
Registers
Processor
BIOS Variables
main()
{
xTaskCreate(1, task1Function);
xTaskCreate(2, task2Function);
vTaskStartScheduler();
}
main stack
readyQueue
blockedQueue
PC = createTask
readyQueue
1, 1, task1Function
0
0
blockedQueue
0
0
0
task1Function()
{
while(1)
getValue;
}
task2Function()
{
while(1)
getValue;
}
xTaskCreate(priority, function pointer)
{
}
task1Stack = task1Function
task1RegisterState
currentTask
0
What does xTaskCreate do?
Adds a Stack Pointer for Task 1
Adds a task1StateContext
Adds Task to readyQueue

## Slide 13
Heap Memory
Stack Memory
Program Memory
BIOS
Registers
Processor
BIOS Variables
main()
{
xTaskCreate(1, task1Function);
xTaskCreate(2, task2Function);
vTaskStartScheduler();
}
main stack
readyQueue
blockedQueue
PC = vStartSchedler
readyQueue
1, 1, task1Function
2, 2, task2Function
0
blockedQueue
0
0
0
task1Function()
{
while(1)
getValue;
}
task2Function()
{
while(1)
getValue;
}
vTaskStartScheduler()
{
setTimer();
scheduler();
}
task1Stack = task1Function
task1RegisterState
currentTask
0
What does vStartScheduler() do?
task2Stack = task2Function
task2RegisterState
Sets Regular Timer for Interrupt
Runs the scheduler for the first time

## Slide 14: Task management
The RTOS scheduler chooses which task to run based on task priority
  The highest priority ready task is always selected
If a task cannot run because it is waiting for something, the task is said to be blocked
Ready
Running
Blocked
Tasks are blocked when they request something that is not available
Only one task can be running at a time
Schedule Task
Preempt Task
Unblock Task
Block Task

## Slide 15: Preemption
A preemptive RTOS will stop the execution of a lower priority task as soon as a higher-priority task becomes ready to run
  Example: highest priority task unblocks when an ISR does a post (sending a message or freeing a semaphore)
A non-preemptive RTOS will stop a task only when that task blocks (e.g., after a pend or delay)

## Slide 16: Task States
Ready
Running
Blocked
Schedule Task
Preempt Task
Unblock Task
Block Task
Interrupted
Interrupt
Return
Preempt Task
(Preemptive RTOS)

## Slide 17: Internal Task Representation
Each task has an OS data structure called a Task Control Block (TCB)
  priority
  pointer to point of execution in task code
  pointer to top of task stack
  other context, status
Kernel code initializes, maintains, and uses TCB contents
Ready Queue: TCBs of all tasks in Ready state
Blocked Queue: TCBs of all tasks in Blocked state

## Slide 18: RTOS Essentials: Scheduler
The scheduler is the kernel routine that decides what to run next
Each task has:
  a unique priority
  a state (running, ready, blocked, interrupted, ...)
The scheduler finds and runs the task with the
  highest priority
  that is ready to run

## Slide 19: An RTOS Scheduler
Schedulers in an RTOS are simple-minded
  Can assume there is always one Ready task
  Not hard to find the one with highest priority
Unlike more complex OSes, the RTOS scheduler does not guarantee fairness
  Low priority tasks can be starved; CPU can be hogged
  Responsibility of application designer (not OS!) to make sure all tasks get what they need

## Slide 20: The Scheduler must also Store/Recall Context
The scheduler’s work is difficult:
  Store the Current Task Context (PC, Register States, Stack)
  Recall the New Task Context
  Pass control to task selected by the scheduler by setting the Program Counter
Must be written in assembly; can’t save context, manipulate stack frames in C

## Slide 21: Context
Each task has its own private context
  Register values
  Stack (including all stack-based variables)
  Program counter
Context must be stored whenever task stops running, be restored by dispatcher when it runs again
Tricky: context must be stored consistently regardless of what caused the task to be suspended
What event sequences can cause task to stop running?
  Something the task did
  Something done by something else in the system. Task? ISR?
How might you save context?
  Options: TCB, stack
  Must be done in assembly

## Slide 22: OS Services
What does the windows/linux OS give you as a user?
file system gui interface
framework to develop code device drivers
memory management etc
An RTOS might provide the following services:
OSInit() OSIntEnter() OSIntExit()
OSMboxCreate() OSMboxPend() OSMboxPost()
OSQCreate() OSQPend() OSQPost()
OSSchedLock() OSSchedUnlock() OSEnterCritical()
OSSemCreate() OSSemPend() OSSemPost()
OSStart() OSTaskChangePrio() OSTaskCreate()
OSTaskDel() OSTimeDly() OSTimeGet()
OSTimeSet() OSTimeTick() OSExitCritical()

## Slide 23: Comparison
RTOS
• Application code and RTOS are compiled and linked together
• The application runs first and calls the RTOS
• RTOS runs only when called by application
• Dedicated to a single embedded application
• Few if any extras
• Designed to run forever without crashing
Windows/Unix
• Application code and OS are separate
• The OS runs first and calls the application
• OS is a separate entity than the processes it runs
• Multi-process, general purpose
• File system, I/O systems, user interface
• Occasionally hangs