## Slide 1
ECEN 361
Real-Time and Embedded Systems
IOT – Internet of Things
Communications

## Slide 2
IOT
Internet of Things
Devices that are always available and always connected

## Slide 3
IOT
Internet of Things
Devices that are always available and always connected
Power
Communications
Information

## Slide 4
IOT - Communications
Internet of Things
Devices that are always available and always connected
Two ways to connect:
Wired
Wireless

## Slide 5
IOT - Communications
Two ways to connect:
Wired
Wireless
Many networks use standard LAN
Some use RS-232 or other low speed serial
Some auto/manufacturing applications use CANBUS.

## Slide 6: What is CANBUS?
CANBUS or CAN bus – Controller Area Network bus
An automotive serial bus system developed to satisfy
the following requirements:
  Network multiple microcontrollers with 1 pair of wires.
  Allow microcontrollers communicate with each other.
  High speed, real-time communication.
  Provide noise immunity in an electrically noisy environment.
  Low cost

## Slide 7: Who uses CANBUS?
Designed specifically for automotive applications
Today - industrial automation / medical equipment
Chart: CANBUS Market Distribution
| Automotive | Medical / Industrial
 | 0.8 | 0.2

## Slide 8: CANBUS History
First idea - The idea of CAN was first conceived by engineers at Robert Bosch Gmbh in Germany in the early 1980s.
Early focus - develop a communication system between a number of ECUs (electronic control units).
New standard - none of the communication protocols at that time met the specific requirements for speed and reliability so the engineers developed their own standard.

## Slide 9: CANBUS Timeline
1983 : First CANBUS project at Bosch
1986 : CAN protocol introduced
1987 : First CAN controller chips sold
1991 : CAN 2.0A specification published
1992 : Mercedes-Benz used CAN network
1993 : ISO 11898 standard
1995 : ISO 11898 amendment
Present : The majority of vehicles use CAN bus.

## Slide 10: CANBUS and the OSI Model
CAN is a closed network
  – no need for security, sessions or logins.
  - no user interface requirements.
Physical and Data Link layers in silicon.

## Slide 11: CANBUS Physical Layer
Conventional multi-wire looms
CAN bus network
Physical medium – two wires terminated at both ends by resistors.
Differential signal - better noise immunity.
Benefits:
  Reduced weight, Reduced cost
  Fewer wires = Increased reliability
vs.
http://canbuskit.com/what.php

## Slide 12: Transmission Characteristics
Up to 1 Mbit/sec.
Common baud rates: 1 MHz, 500 KHz and 125 KHz
All nodes – same baud rate
Max length:120’ to 15000’ (rate dependent)
© esd electronics, Inc. • 525 Bernardston Road • Greenfield, MA 01301

## Slide 13: Message Oriented Transmission Protocol
Each node – receiver & transmitter
A sender of information transmits to all devices on the bus
All nodes read message, then decide if it is relevant to them
All nodes verify reception was error-free
All nodes acknowledge reception
CAN bus
© 2005 Microchip Technology Incorporated. All Rights Reserved.

## Slide 14
IOT - Communications
Two ways to connect:
Wired
Wireless
Lots of choices:
915 MHz dedicated Link
Bluetooth
WLAN
Zigbee

## Slide 15
IOT - Communications

## Slide 16
IOT - Communications
Mesh Networks

## Slide 17
IOT - Communications
Mesh Networks

## Slide 18
IOT - Communications
Gateway Devices

## Slide 19
802.15.3
UWB
Wireless Communications Standards Gateway Link
10 kbits/s
100 kbits/s
1Mbits/s
10 Mbits/s
100 Mbits/s
Débit
Distance
Text
Graphics
Internet
HiFi Audio
Video
streaming
Digital
Video
Multi-channel
Video
1 m
10 m
100 m
1 km
10 km
100 km
BAN
PAN
LAN
WAN
802.11.a/b/g
Wi-Fi/HL
802.15.1
Bluetooth
802.15.4
Zigbee, UWB
GSM/CDMA
GPRS/3G
LMDS
802.16
WI-Max

## Slide 20
IOT
Internet of Things
Devices that are always available and always connected
Power
Communications
Information

## Slide 21
IOT
Internet of Things
Devices that are always available and always connected
What is the information that we receive from the sensor?
Simple Voltage
Packets of Data
Video