## Slide 1: ECEN 150 Circuit Analysis I
First-Order Circuits

## Slide 2: Source-Free RC Circuit
Assume C is charged to Volts at t = 0-.
KCL:
-
Discharge equation for a source-free RC circuit.
This is referred to as the natural response of the circuit, and is referred to as the time constant. Larger results in longer discharge time.
Notes: Image by instructor.

## Slide 3
e-x is bounded between 1 and 0.
Adjacent graph shows amplitude from 100% to 0%.
e-x – Important Function in STEM
(1 - e-x ) is bounded between 0 and 1.
Adjacent graph shows amplitude from 0% to 100%.

## Slide 4: Exponential Decay and Time Constants
Time t in terms of time constant |  | Percent of Initial Value, i.e.
t = 0 | = 1.000 | 100
t = 1 | = 0.3679 | 36.79
t = 2 | = 0.1353 | 13.53
t = 3 | = 49.79 x 10-3 | 4.979
t = 4 | = 18.32 x 10-3 | 1.832
t = 5 | = 6.738 x 10-3 | 0.6738
t = 6 | = 2.479 x 10-3 | 0.2479
t = 7 | = 911.9 x 10-6 | 0.09119
t = 8 | = 335.5 x 10-6 | 0.03355
t = 9 | = 123.4 x 10-6 | 0.01234
t = 10 | = 45.40 x 10-6 | 0.004540
 |  | 100
 |  | 36.79
 |  | 13.53
 |  | 4.979
 |  | 1.832
 |  | 0.6738
 |  | 0.2479
 |  | 0.09119
 |  | 0.03355
 |  | 0.01234
 |  | 0.004540
Exponential Decay

## Slide 5: Source Free RC Circuit Example 1
  The capacitor C is initially charged to 1.0 V in the adjacent circuit,
  i.e., Vo = 1.0 V. Determine the current iR3(t) at time t = 1 ms.
Discharge equation for a source-free RC circuit.
Notes: Image by instructor.

## Slide 6: Source Free RC Circuit Example 2
  The adjacent circuit has R = 390 Ω and C = 2.7 µF and initial capacitor voltage Vo = 1 V.
  Calculate the time for the voltage v(t) to decay to 0.25 V.
Discharge equation for a source-free RC circuit.
Solve for .
This circuit will discharge from 1.0 V to 0.25 V in t =1.46 ms.
Check:
Poll Questions
Notes: Image by instructor.

## Slide 7: 74VHCxx Digital Logic IC Fall Time
74VHCxx Digital Logic IC’s are
powered by a positive supply voltage
called VDD, often equal to 5.0 V. The
zero level for VHC logic has been
defined as ≤ 30% of VDD, which for
VDD = 5.0 V is ≤ 1.5 V.
How many RthCstray time constants
are necessary to provide an acceptable “zero” level to
74VHCxx digital logic starting from a “one” level of VDD?
Notes: Image by instructor.

## Slide 8: RC Discharging Waveforms
For the RC circuit below, capacitor C is fully charged
prior to switch S1 opening at time t = 0-, followed by
switch S2 closing at time t = 0. (Break before make).
Sketch the and waveforms for the first 5 time
constants for t ≥ 0.
Because of switch S1 closed prior t = 0,
Resistor voltage: .
Resistor Current: .
Capacitor voltage cannot change instantaneously, although capacitor current can change instantaneously.
Notes: Images by instructor.

## Slide 9: Source-Free RL Circuit
Assume inductor current equals Amps at t = 0-.
KVL: ,
Discharge equation for a source-free RL circuit.
This is referred to as the natural response of the circuit, and is referred to as the time constant.
Notes: Image by instructor.

## Slide 10: Source Free RL Circuit Example 1
  The initial inductor current Io in the adjacent circuit is 1 mA towards R3.
  Determine the voltage vR3(t) at time t = 50 µs.
Discharge equation for a source-free RL circuit.
This implies an infinite time constant for a zero resistance circuit. How can this be?
The discharging inductor has some initial Io current flowing through it at t = 0. For an ideal inductor and a zero resistance circuit, Io would continue to flow forever because of no opposition voltage required, i.e., . However, practical circuits have non-zero resistance, eliminating the possibility of perpetual inductor current. The inductor current time constant decreases with increasing circuit resistance because the associated increasing opposition voltage implies increasing . The larger is during discharge, the shorter the time constant .
Notes: Image by instructor.

## Slide 11: Inductors – Oppose Changes in Current.
Voltage across an inductor:
If current is constant, voltage is _________.
For constant current, an INDUCTOR behaves just like a/an _______ circuit.

## Slide 12: Capacitors – Oppose Changes in Voltage.
Charging current of a capacitor:
If voltage is constant, charging current is _________.
For constant voltage, a CAPACITOR behaves just like a/an ________ circuit.

## Slide 13: Step Response of a Series RC Circuit
Assume switch closure at time t = 0.
Because capacitors have voltage inertia. Charge transfer from one capacitor plate to the other has to occur before the capacitor voltage changes. Since this charge transfer takes time, the voltage across the capacitor is the same immediatly after switch closure as it was before switch closure.
v(t)
Vo
t
0
Notes: Image by instructor.

## Slide 14: Step Response of a Series RC Circuit (Continued)
From the previous page, the step response of a series
RC circuit for t ≥ 0 is given as:
where
Vo is initial voltage across the capacitor, and equal to v(0).
Capacitor will eventually charge to the voltage Vs and therefore equal to v(∞).
Can view this response as having a steady-state portion along with a transient portion .
. Rising Exponential.
Notes: Image by instructor.

## Slide 15: Step Response of a Series RL Circuit
Assume switch closure at time t = 0.
In adjacent circuit
In the general
Steady-state + transient currents.
.
Assume exponential solution:
and .
.
. Rising exponential.
Notes: Image by instructor.

## Slide 16: Exponential Rise and Time Constants
Time t in terms of time constant |  | Percent of Final Value, i.e.
t = 0 | = 0.000 | 0.000
t = 1 | = 0.6321 | 63.21
t = 2 | = 0.8647 | 86.47
t = 3 | = 0.9502 | 95.02
t = 4 | = 0.9817 | 98.17
t = 5 | = 0.9933 | 99.33
t = 6 | = 0.9975 | 99.75
t = 7 | = 0.9991 | 99.91
t = 8 | = 0.9997 | 99.97
t = 9 | = 0.9999 | 99.99
t = 10 | ≈ 1.000 | 100
 |  | 0.000
 |  | 63.21
 |  | 86.47
 |  | 95.02
 |  | 98.17
 |  | 99.33
 |  | 99.75
 |  | 99.91
 |  | 99.97
 |  | 99.99
 |  | 100
Exponential Rise

## Slide 17: Capacitor Charging Example
For the adjacent series RC circuit with switch closure at
time t = 0, with Vs = 10 V, and what is
for times of 1 and 5 time constants?
For 1 time constant,
For 5 time constants,
Since resulting value is within 1% of final value after 5 time constants, 5 time constants or 5τ is often used as a desired settling time value in transient circuits.
Notes: Image by instructor.

## Slide 18: Capacitor Charging Time
For the adjacent series RC circuit with switch closure at time t = 0, derive an
expression for time t in terms of , and τ, given v(0) = 0.
Example: For the above circuit with R = 470 Ω and C = 2.7 µF. Calculate the time for the capacitor to reach 90% of maximum voltage after switch closure for v(0) = 0.
  =
Notes: Image by instructor.

## Slide 19: 74VHCxx Digital Logic IC Rise Time
74VHCxx Digital Logic IC’s are
powered by a positive supply voltage
called VDD, often equal to 5.0 V. The
one level for VHC logic has been
defined as ≥ 70% of VDD, which for
VDD = 5.0 V is ≥ 3.5 V.
How many time constants are necessary to provide an
acceptable “one” level to 74VHCxx digital logic starting from
a “zero” level of 0 V?
Notes: Image by instructor.

## Slide 20: RC Charging Waveforms
For the series RC circuit below, sketch the waveforms
for , and for the first 5 time constants
after switch closure occurring at time t = 0, for v(0-) = 0 V.
Resistor and capacitor current: .
Resistor voltage: .
Notes: Images by instructor.

## Slide 21: Inductor Current Ramp-Up Example
For the adjacent series RL circuit with switch closure at
time t = 0, with Vs = 10 V, and R = 100 Ωwhat is
for times of 1 and 5 time constants?
Because of the open switch,
For 1 time constant,
For 5 time constants,
Since resulting value is within 1% of final value after 5 time constants, 5 time constants or 5τ is often used as a desired settling time value in transient circuits.
Poll Questions
Notes: Image by instructor.

## Slide 22: RL Circuit Ramp-Up Time
For the adjacent series RL circuit with switch closure at time t = 0,
derive an expression for time t in terms of , R, and τ.
Because of the open switch,
  Example: For the above circuit with R = 100 Ω and L = 100 mH. Calculate the time for the inductor current to reach 80% of maximum current after switch closure. This means i(t)R equals 80% of VS.
  = ==
Notes: Image by instructor.

## Slide 23: RL Current Ramp-Up Waveforms !!!!
For the series RL circuit below, sketch the waveforms
for , and for the first 5 time constants
after switch closure occurring at time t = 0
Because of the open switch,
Inductor Voltage: .
Resistor voltage: .
Time
t = 0
5τ
Time
t = 0
5τ
Time
t = 0
5τ
Notes: Images by instructor.

## Slide 24: Open Circuiting an Inductive Circuit
Switch going from closed to open:
Abrupt interruption of i(t), i.e., large results
in large counter emf from inductor that tries to force
current to remain the same as before the switch was
opened.
Counter emf may cause arcing across switch contacts.
Protective circuitry needed to protect switches that open circuits with significant inductance.
Notes: Image by instructor.

## Slide 25: Ignition Coil
The ignition coil is essentially a high-voltage step-up transformer made up of two coils of wire. One coil of wire is called the primary coil. Wrapped around it is the secondary coil. The secondary coil normally has hundreds of times more turns of wire than the primary coil. Current flows from the battery through the primary winding of the coil.
The key to the coil's operation is what happens when the circuit is suddenly opened by the points. The magnetic field surrounding the secondary coil changes rapidly, inducing very high voltage in the secondary coil, (greater than 20,000 volts) because of the number of coils in the secondary winding.
By Honda CB77 Restoration [CC BY 2.0 (http://creativecommons.org/licenses/by/2.0)], via Wikimedia Commons
Ignition Coil Video. (4:06)
Notes: By Honda CB77 Restoration [CC BY 2.0 (http://creativecommons.org/licenses/by/2.0)], via Wikimedia Commons

## Slide 26
The End

## Slide 27
Extra

## Slide 28: Source-Free RC Circuit
Assume C is charged to VO Volts at t = 0-.
KCL: ,
Discharge equation for a source-free RC circuit.
This is referred to as the natural response of the circuit, and is referred to as the time constant. Larger results in longer discharge time.
Notes: Image by instructor.

## Slide 29: Step and Impulse Functions
Unit step and impulse functions are mathematically useful functions used in signal analysis.
Unit step function u(t) useful to model closing a switch and energizing a circuit.
Unit impulse function used as mathematical input to systems, with the resulting impulse response providing useful information about the response time and stability of the system.
Unit Step: u(t)
0
t
u(t)
1
Unit Impulse: (t)
0
t
(t)
Derivative

## Slide 30: Step Response of a Series RC Circuit
Assume switch closure at time t = 0.
KCL:
What happens at t = 0, since formally u(t) is undefined at t = 0, and equals 1 for t > 0?
So while u(t) is undefined for t = 0, in the above RC circuit, v(t = 0) = v(t = 0+) because of the capacitor. Hence, for t ≥ 0.
v(t)
Vo
t
0
Notes: Image by instructor.

## Slide 31: Step and Impulse Functions (Continued)
Adding the time to to the argument advances the step or impulse in time by to.
Subtracting the time to from the argument delays the step or impulse in time by to.
Unit Step: u(t + to)
0
t
u(t + to)
1
Unit Impulse: (t - to)
0
t
(t - to)
to
-to
0
t
to
u(t - to)
Unit Step: u(t - to)
1
Unit Impulse: (t + to)
0
t
(t + to)
-to

## Slide 32: ex – Important Function in STEM
-
ex is bounded between 0 and infinity.
(STEM – Science, Technology, Engineering & Math)