## Slide 1: SPICE
Simulation Program with Integrated Circuit Emphasis
Originally developed at EE Berkeley
Uses mathematical models to describe circuit elements
SPICE3 is the latest variant.
  - It allows DC and time transient analysis of nonlinear circuits (transistors, diodes, capacitors, etc., also digital circuitry)
  - Command line driven interface
  - Available in public domain (written in C)
  - Has become de-facto the industry standard
  - Many spin-offs exist (use modified SPICE2 or SPICE3 as their engine), such as HSPICE, PSPICE, WinSPICE (commercial)

## Slide 2: LTspice
A freeware circuit simulator (Windows or *nix/Wine)
Mac users: install http://winebottler.kronenberg.org/
Netlist syntax is powerful but hard to visualize
LTspice has schematic capture and is much easier to use than traditional text-based SPICE. The user can enter a circuit to be simulated via a graphical user interface
Has virtual scope, makes Bode plots, performs FFT, etc.
Worth learning about
  It is fast, expandable, powerful, and free
  Most widely used noncommercial CAD electronics software

## Slide 3
Analog Devices (www.analog.com)

## Slide 4
To begin drawing the circuit, click New Schematic, or Ctrl+N
Enable grid if not shown by clicking Ctrl+G

## Slide 5
wire
ground (required)
“Component”
To add a component, click on the corresponding icon
Component button contains slew of predefined components: voltage and current sources; transistors; opamps; gates; user-defined stuff
You can Delete (F5 or Ctrl-X) and Move (F7) components, as well as Drag (F8) them (keep the wires connected)

## Slide 6
To rotate the component prior to placing press Ctrl-R
To mirror the component prior to placing press Ctrl-E

## Slide 7
Right-click to enter component value

## Slide 8: Toolbar Summary
Place Circuit Element
Draw Wire
Place Ground
Label Node
Place Resistor
Place Capacitor
Place Inductor
Place Diode
Move
Drag
Undo
Redo
Rotate
Mirror
Place Comment
Place SPICE Directive
Zoom In
Pan
Zoom Out
Auto Scale
Delete
Copy
Paste
Find
Simulate

## Slide 9: Prompt Sheet from LTspiceIV_flyer.pdf

## Slide 10: Prefixes are case insensitive: T = t, G = g, and so on
T = terra = 1012
G = giga = 109
MEG = meg = 106
K = kilo = 103
M = milli = 10-3
U = micro = 10-6
N = nano = 10-9
P = pico = 10-12
F = femto = 10-15
No need to enter units, they are assumed (e.g. “1M” is 1mV if entered for voltage, 1ms if entered for time, etc.)

## Slide 11: Few gotchas
“M” and “m” are interpreted the same by SPICE. Thus, a resistor value of 10M is the same as 10m (ten milliohms)
  Use 10MEG (or 10E6) to specify ten megohms
Do not enter “1F” or “1f” as the capacitance for a one-farad capacitor (enter “1”). “F” and “f” designate the prefix femto (10-15)
When simulating astable circuits (multivibrator), specify some small nonzero initial voltage in the positive feedback to seed the oscillations
Initial conditions SPICE directive

## Slide 12: Nodal Analysis Example
For the adjacent circuit shown, solve for voltages
v1 and v2 using KCL nodal analysis.
Node v2: i1 = i2 + i3. (vs1 – v2)/R1 = v2 /R2 + (v2 – v3)/R3.
(Equation 1): To simplify, scale by 1000. 17.1 v2 – 5.00 v3 = 160.
Node v3: I3 + I5 = I4. (Va – Vb)/R3 + (V2 – Vb)/R5 = Vb/R4. i3 + i5 = i4.
(v2 – v3)/R3 + (v2 - vs2)/R5 = v3 /R4.
(Equation 2): To simplify, scale by 1000. -5.00 v2 + 16.9 v3 = 109.
Simultaneous Solutions: v2 = 12.3 V. v3 = 10.0 V.
Notes: Image by instructor

## Slide 13: Nodal Analysis Example (Continued)
LTspice .op (Operating Point) analysis solves for all voltages and currents in < 2 seconds.
Notes: Image by instructor

## Slide 14: LTspice DC Sweep
LTspice .step param, sweeps parameter R from 0.1 Ω to 100 Ω in 0.1 Ω steps, determining voltages and currents at each R value.
Plot pane allows viewing of all voltages and currents, and expressions, which is the above example is p = vloadiload.
Cursors allow reading of data point values and differences between data point values.
Notes: Image by instructor

## Slide 15: Two examples
We will look at how to setup two examples
  Example1: crossover corrected push-pull amp (ex6.10)
  Example2: active filter
Any additional files not included with LTspice but required for this course are found under Spice models on the Blackboard.

## Slide 16
First, create the circuit (you may want to use Ctrl-E, Ctrl-R to mirror and rotate the symbols for best orientation)
Next, specify component values for resistors, DC voltages by right-clicking on the elements (be careful, sometimes you may click on the name thinking you are changing the value).
First example demonstrates transient analysis

## Slide 17: Assigning Vin
Right-click on Vin, then click Advanced. You will see a window like this. Choose SINE Function.
Enter:
DC offset[V] : 0
Amplitudep[V]: 0.05
Freq[Hz]: 100
Tdelay[s]: 20m

## Slide 18: Assigning Diodes and Transistors
If you do not assign diode and transistors, LTspice will use some default models. It may be OK for a simple circuit like the one we are looking at. Real-life situations require more accurate model specific to the actual component being used. E.g. to assign a specific diode model, right-click on it, then click “Pick New Diode” and choose IN914.

## Slide 19: Assigning Transistors and opamp
Similarly, assign the transistors to be 2N3904 and 2N3906
Note: you will find some familiar components missing (e.g. LM741 op-amp); you have to add them to LTspice
All major manufacturers will have SPICE model files online

## Slide 20: How to add LM741
Google for LM741, you will get to the manufacturer’s web-site with link to Model file LM741.MOD
Download it, it is an ASCII file in SPICE format:
it comes from National Semiconductor
component model describes frequency response, input and output impedance, etc. can be a subcircuit that includes other elements

## Slide 21: How to add LM741
Place this file where LTspice will look for it, preferably in the local directory (where you circuit file is saved)
Add generic opamp (opamp2) to your circuit
Right-click on the symbol to invoke Component Attribute Editor
Enter Value = LM741/NS (must match the first line in LM741.MOD file, which is not a comment, i.e. not preceded by *, something like .SUBCKT LM741/NS …)
Add SPICE directive

## Slide 22: Time Transient Analysis
Choose Simulate  Edit Simulation Cmd
Indicate Stop Time of 0.1 s
Click OK and place SPICE directive somewhere on your circuit
Ready to go!

## Slide 23: Looking at the result
LTspice has nice tools to look at the waveforms, voltages or currents, FFT (Fourier Analysis), gain amplitude and phase (in AC analysis)
You can open multiple panes, plot signals versus time or signal versus another signal
You can zoom in, zoom out, also activate scope-like cursor(s) for more accurate measurements on waveforms
By default the mouse cursor transforms into voltage probe , however, when hovering over a component (or pressing Alt over wire), it transforms into current probe
Pressing Alt over an element will report instantaneous power drawn by the element (thermometer icon)

## Slide 24
Second example will demonstrate AC analysis
Use ideal opamp from the list of components
Must include with this opamp!

## Slide 25: Assigning Vin
Right-click on Vin, then click Advanced. Use Small signal AC analysis section.
AC amplitude 1 volt

## Slide 26: AC Analysis
Choose Simulate  Edit Simulation Cmd
On AC analysis tab specify type of sweep (decade), number of points per decade, initial and final frequencies
Click OK, plant SPICE directive somewhere
Ready to go!

## Slide 27
Click on Vout to display Bode plot

## Slide 28: Additional resources
Yahoo! LTspice group (great resource, kept active by many thousands of users)