## Slide 1
ECEN 361
Real-Time and Embedded Systems
Lecture 11 – FreeRtos (cont)

## Slide 2: Outline
Quick review of real-time systems
Overview of RTOSes
  Goals of an RTOS
  Features you might want in an RTOS
Learning by example: FreeRTOS
  Introduction
  Tasks
  Interrupts
  Internals (briefly)
  What’s missing?

## Slide 3: FreeRTOS Features
  Source code
  Portable
  Romable
  Scalable
  Preemptive and co-operative scheduling
  Multitasking
  Services
  Interrupt management
  Advanced features

## Slide 4: Source Code
  High quality
  Neat
  Consistent
  Organized
  Commented

## Slide 5: Portable
  Highly portable C
  24 architectures supported
  Assembly is kept minimum.
  Ports are freely available in source code.
  Other contributions do exist.

## Slide 6: Scalable
  Only use the services you only need.
    FreeRTOSConfig.h
  Minimum footprint = 4 KB
  Version in lab is 24 KB including the application (which is fairly large) and data for the OS and application.
    Pretty darn small for what you get.
    ~6000 lines of code (including a lot of comments, maybe half that without?)

## Slide 7: Preemptive and Cooperative Scheduling
  Preemptive scheduling:
    Fully preemptive
    Always runs the highest priority task that is ready to run
    Comparable with other preemptive kernels
    Used in conjunction with tasks
  Cooperative scheduling:
    Context switch occurs if:
      A task/co-routine blocks
      Or a task/co-routine yields the CPU
    Used in conjunction with tasks/co-routines

## Slide 8: Multitasking
  No software restriction on:
    # of tasks that can be created
    # of priorities that can be used
    Priority assignment
      More than one task can be assigned the same priority.
      RR with time slice = 1 RTOS tick

## Slide 9: Services
  Queues
  Semaphores
    Binary and counting
  Mutexes
    With priority inheritance
    Support recursion

## Slide 10: Interrupts
  An interrupt can suspend a task execution.
  Interrupt mechanism is port dependent.

## Slide 11: Advanced Features
  Execution tracing
  Run time statistics collection
  Memory management
  Memory protection support
  Stack overflow protection

## Slide 12: Device support in related products
  Connect Suite from High Integrity Systems
    TCP/IP stack
    USB stack
      Host and device
    File systems
      DOS compatible FAT

## Slide 13: Licensing
  Modified GPL
    Only FreeRTOS is GPL.
    Independent modules that communicate with FreeRTOS through APIs can be anything else.
    FreeRTOS can’t be used in any comparisons without the authors’ permission.

## Slide 14: A bit more
System runs on “ticks”
  Every tick the kernel runs and figures out what to do next.
    Interrupts have a different mechanism
  Basically hardware timer is set to generate regular interrupts and calls the scheduler.
    This means the OS eats one of the timers—you can’t easily share.
OK, onto tasks!

## Slide 15: Outline
Quick review of real-time systems
Overview of RTOSes
  Goals of an RTOS
  Features you might want in an RTOS
Learning by example: FreeRTOS
  Introduction
  Tasks
  Interrupts
  Internals (briefly)
  What’s missing?

## Slide 16: Tasks
Each task is a function that must not return
  So it’s in an infinite loop (just like you’d expect in an embedded system really, think Arduino).
You inform the scheduler of
  The task’s resource needs (stack space, priority)
  Any arguments the tasks needs
All tasks here must be of void return type and take a single void* as an argument.
  You cast the pointer as needed to get the argument.
    I’d have preferred var_args, but this makes the common case (one argument) easier (and faster which probably doesn’t matter).
Code examples mostly from Using the FreeRTOS Real Time Kernel (a pdf book), fair use claimed.

## Slide 17: Example trivial task with busy wait (bad)

## Slide 18: Task creation
portBASE_TYPE xTaskCreate(
pdTASK_CODE pvTaskCode,
const char * const pcName,
unsigned short usStackDepth,
void *pvParameters,
unsigned portBASE_TYPE uxPriority,
xTaskHandle *pvCreatedTask
);
Create a new task and add it to the list of tasks that are ready to run. xTaskCreate() can only be used to create a task that has unrestricted access to the entire microcontroller memory map. Systems that include MPU support can alternatively create an MPU constrained task using xTaskCreateRestricted().
pvTaskCode: Pointer to the task entry function. Tasks must be implemented to never return (i.e. continuous loop).
pcName: A descriptive name for the task. This is mainly used to facilitate debugging. Max length defined by tskMAX_TASK_NAME_LEN – default is 16.
usStackDepth: The size of the task stack specified as the number of variables the stack can hold - not the number of bytes. For example, if the stack is 16 bits wide and usStackDepth is defined as 100, 200 bytes will be allocated for stack storage.
pvParameters: Pointer that will be used as the parameter for the taskbeing created.
uxPriority: The priority at which the task should run. Systems that include MPU support can optionally create tasks in a privileged (system) mode by setting bit portPRIVILEGE_BIT of the priority parameter. For example, to create a privileged task at priority 2 the uxPriority parameter should be set to ( 2 | portPRIVILEGE_BIT ).
pvCreatedTask: Used to pass back a handle by which the created task can be referenced.
pdPASS: If the task was successfully created and added to a ready list, otherwise an error code defined in the file errors.h
From the task.h file in FreeRTOS

## Slide 19: Creating a task: example

## Slide 20: OK, I’ve created a task, now what?
Task will run if there are no other tasks of higher priority
  And if others the same priority will RR.
But that begs the question: “How do we know if a task wants to do something or not?”
  The previous example gave always wanted to run.
    Just looping for delay (which we said was bad)
    Instead should call vTaskDelay(x)
      Delays current task for X “ticks” (remember those?)
    There are a few other APIs for delaying…
Now we need an “under the hood” understanding

## Slide 21: Task status in FreeRTOS
Running
  Task is actually executing
Ready
  Task is ready to execute but a task of equal or higher priority is Running.
Blocked
  Task is waiting for some event.
    Time: if a task calls vTaskDelay() it will block until the delay period has expired.
    Resource: Tasks can also block waiting for queue and semaphore events.
Suspended
  Much like blocked, but not waiting for anything.
  Tasks will only enter or exit the suspended state when explicitly commanded to do so through the vTaskSuspend() and xTaskResume() API calls respectively.
Mostly from http://www.freertos.org/RTOS-task-states.html

## Slide 22: Tasks: there’s a lot more
Can do all sorts of things
  Change priority of a task
  Delete a task
  Suspend a task (mentioned above)
  Get priority of a task.
Example on the right
  But we’ll stop here…
void vTaskPrioritySet( xTaskHandle pxTask,
unsigned uxNewPriority );
Set the priority of any task.
pxTask: Handle to the task for which the priority is being set. Passing a NULL handle results in the priority of the calling task being set.
uxNewPriority: The priority to which the task will be set.

## Slide 23: Outline
Quick review of real-time systems
Overview of RTOSes
  Goals of an RTOS
  Features you might want in an RTOS
Learning by example: FreeRTOS
  Introduction
  Tasks
  Interrupts
  Internals (briefly)
  What’s missing?

## Slide 24: Interrupts in FreeRTOS
There is both a lot and a little going on here.
  The interface mainly uses whatever the native environment uses to handle interrupts
    This can be very port dependent. In Code Composer Studio you’d set it up as follows:
      #pragma vector=PORT2_VECTOR
      interrupt void prvSelectButtonInterrupt( void )
  That would cause the code to run on the PORT2 interrupt.
    Need to set that up etc. Very device specific (of course).

## Slide 25: More: Deferred Interrupt Processing
The best way to handle complex events triggered by interrupts is to not do the code in the ISR.
  Rather create a task that is blocking on a semaphore.
    When the interrupt happens, the ISR just sets the semaphore and exits.
      Task can now be scheduled like any other. No need to worry about nesting interrupts (and thus interrupt priority).
      FreeRTOS does support nested interrupts on some platforms though.
  Semaphores implemented as one/zero-entry queue.

## Slide 26: Outline
Quick review of real-time systems
Overview of RTOSes
  Goals of an RTOS
  Features you might want in an RTOS
Learning by example: FreeRTOS
  Introduction
  Tasks
  Interrupts
  Internals (briefly)
  What’s missing?

## Slide 27: Common data structures
This figure and the next are from http://www.aosabook.org/en/freertos.html