## Slide 1
ECEN 361
Real-Time and Embedded Systems
Lecture 3 – Interfaces

## Slide 2
Accessing the Processor
We need to get information in/out of our system
Some of that information is Digital – On/off
Some of that information is Analog – A continuous signal
Both of these might come synchronously or asynchronously
Some of that information comes in the form of Standard Communications Busses
  UART
  I2C/SPI
  USB
  Bluetooth/WIFI

## Slide 3
Notes: Look up analog ref

## Slide 4
Digital I/O
These signals are either On or Off – Or are they?
What does On mean?
Voltage – 5 Volts? 3.3 Volts? 1.8 Volts?
Current – How much current?

## Slide 5
Digital I/O Output
These signals are either On or Off – Or are they?
Voltage – 3.3 Volts
Current limit – 6/20 mAmps – Is this enough?
Damage on a short circuit?

## Slide 6
Digital I/O Output

## Slide 7
Digital I/O Output
What if this is not enough?

## Slide 8
Digital I/O Output

## Slide 9
Digital I/O Output

## Slide 10
Digital I/O Output
What if we need 3.3 Volts and are given 5?
What if we need 5 Volts and are give 3.3?

## Slide 11
Digital I/O Input
What is the input voltage?
  What if we need 3.3 Volts and are given 5?
  What if we need 5 Volts and are give 3.3?
  On the MSP432 – 5 Volts input will damage the part!

## Slide 12
Digital I/O Output
What if we need 3.3 Volts and are given 5?
What if we need 5 Volts and are give 3.3?

## Slide 13
Digital I/O Output
From the Software perspective we can either use a low level or a high level driver to configure and access the hardware.

## Slide 14
Digital I/O Output

## Slide 15
Digital I/O Output

## Slide 16
Digital I/O Output

## Slide 17
Digital I/O Output

## Slide 18
Digital I/O Input
Is the input synchronous or asynchronous?
  Synchronous – We will read a value at a specific time in the program.
  Asynchronous – We can either poll or use an interrupt.

## Slide 19
Digital I/O Input - Synchronous

## Slide 20
Digital I/O Input - Synchronous

## Slide 21
Digital I/O Input - Synchronous
GPIOPinTypeGPIOInput(GPIO_PORTA_BASE, GPIO_PIN_2); GPIOPinTypeGPIOInput(GPIO_PORTA_BASE, GPIO_PIN_3);

## Slide 22
Digital I/O Input – Asynchronous using Polling
  Asynchronous – Using a Polling loop
#include <msp430.h>
int main(void)
{
WDTCTL = WDTPW + WDTHOLD;
// Stop watchdog timer
P1DIR |= 0x01;
// Set P1.0 to output direction
while (1)
// Test P1.3
{
if ((BIT3 & P1IN))
P1OUT |= 0x01;
// if P1.3 set, set P1.0
else
P1OUT &= ~0x01;
// else reset
}
}

## Slide 23
Digital I/O Input – Asynchronous using Interrupts
int main(void)
{
Board_initGeneral();
Board_initGPIO();
Board_initUART();
GPIO_write(Board_LED0, Board_LED_ON);
System_printf("Starting the GPIO Interrupt example\nSystem provider is set"
" to SysMin. Halt the target to view any SysMin contents in"
" ROV.\n");
System_flush();
/* install Button callback */
GPIO_setCallback(Board_BUTTON0, gpioButtonFxn0);
/* Enable interrupts */
GPIO_enableInt(Board_BUTTON0);
if (Board_BUTTON0 != Board_BUTTON1) {
/* install Button callback */
GPIO_setCallback(Board_BUTTON1, gpioButtonFxn1);
GPIO_enableInt(Board_BUTTON1);
}
/* Start BIOS */
BIOS_start();
return (0);
}

## Slide 24: Digital I/O - Standard Communications Busses
Some information comes in the form of Standard Communications Busses
  UART
  I2C
  USB
  Wifi/Bluetooth

## Slide 25: Digital I/O - Data Transmission Tree
Data Transmission
Parallel
Serial
Synchronous
Asynchronous

## Slide 26: Digital I/O - Parallel
Data is sent and received more than one bit at a time
Transmission on multiple wires

## Slide 27: Digital I/O - Parallel
Many lines of communication, synchronized bursts of data
Time
Transmitter
Receiver

## Slide 28: Endianness, how it relates to communication
Big Endian- MSB first, less significant bytes in descending order
Little Endian- MSB last, data in ascending order
Endian type determines how the data is interpreted, and how it should be sent in both serial and parallel communication.

## Slide 29: Digital I/O - Serial
Data is sent and received one bit at a time
Transmission on single wire*

## Slide 30: Digital I/O - Serial Communication
One line of communication, long string of data
Time
Signal

## Slide 31: Digital I/O - Why Serial?
Fewer wires translates to
  Lower cost
  Simpler set-up

## Slide 32: Digital I/O – Synchronous Serial
Sender and receiver have their clocks synchronized
Transmissions occur at specified intervals
Advantage – Faster

## Slide 33: Digital I/O – Serial Asynchronous
Devices are not synchronized
Transmissions happen at unpredicted intervals
Advantages
  Simpler
  More robust

## Slide 34: Digital I/O
Both synchronous and asynchronous must have agreed upon bit transfer rate

## Slide 35: Digital I/O - Why Asynchronous?
Disadvantage:
  - Slower due to overhead
Advantages:
  - Simpler
  - Cheaper
  - Information can be sent when ready

## Slide 36: FYI Term: “UART”
Universal
Asynchronous
Receiver-
Transmitter
“…a computer component that handles asynchronous serial communication.”
www.webopedia.com

## Slide 37
UART

## Slide 38
UART

## Slide 39: Definitions
Start Bit
  Signals the beginning of the data word
  A low bit after a series of high bits
Data Bits
  The meat of the transmission
  Usually 7 or 8 bits

## Slide 40: Definitions Continued
Parity Bit
  An error check bit placed after the data bits
  Can be high or low depending on whether odd parity or even parity is specified
Stop Bit/s
  One or two high bits that signal the end or the data word
Data Word
  Start Bit, Data Bits, Parity Bit, & Stop Bit/s

## Slide 41
BAUD RATE
BIT RATE
UART

## Slide 42: Baud Rate
Baud Rate = bits transferred/second
baud rate INCLUDES start, stop, and parity
“bit rate” refers to JUST data bits transferred per second (may include parity)
baud rate > bit rate

## Slide 43: Baud Rate Example
Calculate baud rate
  1/bit time = 1/9.09ms = 110 baud
Time to transmit word:
  (11 bits) x (9.09ms) = 0.1 s
Word rate
  1/0.1s = 10 char/s
Bit rate
  (10 char/s) x (8 bits/char) = 80 bits/s