## Slide 1
ECEN 361
Real-Time and Embedded Systems
Lecture 3 – Interfaces

## Slide 2
Accessing the Processor
We need to get information in/out of our system
Some of that information is Digital – On/off
Some of that information is Analog – A continuous signal
Both of these might come synchronously or asynchronously
Some of that information comes in the form of Standard Communications Busses
  UART
  I2C/SPI
  USB
  Bluetooth/WIFI

## Slide 3: Inter-Integrated Circuit (I2C)
2-Wire Serial Communication Bus
Introduced By Philips In 1992
Communication Protocol Between Microcontroller And Peripherals
  Real Time Clocks (RTCs)
  Analog to Digital Converters (ADCs)
  Various Sensors
  Many, many, more

## Slide 4: I2C Characteristics
Only 2 Wires Needed On Bus
  Serial Data (SDA)
  Serial Clock (SCL)
Multiple Devices Connected On Bus
  Typically Limited (i.e. 8, 20, 27, 210,...?)
Similar Code For All I2C Peripherals
Supports Various Data Transfer Rates

## Slide 5: How Does It Work?

## Slide 6: Serial Peripheral Interface (SPI)
Synchronous Communication Protocol
  3-Wire (Plus 1 Chip-Select Pin/Device)
  Hardware On Microcontroller
Developed By Motorola
  “Loose” Standard
Broad Range of Devices Supported
  Memory (i.e. EEPROM, RAM, Etc.)
  Sensors

## Slide 7: SPI Characteristics
3 Wires (Plus Chip Select Pin/Device)
  Master Out Slave In (MOSI)
  Master In Slave Out (MISO)
  Master/Slave Clock Output/Input (SCK)
  Chip/Slave Select (SS)
Multiple Devices Connected On Bus
  Limited Only By Number Of uC Pins
Supports Various Data Transfer Rates

## Slide 8: How Does It Work?

## Slide 9: SPI Summary
3-Wire (+ SS/Device)
1.5 MHz Bit Frequency (AT89S53)
Microcontroller Hardware
Supports Many Devices

## Slide 10: Wireless Communications
Simple Point-to-Point communications
Bluetooth
WIFI
Xbee – Other mesh networks

## Slide 11: Simple RF
A Point-to-Point communication Technology
Normally works in an unlicensed band
Connects to the UART – The device sees a UART terminal
Requires some sort of configuration

## Slide 12: Simple RF

## Slide 13: Simple RF

## Slide 14: Simple RF

## Slide 15: Bluetooth
Short range communication in the 2.4 GHz band
Initially designed as a cable replacement technology – Connecting keyboards, mice, speakers.
Set up mostly in a single master, many slave configuration.

## Slide 16: Bluetooth

## Slide 17: WIFI - What is IEEE 802.11?
Standard for wireless local area networks (wireless LANs) developed in 1990 by IEEE
Intended for home or office use (primarily indoor)
802.11 standard describes the MAC layer, while other substandards (802.11a, 802.11b) describe the physical layer
Wireless version of the Ethernet (802.3) standard

## Slide 18: Wifi
Short range communication in the 2.4/5.8 GHz band
Designed to replace LAN cables
Set up in mostly a peer network – however one of the devices has to provide the IP addresses (DHCP). This is the access point.

## Slide 19: Wifi

## Slide 20: Wifi

## Slide 21: Wifi
Range of Wifi
Standard Range – 30 meters
Range with Antenna
  Several hundreds of meters

## Slide 22: What is Zigbee?
Based on IEEE 802.15.4 Standard
Designed for sensor and control networks
Used for applications that require:
  Low Power Consumption
  Low Data Rate
  Network Security

## Slide 23: Zigbee Layers

## Slide 24: A Zigbee Network

## Slide 25: Xbee Wireless Modules
Features/Benefits
www.digi.com
802.15.4/Multipoint network topologies
2.4 GHz for worldwide deployment
900 MHz for long-range deployment
Low-power sleep modes
Multiple antenna options
Low power and long range variants available

## Slide 26: Xbee Wireless Modules

## Slide 27: Cellular Connection

## Slide 28
The Arduino GSM Shield connects our Arduino to the network. Plug in a SIM card from an operator offering GPRS coverage and also you can also make/receive voice calls and send/receive SMS messages.
Quad-band GSM/GPRS modem that works at frequencies GSM850MHz, GSM900MHz, DCS1800MHz andPCS1900MHz
Cellular Connection

## Slide 29: The Various Protocols