## Slide 1
ECEN 361
Real-Time and Embedded Systems
SW Architectures and Lab Tools

## Slide 2: Embedded Software Architectures
All embedded systems are designed to handle different kinds of events
  button press
  sensor reading
  network data traffic
  timer expires
  etc

## Slide 3: Defn - Event Handlers
Event handlers are procedures or functions (typically written in C) that do the “work” to respond to these events
The Embedded Software Architecture determines how
  the event is detected
  the event handler is called
Handlers
Events
Architecture

## Slide 4: Embedded Software Architectures
There are 4 main SW architectures used in embedded systems
  Round Robin
  Round Robin with Interrupts
  Function Queue Scheduling
  Real Time Operating System
Each of these architectures handle the events differently

## Slide 5: Architecture 1: Round-Robin No interrupts required
One Event
while(1)
{
if (event)
handle_event();
}
Multiple Events
while(1)
{
if (event_1)
handle_event1();
if (event_2)
handle_event2();
...
if (event_n)
handle_eventn();
}
This is also called polling
What are the advantages/disadvantages of Round Robin?

## Slide 6: Characteristics of Round-Robin
Advantage:
  Simplicity: really just a single task, no shared data, no ISRs, no OS’s
Disadvantages:
  Worst-case response time - one full iteration of loop (possibly handling all other events first)
  Response time for every event is terrible if any single event requires lengthy processing
  System is fragile: adding a single new event handler may cause deadlines to be missed for other events
Priorities available
  None: actions are all equal; each handler must wait its turn

## Slide 7: How to decrease response time?
while(1)
{
if (event1)
handle_event1();
if (event2)
handle_event2();
if (event3)
handle_event3();
if (event4)
handle_event4();
}
while(1)
{
if (event1)
handle_event1();
if (event2)
handle_event2();
if (event1)
handle_event1();
if (event3)
handle_event3();
if (event1)
handle_event1();
if (event4)
handle_event4();
}
How can I reduce the response time for event 1?

## Slide 8: Application of Round-Robin
Digital Multimeter
Hand-Held Spectrum Analyzer
Round Robin good for
  Few input devices/events to respond to
  Response time constraints not demanding
  No lengthy processing required

## Slide 9: Architecture 2: Round-Robin with Interrupts
Add interrupts to single polling loop
  Have ISRs do some work
  Remainder done by functions called in loop
  ISR sets flag to indicate that processing is required
Offers greater flexibility
  Time critical response can be done in ISR
  Longer-running code can be done in handlers

## Slide 10: Round Robin with Interrupts
while(1)
{
if (flagA) {
flagA = 0;
handle_eventA();
}
if (flagB){
flagB = 0;
handle_eventB();
}
if (flagC){
flagC = 0;
handle_eventC();
}
}
ISR_A
{
// do some A stuff
flagA = 1;
}
ISR_B
{
// do some B stuff
flagB = 1;
}
ISR_C
{
// do some C stuff
flagC = 1;
}
Work split between ISR
and task code.
What is flagA?
What are the advantages/disadvantages of Round Robin w/ Interrupts?

## Slide 11: Characteristics of Round-Robin with Interrupts
Advantages
  Work performed in ISRs has higher priority
  ISR response time stable through most code changes
Disadvantages
  ISRs and handlers will share data, shared data problems will appear (will discuss next week)
  Handler response time not stable when code changes
Priorities available:
  interrupts are serviced in priority order
  all other actions have equal priority (none more important than rest)
Worst-case response time
  For ISR - execution time for higher priority ISRs
  For handler - sum of all other handlers + execution time for interrupts

## Slide 12: Application of RR w/ Interrupts
Hand-Held Spectrum Analyzer – Gen 2
RR w/ Interrupts good for
  Med # input devices/events to respond to
  Response time constraints not too demanding
  No lengthy processing required

## Slide 13: Architecture 3: Function-queue scheduling
What is a function pointer?
Work split
between ISR
and task code
Order of tasks
is dynamic
Queue can be
FIFO or sorted
by priority
ISR_A
{
// do some work relating to A
queue_put(handle_eventA);
}
ISR_B
{
// do some work relating to B
queue_put(handle_eventB);
}
while(1)
{
while(queue_empty()) // wait
task = get_queue();
task();
}

## Slide 14: Characteristics of Function-queue scheduling
Advantages
  improved response-time stability when code changes
Disadvantages
  increased complexity: must implement a function queue
Priorities available
  interrupts are serviced in priority order
  tasks can be run in priority order
Worst-case response time for task
  just started executing another task, have to wait
  longest task time + execution time for ISRs
Just FYI - I have never seen this architecture used in industry

## Slide 15: Architecture 4: Real-time operating system (RTOS)
What is an OS? What does it really do?
RTOS
  Work is split between ISRs and tasks
  Tasks are prioritized and run by a scheduler
    Highest priority task is always the “running” task
    If higher priority task becomes ready to run, other tasks are preempted
      ISRs can cause tasks to become unblocked
    Tasks can block when they are waiting for events
      Tasks can delay themselves for fixed time intervals
RTOS contains code to
  Create tasks, block and unblock tasks, schedule tasks, allow tasks and ISRs to communicate, etc

## Slide 16: RTOS Architecture
RTOS
Task A
Task B
Task C
:
:
ISR for
Event 1
:
:
ISR for
Event 2
ISR for
Event 3

## Slide 17: RTOS Characteristics
Advantages:
  Stability when code changes: adding a lower-priority task will not affect response time of tasks with higher priorities
  Many commercial RTOSs available
Disadvantages:
  Software complexity (but much of complexity in RTOS)
  Runtime overhead of RTOS
Priorities available
  interrupts are serviced in priority order
  tasks are serviced in priority order - lower priority tasks are preempted
Worst-case response time for highest-priority task
  sum of interrupt execution times (other tasks preempted)

## Slide 18: Priority Levels of Different Architectures
High Priority Processing
Low Priority Processing
Everything
Device A ISR
Device B ISR
Device ... ISR
Device x ISR
All Task Code
Device A ISR
Device B ISR
Device ... ISR
Device x ISR
Task Code 1
Task Code 2
Task Code ...
Task Code x
Round-Robin
Round-Robin w/ Interrupts
Real Time Operating System

## Slide 19: Factors in choosing a SW Architecture
How much control do you need over system response time?
  absolute response time requirements
  other processing requirements (speed of uproc)
How many different events do you have to respond to?
  different deadlines
  different priorities

## Slide 20: Selecting an Architecture
Select the simplest architecture that will meet your current and future response time requirements
If you have difficult response-time requirements, you should lean toward using an RTOS
  Many to choose from, debugging support, etc.
You can also construct architectural hybrids
  An RTOS where one task does polling
  RR w/ interrupts: main loop polls slower HW directly

## Slide 21: Pointers
In ECEN 260, how did we send data to a particular memory/IO location?
How can you do this in C?
  More specific, how can you get a pointer to point to a particular memory location?
uint32 *p = (uint32 *)0x400000;

## Slide 22: Function Pointers
While many programming languages support the concept of pointers to data, only a few enable you to define pointers to code -- that is, pointers that point to functions.
Originally introduced in C, pointers to functions are widely used in C++
Unfortunately, their cumbersome syntax baffles both novices and experienced programmers.

## Slide 23: What are function Pointers?
C does not require that pointers only point to data, it is possible to have pointers to functions
Functions occupy memory locations therefore every function has an address just like each variable

## Slide 24: Define a Function Pointer
A function pointer is nothing else than a variable, it must be defined as usual.
Eg,
int (*funcPointer) (int, char, int);
funcPointer is a pointer to a function.
The extra parentheses around (*funcPointer) is needed because there are precedence relationships in declaration just as there are in expressions

## Slide 25: Assign an address to a Function Pointer
//assign an address to the function pointer
int (*funcPointer) (int, char, int);
int firstExample ( int a, char b, int c){
printf(“ Welcome to the first example”);
return a+b+c;
}
funcPointer= firstExample; //assignment
funcPointer=&firstExample; //alternative using address operator

## Slide 26: Calling a function using a Function Pointer
There are two alternatives
Use the name of the function pointer
Can explicitly dereference it
int (*funcPointer) (int, char, int);
// calling a function using function pointer
int answer= funcPointer (7, ’A’ , 2 );
int answer=(* funcPointer) (7, ’A’ , 2 );

## Slide 27: Arrays of Function Pointers
C treats pointers to functions just like pointers to data therefore we can have arrays of pointers to functions
This offers the possibility to select a function using an index
Eg.
suppose that we’re writing a program that displays a menu of commands for the user to choose from. We can write functions that implement these commands, then store pointers to the functions in an array:

## Slide 28
void (*file_cmd[]) (void) =
{ new_cmd,
open_cmd,
close_cmd,
save_cmd ,
save_as_cmd,
print_cmd,
exit_cmd
};
If the user selects a command between 0 and 6, then we can subscript the file_cmd array to find out which function to call
file_cmd[n]();
Arrays of Function Pointers

## Slide 29: Testing and Debugging
Oscilloscope
  Shows electrical details
    Benefits: Wideband, accurate
    Disadvantages: < 4 inputs; triggering
Logic analyzer
  Shows 0/1 - according to some threshold
    Benefits: Many channels, trigger on patterns
    Disadvantages: Idealized waveforms, insufficient access
3. Embedded test
  You design in built-in test features
    Benefits: Only way to test large chips
    Disadvantages: Uses chip area, incomplete scan, difficult design

## Slide 30: Oscilloscope
Samples signal voltage over time
  Displays signal as a waveform, one voltage value per time step\
Triggering
  Choose when to start sampling the signals
  Slope: rising voltage/falling voltage
  Threshold: trigger when signal reaches this value
Repeat mode
  Assume that signal is periodic
  Repeated triggering captures the same signal
  You’ll never see a glitch
Capture mode
  Triggers only once, stores waveform in memory
  You’ll be very lucky to catch a glitch

## Slide 31: Logic analyzers
Instruments for acquiring digital data
  Wide data “bus” - capture many signals
  Memory stores bus data
  Smart triggering decides what data to store
  Embedded computer processes the data
We use the Logitech
  128 channels
  32k memory per channel
  100MHz state
  2GSPS sampling

## Slide 32: Clocking a logic analyzer
Samples data every clock cycle
External/synchronous clocking
  You supply the clock
  Use when you need to see long data records
    Analyzer stores one sample per clock period
Internal/asynchronous clocking
  Analyzer supplies the clock
    4ns to 50ms
  Use when you need to see precise timing
    Find glitches

## Slide 33: Triggering and acquisition
Derive trigger from sampled data
  Data values
  Data ranges
  Signals from another module
  Internal counters
Data acquisition is continuous
  Memory is a circular buffer
  New samples continually overwrite oldest samples
  Trigger tells the acquisition to stop
Triggers can qualify acquisition
  Store only selected data

## Slide 34: Data windows
Many types
  Listing window
  Waveform window
  Histogram window
  Source-data window
Features common to all
  Cursors
  Flags
  Scroll
  Search

## Slide 35: Capturing glitches
Trigger on the glitch
  Triggering looks for multiple transitions in a clock cycle
  Captures dynamic hazards
Can also trigger on setup and hold violations