## Slide 1
ECEN 361
Real-Time and Embedded Systems
Interrupts

## Slide 2: Embedded systems software
How is embedded SW different than desktop SW?
Embedded SW has a different set of issues than desktop
  work directly with the hardware
  Multitask - do several functions simultaneously
  respond to external events (button presses, sensor readings, etc)
  cope with all unusual conditions without human intervention
  meet strict processing deadlines – can’t just hang for a little while
  never fail

## Slide 3: Definition
What do you think the term real time embedded system means?
An embedded real-time system is a system that must satisfy explicit response-time characteristics or risk severe consequences, including failure
If a deadline is not met, system failure may result (plane crashes, nuclear plant goes critical, ... )
Many embedded systems can be classified as real-time based on this definition
  Depends on criticality of deadlines

## Slide 4: Classification of RT systems
Key question: how critical are the deadlines?
  Soft RT
    missing deadline causes performance degradation, but system is still functional
  Firm RT
    occasional deadline can be missed for a functional system
  Hard RT
    missing deadline causes system failure
What would be some examples of these?

## Slide 5: Embedded Software Architectures
What are the 4 different embedded software architectures?
  Round-Robin
  Round-Robin with Interrupts
  Functions Queue Scheduling
  Real Time OS
Which of these could be considered real-time?

## Slide 6: Interrupts
Essential in meeting hard deadlines with multiple tasks that need to run
What is an interrupt?
  Interrupt’s are a nifty collaboration between hardware and software
    Both are essential
  Understanding details is an essential part of computer system literacy

## Slide 7: Computer Interrupts
What can cause an interrupt in a computer?
  Arrival of data from an I/O device
  Completion of a previous request to an I/O device
  Change in sensor data
  Action by a human – mouse, keyboard, etc
  Detection of an error condition
    external (hardware configuration specific)
    internal to processor, known as exceptions
      Examples: divide by zero, overflow, segmentation fault
  Timer expires
  Power failure
Let’s start here: What does a processor do when an interrupt is asserted?

## Slide 8: Interrupts: Hardware Side
Simple model:
• Interrupt pin is asserted
• HW saves information
about current task
• HW sets PC to start of
corresponding interrupt
service routine
Questions:
• Is delay possible after interrupt assertion?
• Finish current instruction - how long can this take?
• Interrupts may be masked - re-enabled under software control; max wait is up to software
• What information? Where saved?
• At least return address
• On stack, in register, in fixed
memory location, etc.
• Which is correct ISR, and where
is it in memory?
• SW must give this info to HW - usually a table of ISR starting addresses, indexed by interrupt number or level
ISRs are basically hardware induced function calls

## Slide 9
Interrupt Service Routine
Interrupt Service Routine
Saving the Context
Program Counter – so we can get back
Stack Pointer – So we know how we got there
Internal Register States

## Slide 10
Interrupt Vector Table
Interrupt Vector Table
What function runs when which interrup occurs?

## Slide 11
Interrupt Service Routine
Stack Pointer – So we know how we got there
Call Stack
main()
int value1
int value2
foo()
foo1

## Slide 12
Interrupt Service Routine
int foo()
{
int foo1;
<- Interrupt Occurs here.
int main()
int value1;
int value2;
foo();
.

## Slide 13: 2 scenarios for interrupts
CPU
INTR
Device 1
Device 2
Device 3
CPU
INTR1
Device 1
Device 2
Device 3
INTR2
INTR3
These need to be open-collector outputs – with pull-up resistor
Is there anything special about these output pins

## Slide 14: Identifying source of interrupt
Simplest hardware model: single interrupt line
How does the CPU know who interrupted it?
  Single ISR for all interrupts
    ISR Address is located in a register
  Single location required to hold return address
    Typically also in a register
  Software must run down checklist: who interrupted me?
    Poles hardware to see who asserted interrupt
  What is good and bad of this?
    Other interrupts disabled as ISR runs
CPU
Device 1
Device 2
Device 3

## Slide 15: Multiple interrupt lines
More complex hardware: multiple interrupt lines
How does the CPU know who interrupted it?
  For interrupt i, hardware gets entry i from table of n ISR addresses
    software responsible for initializing the table
    table is called interrupt vector table (IVT)
    appropriate ISR can begin to run directly
    Return addresses stored on stack
  What is good and bad of this?
    Software complexity – needs complicated boot code to init IVT
CPU
INTR1
Device 1
Device 2
Device 3
INTR2
INTR3

## Slide 16: Multi-Interrupt Challenges
What if two lines are asserted at same time?
  Need a priority scheme to determine which interrupt is more important
What if higher priority interrupt comes while lower-priority handler is running?
  Nested interrupts
How does the processor handle nested interrupts?
CPU
INTR1
Device 1
Device 2
Device 3
INTR2
INTR3

## Slide 17: Interrupt Nesting
Task
ISR1
ISR2
ISR1
Task
Code Running on Processor
Priority
Time

## Slide 18: Round Robin with Interrupts
while(1)
{
if (flagA) {
flagA = 0;
handle_eventA();
}
if (flagB){
flagB = 0;
handle_eventB();
}
if (flagC){
flagC = 0;
handle_eventC();
}
}
ISR_A
{
!! do some A stuff
flagA = 1;
}
ISR_B
{
!! do some B stuff
flagB = 1;
}
ISR_C
{
!! do some C stuff
flagC = 1;
}
Work split between ISR
and task code.
In general, how long should ISR’s be? Why?

## Slide 19: RR with Interrupt - Code Example
static int iTemperatures[2];
void interrupt ReadTemperatures (void)
{
iTemperatures[0] = // read in value from HW
iTemperatures[1] = // read in value from HW
}
void main (void)
{
int iTemp0, iTemp1;
while (TRUE)
{
iTemp0 = iTemperatures[0];
iTemp1 = iTemperatures[1];
if (iTemp0 != iTemp1)
// Set off howling alarm;
// Do other processing
}
}
Assume interrupt asserted at regular intervals, based on a timer, or when either temperature changes.
What does this code do?

## Slide 20: Code Example
static int iTemperatures[2];
void interrupt ReadTemperatures (void)
{
iTemperatures[0] = !! read in value from HW
iTemperatures[1] = !! read in value from HW
}
void main (void)
{
int iTemp0, iTemp1;
while (TRUE)
{
iTemp0 = iTemperatures[0];
iTemp1 = iTemperatures[1];
if (iTemp0 != iTemp1)
!! Set off howling alarm;
!! Do other processing
}
}
What can go wrong?
Suppose the interrupt occurs here

## Slide 21: Problem
Possible scenario in example code:
  Temperature rising: one reading 80, the next is 81.
  Interrupt occurs between reading temps separately.
  Values are different in test in main(), although in ISR they were identical at every reading.
  Howling alarm set off, needlessly
How can you fix this?

## Slide 22: Is the problem fixed?
static int iTemperatures[2];
void interrupt vReadTemperatures (void)
{
iTemperatures[0] = !! read in value from HW
iTemperatures[1] = !! read in value from HW
}
void main (void)
{
while (TRUE)
{
if (iTemperatures[0] != iTemperatures[1])
!! Set off howling alarm;
}
}

## Slide 23: Consider the Assembly Language Sequence
static int iTemperatures[2];
void interrupt vReadTemperatures (void)
{
iTemperatures[0] = !! read in value from HW
iTemperatures[1] = !! read in value from HW
}
void main (void)
{
while (TRUE)
{
if (iTemperatures[0] != iTemperatures[1])
!! Set off howling alarm;
}
}
….
mov r1, (itemperatures[0])
mov r2, (itemperatures[1])
cmp r1, r2
je okay
; set off alarm
okay: ….

## Slide 24: Ensuring Correctness
Assembly code for other platforms will be similar
Key point: will the two values be accessed by a single machine instruction?
If not,
  There is nothing to prevent an interrupt from coming between the two memory reads
  The howling alarm may be set off incorrectly

## Slide 25: Shared Data Problem
When does this type of problem arise?
  When data is shared between the ISR and the task code that it interrupts, and when the data can appear to be in an inconsistent state when ISR runs at the wrong time
Does the bug manifest itself consistently?
  No, appears randomly, with low probability
Would you catch it with thorough testing?
  Not necessarily; exhaustive testing generally impossible
  Testing shows the presence of bugs, but cannot prove absence
Only real solution: write bug-free code
  Think long and hard about correctness of code at all levels
  Stick with basic principles that work
So, one more time, how could we solve this?

## Slide 26: Better Solution – Disable Interrupts
static int iTemperatures[2];
void interrupt vReadTemperatures (void)
{
iTemperatures[0] = !! read in value from HW
iTemperatures[1] = !! read in value from HW
}
void main (void)
{
while (TRUE)
{
if (iTemperatures[0] != iTemperatures[1])
!! Set off howling alarm;
}
}
….
cli
mov r1, (itemperatures[0])
mov r2, (itemperatures[1])
sti
cmp r1, r2
je okay
; set off alarm
okay: ….

## Slide 27: A “C” Solution
static int iTemperatures[2];
void interrupt vReadTemperatures (void)
{
iTemperatures[0] = !! read in value from HW
iTemperatures[1] = !! read in value from HW
}
void main (void)
{
int iTemp0, iTemp1;
while (TRUE)
{
disableInterrupt();
iTemp0 = iTemperatures[0];
iTemp1 = iTemperatures[1];
enableInterrupt ();
if (iTemp0 != iTemp1)
!! Set off howling alarm;
}
}
A Blackfin solution:

## Slide 28
Backup

## Slide 29: Shared Data
Defn - Critical Section: a section of code that cannot be interrupted for correct operation
Need to remember the shared data problem can arise when task code shares data with ISR’s,
  Lines of C-code rarely map to single instructions
  Disabling and then re-enabling interrupts is really the only way around this

## Slide 30: What can go wrong here? How to fix?
static int iSeconds, iMinutes, iHours;
void interrupt vUpdateTime (void)
{
++iSeconds;
if (iSeconds >= 60)
{
iSeconds = 0;
++iMinutes;
if (iMinutes >= 60)
{
iMinutes = 0;
++iHours;
if (iHours >= 24)
iHours = 0;
}
}
!! Do whatever needs to be done to the HW
}
long lSecondsSinceMidnight(void)
{
return (((iHours * 60) + iMinutes) * 60) + iSeconds;
}

## Slide 31: One Solution
static int iSeconds, iMinutes, iHours;
void interrupt vUpdateTime (void)
{
++iSeconds;
if (iSeconds >= 60)
{
iSeconds = 0;
++iMinutes;
if (iMinutes >= 60)
{
iMinutes = 0;
++iHours;
if (iHours >= 24)
iHours = 0;
}
}
!! Do whatever needs to be done to the HW
}
long lSecondsSinceMidnight(void)
{
return (((iHours * 60) + iMinutes) * 60) + iSeconds;
}
long lSecondsSinceMidnight(void)
{
long lRetVal;
disableInterrupts ();
lRetVal = (((iHours * 60) + iMinutes) * 60) + iSeconds;
enableInterrupts ();
Return lRetVal;
}
What can go wrong with this solution?

## Slide 32: One Solution
static int iSeconds, iMinutes, iHours;
void interrupt vUpdateTime (void)
{
++iSeconds;
if (iSeconds >= 60)
{
iSeconds = 0;
++iMinutes;
if (iMinutes >= 60)
{
iMinutes = 0;
++iHours;
if (iHours >= 24)
iHours = 0;
}
}
!! Do whatever needs to be done to the HW
}
long lSecondsSinceMidnight(void)
{
long lRetVal;
disableInterrupts ();
lRetVal = (((iHours*60)+iMinutes)*60)+iSeconds;
enableInterrupts ();
Return lRetVal;
}
void main (void) {
while (TRUE){
:
:
disableInterrupts ();
:
time = lSecondsSinceMidnight();
:
enableInterrupts ();
:
}
}
What is wrong here?

## Slide 33: Subtle Point
What if the subroutine is called from inside a critical region of another part of the program?
  interrupts will be re-enabled
  not what you want at that point
How could you fix this?

## Slide 34: Another Approach
static long int secondsToday;
void interrupt updateTime (void)
{
...
++secondsToday;
if (secondsToday == 60 * 60 * 24)
secondsToday = 0L;
...
}
int main (void)
{
long value;
value = secondsToday;
:
:
display (secondsToday);
:
:
}
Is there any problem with this main loop?
For efficiency, the variable secondsToday will be saved in a register when it is assigned to value. It will not re-read the memory location in the call to display(). The register value will be passed to the display function.

## Slide 35: Another Approach Discussion
Problem: a good (optimizing) compiler is smart enough to only read memory once, and keep the value in a register
  Justification: no intervening write took place between the two reads, so value in register still okay.
What is the solution?
  Solution: use “volatile” keyword to inform the compiler that special handling is required.
  Forces compiler to read memory every time the variable is accessed and not to make “obvious” optimization.
  “Volatile” says variable is subject to change from something the compiler is not aware of.
  static volatile long int iSecondsToday;

## Slide 36: Blackfin Interrupt Model
16 Core Event Classes
  Emulation
  Reset
  NMI
  Exception
  Interrupts
    Hardware Error
    Core Timer
    IVG7 – IVG15
3 Registers are used to control and coordinate events
  ILAT, IMASK, IPEND
Description of Interrupt functionality is shown in chapter 4 of the HRM

## Slide 37: IMASK Register

## Slide 38: ILAT Register

## Slide 39: IPEND Register

## Slide 40: Blackfin 533 Interrupt Model
Default Peripheral Interrupt Mapping
  Multiple interrupt sources for each interrupt group
Can remap interrupts depending on application
3 Registers are used to control and coordinate events
  SIC_IMASK, SIC_ISR, SIC_IWR

## Slide 41: SIC_IWR register

## Slide 42: SAC_ISR Register

## Slide 43: SIC_IMASK Register

## Slide 44: Interrupt Vector Table

## Slide 45: Setting up Interrupts
The main steps for setting up interrupts are:
  Create the interrupt service routines.
  Initialize the vector table and set up the vectors in the memory map.
  Enable the interrupt
The HRM document describes the entire ISR process

## Slide 46: Interrupts - Key to Responsiveness
Essentially all processors respond to interrupts.
Part of our focus this semester:
  Systems with challenging response-time constraints
  Getting the right answer is important, but it must be delivered when it is required
  Are there systems in which timeliness is not important?
  Implication: sometimes timely response time is critical.
    consequences far worse than (just) an unhappy user

## Slide 47: Hard Real Time Systems
Assumed unless explicitly stated otherwise
  Deadlines must be met!
These are the most demanding real-time systems to design
We learn the most looking at the demands of meeting hard deadlines
  If you can meet hard RT constraints, others can certainly be met, since constraints can be relaxed

## Slide 48: Interrupt Basics
Interrupts: a mechanism used to transfer attention to something of potential importance
Interrupts for humans:
  Doorbell, phone, oven timer (pizza done!)
  Do you sometimes ignore these interrupts?
Fundamental scenario in real-time systems:
  processor is running job A
  something happens that must be dealt with
  processor must put A “on hold”, handle event