## Slide 1
ECEN 361
Real-Time and Embedded Systems
Real Time Operating Systems – Schedulers

## Slide 2: Real Time Operating Systems
What is an operating system? What is a kernel?
Defn.
  RTOS – Real Time Operating System
  Kernel – The core set of essential services
For some, RTOS = kernel = real-time kernel (RTK)
For others, RTOS > kernel
  RTOS includes network support, debugging tools, memory management
  Kernel includes only most basic services
In our class
  RTOS and kernel used synonymously

## Slide 3: Real Time Operating Systems
What is the key aspect of any Operating System?
What does a scheduler do?
  A set of code and data structures that decide which task/process/thread gets time on the processor.
What is a task/process/thread?
  A set of code and data structures that is designed to do “something”. Each task/process/thread has its own Program Counter/Stack Pointer/Register set – this is a execution context.
Scheduler

## Slide 4: Real-Time Operating System (RTOS) Features
What is the difference between a Scheduler and a Round-Robin with Interrupt architecture?
  RR w/Int
    Work is split between ISRs and main thread
    Two contexts – One for the main thread, the other for the ISR. ISRs are non-prememptive.
  RTOS
    Work is split between ISRs and tasks
    Tasks are run in an organized fashion (we can introduce the idea of priority)

## Slide 5: Real-Time Operating System (RTOS) Features
Tasks are run by a scheduler program
  Highest priority task is always the “running” task
    If higher priority task becomes ready to run, other tasks are preempted
  Tasks can block when they are waiting for events
    ISRs can cause tasks to become unblocked
    Tasks can delay themselves for fixed time intervals
RTOS contains code to
  Create tasks
  block and unblock tasks
  schedule tasks
  allow tasks and ISRs to communicate
  etc

## Slide 6: RTOS Architecture
RTOS
Task A
Task B
Task C
:
:
ISR for
Event 1
:
:
ISR for
Event 2
ISR for
Event 3

## Slide 7: RTOS Application Code: Example
void main(void)
{
// initialize (but don’t start) the RTOS
InitRTOS();
// Tell the RTOS about our tasks
StartTask(RespondToButton, HIGH_PRIORITY);
StartTask(CalculateTankLevels, LOW_PRIORITY);
// Start the RTOS (This function never returns)
StartRTOS();
}
void RespondToButton (void)
{
……
}
void CalculateTankLevels (void)
{
……
}
RTOS is essentially a set of functions that can be called from the application code
What do you think InitRTOS does?
INTERRUPT interrupt1 (void)
{
……
}
INTERRUPT interrupt2 (void)
{
……
}

## Slide 8: RTOS Application Code: Example
void main(void)
{
// initialize (but don’t start) the RTOS
InitRTOS();
// Tell the RTOS about our tasks
StartTask(RespondToButton, HIGH_PRIORITY);
StartTask(CalculateTankLevels, LOW_PRIORITY);
// Start the RTOS (This function never returns)
StartRTOS();
}
void RespondToButton (void)
{
……
}
void CalculateTankLevels (void)
{
……
}
INTERRUPT interrupt1 (void)
{
……
}
INTERRUPT interrupt2 (void)
{
……
}
InitRTOS
  Initializes OS timers
  Initializes PLL
  Initializes mode of operation
What do you think StartTask does?

## Slide 9: RTOS Application Code: Example
void main(void)
{
// initialize (but don’t start) the RTOS
InitRTOS();
// Tell the RTOS about our tasks
StartTask(RespondToButton, HIGH_PRIORITY);
StartTask(CalculateTankLevels, LOW_PRIORITY);
// Start the RTOS (This function never returns)
StartRTOS();
}
void RespondToButton (void)
{
……
}
void CalculateTankLevels (void)
{
……
}
INTERRUPT interrupt1 (void)
{
……
}
INTERRUPT interrupt2 (void)
{
……
}
StartTask ()
  Tasks are the main functions of the
  application software
  Tasks run independently from each other
  The RTOS determines which task will run
  next
  Each task has its own private context:
    register values
    program counter
    stack
  All other data is shared by all tasks
  Tasks are more like Windows/Unix threads
  than like processes

## Slide 10: Multitasking systems
What is a multitasking system?
  Systems with more than one task
    potentially many tasks
  Architectures that are not multitasking:
    Round-Robin
    Round-Robin with interrupts
  Architectures that are multitasking:
    Function-queue scheduling
    RTOS
  Multitasking systems need a scheduler

## Slide 11: RTOS Application Code: Example
void main(void)
{
// initialize (but don’t start) the RTOS
InitRTOS();
// Tell the RTOS about our tasks
StartTask(RespondToButton, HIGH_PRIORITY);
StartTask(CalculateTankLevels, LOW_PRIORITY);
// Start the RTOS (This function never returns)
StartRTOS();
}
void RespondToButton (void)
{
……
}
void CalculateTankLevels (void)
{
……
}
INTERRUPT interrupt1 (void)
{
……
}
INTERRUPT interrupt2 (void)
{
……
}
StartTask ()
  Tasks are the main functions of the
  application software
  Tasks run independently from each other
  The RTOS determines which task will run
  next
  Each task has its own private context:
    register values
    program counter
    stack
  All other data is shared by all tasks
  Tasks are more like Windows/Unix threads
  than like processes
What do you think StartRTOS does?

## Slide 12: Task management
The RTOS scheduler chooses which task to run based on task priority
  The highest priority ready task is always selected
If a task cannot run because it is waiting for something, the task is said to be blocked
Ready
Running
Blocked
Tasks are blocked when they request something that is not available
Only one task can be running at a time
Schedule Task
Preempt Task
Unblock Task
Block Task

## Slide 13: Preemption
A preemptive RTOS will stop the execution of a lower priority task as soon as a higher-priority task becomes ready to run
  Example: highest priority task unblocks when an ISR does a post (sending a message or freeing a semaphore)
A non-preemptive RTOS will stop a task only when that task blocks (e.g., after a pend or delay)

## Slide 14: Task States
Ready
Running
Blocked
Schedule Task
Preempt Task
Unblock Task
Block Task
Interrupted
Interrupt
Return
Preempt Task
(Preemptive RTOS)

## Slide 15: Internal Task Representation
Each task has an OS data structure called a Task Control Block (TCB)
  priority
  pointer to point of execution in task code
  pointer to top of task stack
  other context, status
Kernel code initializes, maintains, and uses TCB contents
Ready list: TCBs of all tasks in Ready state
Suspended list: TCBs of all tasks in Blocked state

## Slide 16: RTOS Essentials: Scheduler
The scheduler is the kernel routine that decides what to run next
Each task has:
  a unique priority
  a state (running, ready, blocked, interrupted, ...)
The scheduler finds and runs the task with the
  highest priority
  that is ready to run

## Slide 17: A Dumb Scheduler
Schedulers in an RTOS are simple-minded
  Can assume there is always one Ready task
  Not hard to find the one with highest priority
Unlike more complex OSes, the RTOS scheduler does not guarantee fairness
  Low priority tasks can be starved; CPU can be hogged
  Responsibility of application designer (not OS!) to make sure all tasks get what they need

## Slide 18: The Dispatcher
The scheduler’s work is easy; it calls the dispatcher to do the hard part:
  pass control to task selected by the scheduler, (perhaps) save context of previously running task
Tricky because it must handle all of the low-level details, such as
  saving and restoring context, including IP and SP, and stack frame, TCB manipulation
Must be written in assembly; can’t save context, manipulate stack frames in C

## Slide 19: Context
Each task has its own private context
  Register values
  Stack (including all stack-based variables)
  Program counter
Context must be stored whenever task stops running, be restored by dispatcher when it runs again
Tricky: context must be stored consistently regardless of what caused the task to be suspended
What event sequences can cause task to stop running?
  Something the task did
  Something done by something else in the system. Task? ISR?
How might you save context?
  Options: TCB, stack
  Must be done in assembly

## Slide 20: OS Services
What does the windows/linux OS give you as a user?
file system gui interface
framework to develop code device drivers
memory management etc
An RTOS might provide the following services:
OSInit() OSIntEnter() OSIntExit()
OSMboxCreate() OSMboxPend() OSMboxPost()
OSQCreate() OSQPend() OSQPost()
OSSchedLock() OSSchedUnlock() OSEnterCritical()
OSSemCreate() OSSemPend() OSSemPost()
OSStart() OSTaskChangePrio() OSTaskCreate()
OSTaskDel() OSTimeDly() OSTimeGet()
OSTimeSet() OSTimeTick() OSExitCritical()

## Slide 21: Comparison
RTOS
• Application code and RTOS are compiled and linked together
• The application runs first and calls the RTOS
• RTOS runs only when called by application
• Dedicated to a single embedded application
• Few if any extras
• Designed to run forever without crashing
Windows/Unix
• Application code and OS are separate
• The OS runs first and calls the application
• OS is a separate entity than the processes it runs
• Multi-process, general purpose
• File system, I/O systems, user interface
• Occasionally hangs

## Slide 22: Commercial RTOS’s
Comes with nice tools and are debugged
  AMX
  MultiTask!
  QNX
  LynxOS
  C Executive
  Nucleus
  pSOS
  VRTX
  VxWorks
  WinCE

## Slide 24: Mars rover bug
The code failed because of a priority inversion problem
The commercial RTOS (VxWorks) includes versions of take semaphore functions with and without priority inheritance
Programmer intended to use take with priority inheritance, but used other take by mistake
Lengthy, medium priority task to record weather caused a (blocked) high-priority task to miss a deadline
  Code detected missed deadline, assumed major malfunction, shut down the robot, waited for instructions from earth.
“Every use of semaphores is a bug waiting to happen.” (page 167)

## Slide 25
Backup

## Slide 26: RTOS Memory Organization
Registers & Stack
(Local Private Memory)
Task
Registers & Stack
(Local Private Memory)
Task
Registers & Stack
(Local Private Memory)
Task
Registers
&
Stack
(Local Private Memory)
Task
Registers
&
Stack
(Local Private Memory)
Task
Global Shared Memory (Shared Resource)
Note: Tasks share global memory space.

## Slide 27: Global data
Tasks share global data with all other tasks, ISRs and the kernel
Easy, convenient to send data from task to task; just use global variables
Problems arise in
  tasks that access global variables
  calls to kernel functions that access internal kernel variables

## Slide 28: Example: Figure 6.6 What can go wrong here?
struct {
long TankLevel;
long TimeUpdated;
} tankdata[MAX_TANKS];
void RespondToButton(void)
{ /* high priority task */
int i;
while (TRUE) {
!! Block until button pressed
i = !! ID of button pressed
tankdata[i].TimeUpdated = !! tankdata[i].TankLevel = !!
}
}
void CalculateTankLevels(void)
{ /* low priority task */
int i = 0;
while (TRUE) {
!! read float levels in task i
!! do bunches of calculations
/* store result */
tankdata[i].TimeUpdated =
!! current time
tankdata[i].TankLevel =
!! result of long calculation
!! pick next tank to handle, etc.
}
}
Where have we seen these types of problems before?

## Slide 29: Shared Resources
When two or more tasks use a shared resource at the same time, failures may occur.
  Just like with sharing global data between ISR’s
A shared resource is
  Global Variables
  Shared Functions
  Hardware
How did we stop these problems in ISR’s?
  We had to disable/enable interrupts around critical sections of code
In RTOS’s, we have to do the same thing. Each task must assure mutual exclusion. When one task is using the shared resource, other tasks are excluded by:
  Enable/Disable Interrupts
  Semaphores

## Slide 30: Priority Levels of Different Architectures
High Priority Processing
Low Priority Processing
Everything
Device A ISR
Device B ISR
Device ... ISR
Device x ISR
All Task Code
Device A ISR
Device B ISR
Device ... ISR
Device x ISR
Task Code 1
Task Code 2
Task Code ...
Task Code x
Round-Robin
Round-Robin w/ Interrupts
Real Time Operating System