## Slide 1: ECEN 150 Circuit Analysis I
Capacitors and Inductors

## Slide 2: Capacitors
A capacitor consists of two conducting plates separated
by an insulator (dielectric).
A capacitor holds separated electric charge, given as q = Cv.
Capacitance
A charged capacitor can provide electrical energy
to a load.
An ideal capacitor can hold a charge forever.
Practical capacitors can hold separated charge for
hours, days and perhaps weeks.

## Slide 3: Common Capacitor Types and Symbols
Don’t need to worry about voltage polarity across non-polarized capacitors such as film and ceramic capacitors, which simplifies their usage.
Electrolytic capacitors use either a liquid or solid electrolyte to achieve a large capacitance per area, which is good.
However, electrolytic capacitors are polarized, meaning that connecting to the proper voltage polarity is necessary.
Incorrect voltage polarity applied across an electrolytic capacitor can cause current flow resulting in heating that eventually can destroy the capacitor.
While the large capacitance per area of electrolytic capacitors has benefitted the electronics industry, electrolytic capacitors inadvertently installed backwards have plagued and continue to plague the industry.
Non-Polarized
Capacitor Schematic
Symbol
Polarized Capacitor Schematic
Symbol

## Slide 4: Capacitors (Continued)
The capacitance of a parallel plate capacitor is calculated as follows:
where A is the plate area, d is the distance
between plates and ε is a material property called
permittivity of the insulating (dielectric) material between the plates.
The permittivity
Relative permittivity ɛr = 1 for air or a vacuum.
According to the parallel plate capacitor equation, increasing will increase C.
So dielectrics with large relative permittivity are desirable for capacitors.
Some ceramics used in ceramic capacitors have ɛr > 1000.
+q charge on top plate
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
_
-q charge on bottom plate
Cross-Section of Rectangular Parallel Plate Capacitor
E
Distance
between
Plates: d

## Slide 5: Capacitors (Continued)
Permittivity describes the ability of a dielectric
material (insulator) to polarize (align) when
exposed to an electric field.
So increasing ɛr means increasing polarization.
Dielectric polarization results in a reduced electric
field between the capacitor plates for a given charge, resulting in more charge per volt, i.e., more capacitance.
Reducing the distance d between plates also results in a smaller voltage between the plates for a given charge, i.e., more charge per volt, and therefore more capacitance. The smaller voltage is because less work is involved to separate charges from one plate to the other.
Also increasing plate or surface area A increases the capacitor charge storage capability. This implies that paralleling capacitors results in an increase in capacitance, i.e., Ceq = C1 + C2 + … + CN for parallel capacitors.
Physics of capacitors is covered in more detail in Physics 220 and ECEN 390 – Electricity and Magnetism.

## Slide 6: Capacitor Current and Voltage
This says that the current flowing into or out of a capacitors plates is zero, unless the voltage across the capacitor is changing.
A capacitor behaves as an open circuit to constant dc.
Capacitors oppose a change in voltage, i.e., capacitors provide voltage inertia.

## Slide 7: Capacitor Energy Storage
Ideal capacitors do not dissipate power, rather they are energy storage and delivery elements.
Power delivered to a capacitor:
Power is the energy rate, i.e., the rate at which energy is generated or expended.
is a simply a dummy variable to be distinguished from t).

## Slide 8: Parallel Capacitors
Adjacent capacitor of value C charges to voltage vs, resulting ina charge of
q = Cvs on the top plate and a charge of – Cvs on the bottom plate.
Add a second capacitor C2 of value C in parallel with C1 and the
resulting charge stored in the circuit is doubled. Overall charge stored
on the top plates of C1 and C2 now equals 2Cvs. Overall circuit behaves
as if an equivalent capacitor Ceq = 2C were connected across the source
voltage vs. So equivalent capacitance of two parallel capacitors each of
value C equals 2C.
For N capacitors connected in parallel: Ceq = C1 + C2 + …. CN.
Capacitors in parallel add the same as resistors in series.

## Slide 9: Series Capacitors
Adjacent capacitor of value C charges to voltage vs, resulting in a charge of q = Cvs on
the top plate and a charge of –Cvs = -q on the bottom plate.
Add a second capacitor C2 of value C in series with C1 and the resulting voltage
across each capacitor is halved, resulting in ½ of the charge stored on each capacitor.
Now the overall charge stored on the top plates of C1 and C2 equals Cvs/2, as
series connected capacitor all have the same separated charge. Overall circuit
behaves as if an equivalent capacitor Ceq = C/2 were connected across the source
voltage vs. So equivalent capacitance of two series capacitors each of value C equals C/2.
Capacitors in series add the same as resistors in parallel.
Poll Questions

## Slide 10: Series Capacitor Example
Determine the voltage across C2 in the adjacent DC circuit, i.e., vC2.
Series capacitors all have the same current , and therefore the same
separated charge.
q = vbattCeq = (12 V)() = 18 µC. This is separated charge magnitude on each plate of the two series capacitors.
Consequently, both C1 and C2 have +18 µC on the top plate and -18 µC on the bottom plate.
vC1 = q/C1 = (18 µC)/(2.2 µF) = 8.18 V. vC1 = 8.18 V.
vC2 = q/C2 = (18 µC)/(4.7 µF) = 3.83 V. vC2 = 3.83 V. vC1 + vC2 = 8.18 V + 3.83 V = 12.0 V, i.e., KVL applies.
Series capacitors have the same separated charge. Since q = Cv, the larger capacitor has the smaller voltage across it in a series string, i.e., v = q/C.

## Slide 11: Capacitor Summary
Capacitance
For a parallel-plate capacitor: .
Capacitors store energy in an electric field.
Equivalent capacitance of series capacitors is smaller than the smallest capacitance.
For capacitors connected in Parallel: Ceq = C1 + C2 + …. CN.
Paralleling capacitors increases charge storage for a given voltage, i.e., increases capacitance.

## Slide 12: Capacitance Calculation Examples
Example 1: Calculate the capacitance of a capacitor with 1 meter by 1 meter plate area and a plate spacing of 1 mm with an air dielectric air (ɛr = 1). ɛo = 8.85E-12 Farads/meter.
Area A = 1 m2 . Distance d = 0.001 m.
Example 2: How big of capacitor is required to store 1 µCoulomb of charge for a voltage of 1 V?
q = Cv. C = q/v = (1 µC)/(1 V) = 1 µF. C = 1 µF.
Example 3: How much energy is stored in capacitor C1 in the adjacent DC circuit?
Capacitors appear as an open circuit to DC.
w =

## Slide 13: Equivalent Capacitance Examples
What is the equivalent capacitance as seem at the
a – b terminals of the adjacent circuit?
Ceq equals C1 in series with C2ǁC3.
Series capacitor application:
Polarized capacitors can be connected in series as shown in the adjacent schematic
and reliably used in AC applications. The opposite polarity series connection means
that one capacitor has the proper polarity, while the other has reversed polarity. The capacitor with proper polarity prevents current flow through the reversed polarity capacitor, which prevents damage, resulting in a reliable polarized capacitor configuration for AC applications. This technique is used to construct large value capacitors from larger value polarized capacitors.

## Slide 14
Aluminum Electrolytic Capacitors
Anodizing aluminum foil forms aluminum oxide dielectric (εr ≈ 10), resulting in large capacitance per volume because of large surface area due to etched anode along with thin insulative layer d. Reverse biasing the capacitor can damage the anode oxidized (insulative) layer if nonnegligible current is allowed to flow, causing heating which can result in an exploding capacitor.
Polarized capacitors have been a staple of the electronics industry for years, and have also resulted in many circuit failures when inadvertently reverse biased.

## Slide 15
Electrochemical Double Layer Capacitors (EDLC)
Large capacitance attributed to extremely large surface area and extremely small distance between charges in the electrostatic double layer.
EDLC capacitors can have capacitance values > 1 F (Farad), and are often referred to as supercapacitors.

## Slide 16: DC Blocking Capacitor
Given that vac is a high frequency ac signal, what does the output voltage vout equal in the circuit below?
vout = vac, because capacitors block constant dc voltages.
Can analyze this circuit using Superposition, separating out the
DC and AC supplies.
Oscilloscopes offer ac coupling, meaning that a large value capacitor is placed in series with the input to block constant dc voltages associated with the signal to be measured.

## Slide 17: Electromagnetisms
Current flow in a conductor produces a
magnetic field around the conductor.
Electricity and magnetism are linked.
Right-hand rule - Point thumb in the direction of
current flow and curled fingers point in the direction
of magnetic lines of force.
Can concentrate magnetic field by utilizing coils of wire.
Solenoid  Helical coil electromagnet used to actuate
many electromechanical devices.
Solenoid works on constant dc currents, because
constant dc currents create a magnetic field.

## Slide 18: Electromagnetisms (Continued)
Electromagnetic Induction – an emf is generated within a conductor or a coil when magnetic field lines, referred to as magnetic flux, cut a conductor or coil. Changing magnetic flux produces an emf.
Electromagnetic induction is employed in electrical generators used to convert mechanical energy into electrical energy.
Faraday’s Law of Electromagnetic Induction – The emf induced in a coil of wire is proportional to the rate of change of magnetic flux () linking (surrounding) the coil.
Induced voltage can be magnified by using coils with many turns, with N being the number of turns.
For a complete circuit, the induced voltage will produce a current.
Lenz’s Law – Currents induced by changing magnetic flux flow in a direction so as to create magnetic flux that oppose the original change in flux. (Conservation of energy).

## Slide 19: Inductance
Self Inductance – Changing currents in coils induce coil voltages that oppose the current changes.
Linear relationship between counter-emf and rate of change of current,
the slope of which is inductance L with units of Henrys.
Induced emf for Increasing diL/dt.
Induced emf for Decreasing diL/dt.
No Induced emf for diL/dt = 0.

## Slide 20: Inductors
An inductor consists of a coil of magnet wire (copper wire with insulating varnish coating), with or without a ferromagnetic core.
A current flowing through an inductor results in an associated
magnetic field, with electrical energy stored in the field.
Inductor Schematic
Symbol

## Slide 21: Inductor Voltage and Current
This says that the voltage across an inductor is zero, unless the current through the inductor is changing.
An inductor behaves as a short circuit to constant dc.
Inductors oppose a change in current, i.e., inductors provide current inertia.

## Slide 22: Inductor Energy Storage
Ideal inductors do not dissipate power, rather they are energy storage and delivery elements.
Power Delivered to an Inductor:
Power is the energy rate, i.e., the rate at which energy is generated or expended.
is a simply a dummy variable to be distinguished from t).

## Slide 23: Inductor Energy Storage Example
Example 1: How much energy is stored in inductor L1 in
the adjacent DC circuit?
Inductors appear as a short circuit to DC.
w =

## Slide 24: Inductor and Capacitor Summary
Inductor voltage:
No current change, no induced voltage, i.e., inductors act as short circuits to constant dc.
Inductors oppose a change in current, i.e., inductors provide current inertia.
Inductors store energy in a magnetic field.
For inductors connected in Series: Leq = L1 + L2 + …. LN.
Capacitor current:
No voltage change, no current flow, i.e., capacitors act as open circuits to constant dc.
Capacitors oppose a change in voltage, i.e., capacitors provide voltage inertia.
Capacitors store energy in an electric field.
Poll Questions

## Slide 25
Transformers
Transformer: Magnetic circuit used for stepping AC voltages and currents up or down.
Magnetic flux is contained within high permeability core.
Changing (AC) primary current produces changing magnetic flux in the transformer core that induces a changing (AC) secondary voltage. Mainstream application of Faraday’s Law.
Why AC and not DC also?
Because changing flux is necessary for electromagnetic induction.

## Slide 26: Transformer Examples
By me (Photograph) [GFDL (http://www.gnu.org/copyleft/fdl.html), CC-BY-SA-3.0 (http://creativecommons.org/licenses/by-sa/3.0/) or CC BY-SA 2.5-2.0-1.0 (https://creativecommons.org/licenses/by-sa/2.5-2.0-1.0)], via Wikimedia Commons
Notes: By me (Photograph) [GFDL (http://www.gnu.org/copyleft/fdl.html), CC-BY-SA-3.0 (http://creativecommons.org/licenses/by-sa/3.0/) or CC BY-SA 2.5-2.0-1.0 (https://creativecommons.org/licenses/by-sa/2.5-2.0-1.0)], via Wikimedia Commons

## Slide 27: Transformer Examples (Continued)

## Slide 28: Ignition Coil
The ignition coil is essentially a high-voltage step-up transformer made up of two coils of wire. One coil of wire is called the primary coil. Wrapped around it is the secondary coil. The secondary coil normally has hundreds of times more turns of wire than the primary coil. Current flows from the battery through the primary winding of the coil.
The key to the coil's operation is what happens when the circuit is suddenly opened by the points. The magnetic field surrounding the secondary coil changes rapidly, inducing very high voltage in the secondary coil, (greater than 20,000 volts) because of the number of coils in the secondary winding.
By Honda CB77 Restoration [CC BY 2.0 (http://creativecommons.org/licenses/by/2.0)], via Wikimedia Commons
Ignition Coil Video. (4:06)
Notes: By Honda CB77 Restoration [CC BY 2.0 (http://creativecommons.org/licenses/by/2.0)], via Wikimedia Commons

## Slide 29
The End

## Slide 30: Capacitors and Inductors
Why does a capacitor oppose changes in voltage?
  Because voltage changes across a capacitor results in current flow to or from the capacitor, which limits the abruptness of the voltage change. Charge has to transfer before the voltage across the capacitor can change and this takes time.
The voltage across a capacitor cannot change instantaneously.
Why does an inductor oppose changes in current?
  Because a current change in an inductor results in a changing magnetic flux, which then produces a counter emf that opposes the change in the current.
The current through an inductor cannot change instantaneously.

## Slide 31
Extra

## Slide 32: American Wire Gauge Wire Sizes
Increasing gauge number denote decreasing wire diameters.
Smaller gauge number wire can conduct larger currents.
Stranded copper wire often used for heavy gauge as it bends easier.
Want to choose the correct AWG number to handle largest expected current.
Notes: Graphic by BYU-Idaho Campus Curriculum Development in Illustrator

## Slide 33: Series Capacitors
Series capacitors all have the same current ,
and therefore the same charge. Connected plates between
C1 and C2 and C2 and C3 have equal and opposite charge
on the connected plates.
Applying KVL: vs = vC1 + vC2 + vC3. vc = q/C.
Equivalent capacitance of series capacitors is smaller than the smallest capacitance.

## Slide 34: Inductor Summary
Inductors store energy in a magnetic field.
Equivalent inductance of parallel inductors is smaller than the smallest inductor.
For inductors connected in Series: Leq = L1 + L2 + …. LN.
Series inductors increases energy storage for a given current, i.e., increases inductance.
Why do inductors oppose a change in current?
Physically, because a current change in an inductor results in a changing magnetic flux, which induces a counter emf opposing the original current change.

## Slide 35: Capacitors and Inductors
Capacitor current: .
Capacitor current proportional to voltage changes.
No voltage change, no current flow, i.e., capacitors block constant dc voltages.
Capacitors oppose a change in voltage, i.e., capacitors provide voltage inertia.
Inductor voltage: .
Inductor voltage proportional to current changes.
No current change, no induced voltage, i.e., inductors act as short circuit to constant dc.
Inductors oppose a change in current, i.e., inductors provide current inertia.
Poll Questions