## Slide 1: ECEN 150 Circuit Analysis I
Frequency Response

## Slide 2
Exponents and Logarithms
a = bx, where a is the argument, b is the base and x is the exponent.
What bx corresponds to a?
x = logba.
For example, 10x = 10,000. What exponent x for the base 10 results in 10,000?
x = log10(10,000) = 4, which means that 104 = 10,000.
For example, 2x = 4096. What exponent x for the base 2 results in 16?
x = log2(4096) = 12, which means that 212 = 4096.

## Slide 3
Exponents and Logarithms (Continued)
By definition, base b > 0. So, for any real exponent x, bx ≥ 0.
Even 10-100 > 0, although very close to zero.
So argument a = bx ≥ 0. For -∞ ≤ x ≤ 0, 0 ≤ a = bx ≤ 1.
Logarithms are only defined for positive arguments a.
logb(0) corresponds to 0 = bx, which is true for exponent x = -∞.
Logarithms useful for wide ranging quantities, such as the magnitude of seismic oscillations (Richter scale), dynamic range of human hearing, amplifier gain levels, and filter attenuation levels.
In science and engineering there is no escaping the need to become proficient with logarithms.
Some Important Logarithmic Properties:
  log(P1P2) = log(P1) + log(P2). Similarly, log(P1/P2) = log(P1) - log(P2).
  log(P)n = nlog(P).
  log(1) = 0.
Exponential form
Logarithmic form
base
exponent
a = bx x = logba

## Slide 4
decibels (dB)
Human hearing responds logarithmically in changes to sound pressure level (SPL).
At normal human hearing levels, sound pressure level has to double to be perceived as being louder.
Hence, logarithmic scales are used when describing sound level pressure, i.e., dB SPL.
The decibel (dB) scale defined as GdB = Dimensionless ratio assigned the unit dB.
Power gain in dB: GdB =
Voltage gain in dB: AV_dB for .
For , AV_dB
  K, where K = .
Often this K is ignored when .
Power Gain: GdB =

## Slide 5
Ex. 1: An electrical filter attenuates an unwanted 120 Hz 1 V peak input sinusoid signal so that the resulting peak output amplitude, i.e., Vom = 3 mV. What is the dB voltage gain of the filter at 120 Hz?
Voltage gain magnitudes < 0 dB imply the magnitude of / < 1, i.e., attenuation.
Ex. 2: For an amplifier with voltage gain of 41 dB, i.e., AV_dB = 41 dB, what is the magnitude of the peak sinusoidal output voltage, i.e., Vom, for peak sinusoidal input voltage Vim = 2 mV?
Voltage (dB) Examples

## Slide 6
Ex. 3: A signal is first amplified by a voltage amplifier having 36 dB voltage
gain, then amplified by another amplifier with 32 dB voltage gain. What is
the overall dB voltage gain for the system?
Many amplifiers, including op-amps utilize multiple voltage gain stages.
Voltage (dB) Examples (Continued)

## Slide 7
Example 4: For gain magnitude
Need to either convert all to absolute gain ratio or all to dB gain. I chose to convert to dB gain.
.
When working with amplifier gains, often have to switch back and forth between dB gain or absolute gain ratio.
Voltage (dB) Examples (Continued)
Poll Questions

## Slide 8: Transfer Function in Terms of Phasors: H(ω)
Then for a linear network the input phasor X(ω) equals (ω) equals B
Note, that the input phasor X(ω) does not mean reactance, and(ω) does not mean admittance. Rather the variables X(ω) and Y(ω) mean input and output phasors when referring to transfer functions.
System Transfer Function H(ω) of a circuit is the frequency dependent ratio of phasor output Y(ω) to phasor input X(ω). When both Y(ω) and X(ω) are voltages, then the Transfer Function corresponds to system voltage gain.
Frequency response of a circuit can be determined by evaluating for ω ranging 0 to ∞.
Linear Network
H(ω)
Input Phasor X(ω)
Output Phasor Y(ω)

## Slide 9: Transfer Function and Frequency Response
Frequency response of a circuit can be determined by evaluating for ω ranging 0 to ∞.
When X(ω), and Y(ω) are voltages, then is the frequency dependent voltage gain, having a magnitude, often expressed in dB, along with a phase angle, usually expressed in degrees.
Roots of numerator polynomial Y(ω) are zeros of Transfer Function. Frequency Response equals zero at a zero.
Roots of denominator polynomial X(ω) are poles of Transfer Function.
Poles and zeros of the transfer function determine the resulting frequency response. Transmission zeros result in an increase in the slope of the magnitude of the transfer function, whereas poles result in a decrease in the slope.
Linear Network
H(ω)
Phasor X(ω)
Phasor Y(ω)
Result of a Zero at 102 rad/s.
Log Frequency (ω)
100
101
102
103
104
|H(ω)| dB
Result of a Pole at 102 rad/s.
Log Frequency (ω)
100
101
102
103
104
|H(ω)| dB

## Slide 10: Basic Filter Types
Electrical filters are designed to allow some frequencies through, while blocking (attenuating) others, i.e., frequency discrimination.
A low-pass filter can be used to block (attenuate) unwanted high-frequency noise.

## Slide 11: Filter Bandwidth
Filter bandwidth indicates the range of frequencies allowed through the filter.
Practical filters do not treat all frequencies equally in the passband, attenuating frequencies near to and at the cutoff frequency, i.e., ωc = 2πfc.
Defining the cutoff frequency as an attenuation equal to ½ of the maximum power passing through the filter is a commonly used bandwidth definition for practical filter.
Half-Power Point: -3.01 dB corresponds to ½ power.
Hence, -3.01 dB, often referred to as the 3 dB attenuation is a commonly used bandwidth definition for electrical filters.
ωc is referred to as the 3 dB cutoff frequency for the above practical low-pass filter, and is the frequency at which the associated power is ½ of the maximum power passing through the filter.

## Slide 12: 3 dB Bandwidth
Need to arrive at a bandwidth definition for electrical filters, with 3 dB Bandwidth being one common definition.
Half-Power Point:
Voltage amplitude ratio of 0.707, i.e., -3.01 dB,
corresponds to the Half-Power points for electrical
filters.
The adjacent lowpass filter transfer function
characteristics has a 3 dB bandwidth, i.e., cutoff frequency
of 159 Hz.
The cutoff frequency also corresponds to the magnitude
of the pole location in the complex plane. Filtering, poles and
zeros are studied in more detail in signal processing classes such as ECEN 380 and ECEN 480.

## Slide 13: Transfer Function Example 1
For a Capacitor:

## Slide 14: Transfer Function Example 1 (Continued)
Frequency dependent voltage divider.
As frequency of Vs increases, decreases because of decreasing
magnitude of .
LTspice automatically plots the transfer function
magnitude in terms of dB and uses a logarithmic
frequency axis, which is termed a Bode plot.
LTspice

## Slide 15: Bode Plots
Bode magnitude plot utilize dB magnitude and linear phase versus logarithmic frequency axis.
The logarithmic magnitude and frequency axes are beneficial when there are large differences between the minimum and maximum amplitudes and frequencies of interest.
Originally referred to a straight-line
approximation to the actual filter response,
but now also refers to exact calculated and/or
measured values.
Regarding the straight-line approximation to
the magnitude of the transfer function, the slope
increases by 20 dB/decade well beyond a pole
frequency. (The slope of the magnitude increases
by 20 dB/decade well beyond a zero frequency).
Regarding the straight-line approximation to
the phase shift of the transfer function, there is a
-45˚ phase shift at the pole frequency and a -90˚
phase shift well beyond the pole frequency.
(The phase shifts by +45˚ at a zero frequency
and +90˚ well beyond a zero frequency).

## Slide 16: Reactance – Magnitude of Impedance
Capacitors look like an open at DC, and a short
at high-frequency AC.
Inductors look like a short at DC, and an open
at high-frequency AC.

## Slide 17
At series resonance ZL = -ZC, so that ZL + ZC = 0, implying that the voltage across the series inductor and capacitor equals 0 at the series resonance frequency.
Series Resonance

## Slide 18
Half-Power Level:
Current Is decreases in magnitude by at half-power level.
Impedance has magnitude equal to at the half-power level.
.
Series Resonance (Continued)

## Slide 19
3 dB Frequencies:
Current Is decreases in magnitude by
at half-power level.
Hence, half-power levels also corresponds to -3.01 dB
decrease in current from maximum value.
For the above circuit: = 143. = 404.
261 rad/s. 547 rad/s.
are the 3 dB frequencies.
3 dB (Half-Power) Bandwidth. B = -= 286 rad/s =
Series Resonance (Continued)

## Slide 20
3 dB Bandwidth:
3 dB (Half-Power) Bandwidth. B = -
For a series resonant circuit:
Decreasing R/L ratio results in narrower bandwidth.
Quality Factor Q of a resonant circuit is ratio
of resonant frequency to 3 dB bandwidth.
Series Resonance (Continued)

## Slide 21
Q of a resonant circuit is ratio of energy stored to energy dissipated per cycle at resonance.
Decreasing R, increases Q in a
series resonant circuit because of
decreased energy loss.
3 dB Bandwidth B = -
Q is a dimensionless ratio.
High Q circuits (Q ≥ 10) have a relatively large ratio of energy storage to energy dissipated per cycle at resonance.
Series Resonance (Continued)

## Slide 22
At parallel resonance ZL = -ZC, so that ZL in parallel with ZC = = , implying that Vo is maximum at the parallel resonance frequency.
Parallel Resonance

## Slide 23
Impedance decreases in magnitude by
at the following frequencies:
For the above circuit: = 98.0.
= 390, 292 rad/s. 488 rad/s.
3 dB Bandwidth. B = -=196 rad/s =
Parallel Resonance (Continued)

## Slide 24
3 dB Bandwidth:
3 dB Bandwidth. B = -
For a parallel resonant circuit:
Increasing RC product results in narrower bandwidth.
Quality Factor Q of a resonant circuit is ratio
of resonant frequency to 3 dB bandwidth.
Parallel Resonance (Continued)

## Slide 25
Q of a resonant circuit is ratio of energy stored to energy dissipated per cycle at resonance.
Increasing R, increases Q in a
parallel resonant circuit, because of
decreased energy loss.
3 dB Bandwidth B = -
Q is a dimensionless ratio.
High Q circuits (Q ≥ 10) have a relatively large ratio of energy storage to energy dissipated per cycle at resonance.
Parallel Resonance (Continued)

## Slide 26
For the adjacent series RLC circuit, choose the best answer for
the overall impedance magnitude in ohms between the a and b
terminals at the resonant frequency.
    a. 0.
    b. R.
    c.
    d. .
  b. R, because the series L and C appear as a short circuit.
For the adjacent parallel RLC circuit, choose the best answer for
the overall impedance magnitude in ohms between the a and b
terminals at the resonant frequency.
    a. 0.
    b. R.
    c.
    d. .
  b. R, because the parallel L and C appear as an open circuit.
Resonance Review

## Slide 27: Basic Filter Types
Electrical filters are designed to allow some frequencies through, while blocking (attenuating) others, i.e., frequency discrimination.
A low-pass filter can be used to block (attenuate) unwanted high-frequency noise.

## Slide 28
RC Lowpass Filter Frequency Response
Use substitution s = jω = initially to avoid complex math.
For a Capacitor:
LTspice

## Slide 29
RC Lowpass Noise Filter with fc = 15.9 Hz
Noisy dc measurement can be improved by noise filtering via a lowpass filter.
For the adjacent low-pass filter, fc = 15.9 Hz.
All measurements have some unwanted variation, i.e., noise.
Additional digital lowpass filtering can be incorporating by means of averaging of individual measured results.

## Slide 30: RC Highpass Filter Frequency Response
LTspice

## Slide 31
RC Highpass Filter with fc = 159 Hz
Some ac signals have unwanted dc offset voltages.
Unwanted dc offset voltages can be removed via a highpass filter.
For the adjacent high-pass filter, fc = 159 Hz.
Highpass filter blocks dc and low-frequency signals,
while passing through higher-frequency signals.
Mean (average) of the input signal is 1 V, whereas the
mean of the output signal is 0 V, i.e., dc offset voltage has
been removed.
ECEN 380 – “Signals and Systems” and
ECEN 480 – “Digital Signal Processing” go into
much more detail on filtering and signal processing.

## Slide 32: Source Transformations
Source transformation relationships: R = R, is = vs/R, vs = isR.
Resulting resistance R, stays the same for the above source transformations.
Resonant frequency and 3 dB bandwidth equations also stay the same for the above parallel resonant circuit source transformation.
is = vs/R
vs = isR

## Slide 33
Frequency Dependent Voltage Divider:
At DC, because of inductor L.
At high frequency AC,
because of capacitor C.
because
Transfer Function: Use the substitution s = jω to avoid complex math for now.
Bandpass Filter Using Parallel Resonance

## Slide 34
From previous slide:
Substitute jω for s.
Resulting circuit is a band-pass filter with a
center frequency of 60 Hz and 3 dB bandwidth
of 31.3 Hz.
At parallel resonance ZL = -ZC, so that ZLǁZC = ,
implying that magnitude of Vo is maximum at the
parallel resonance frequency.
Bandpass Filter (Continued)

## Slide 35
Bode Plots.
Bandpass Filter (Continued)
MATLAB
LTspice

## Slide 36
Frequency dependent voltage divider using phasors.
At DC, because of capacitor C.
At high frequency AC,
because of inductor L.
because
Resulting circuit is a band-stop filter with a notch frequency of 60 Hz.
Transfer Function: Use the substitution s = jω to avoid complex math for now.
Bandstop (Notch) Filter Using Series Resonance

## Slide 37
Resulting circuit is a band-stop (notch) filter with a
notch frequency of 60 Hz and 3 dB bandwidth
of 31.3 Hz.
At series resonance ZL = -ZC, so that ZLǁZC = ,
implying that magnitude of Vout is zero at the
series resonance frequency.
Bandstop (Notch) Filter (Continued)

## Slide 38
Bode plots.
Bandstop (Notch) Filter (Continued)
MATLAB
LTspice

## Slide 39
The End

## Slide 40
Extra

## Slide 41
Voltage Gain in decibels (dB)
Since and/or can be determined from an oscilloscope at various frequencies simply by measuring the peak sinusoidal input value and the peak sinusoidal output value and calculating the ratio of the results at each frequency of interest.
The logarithm of a reciprocal of a quantity is simply the negative logarithm of that quantity.
Linear Network
H(ω)
Phasor X(ω)
Phasor Y(ω)

## Slide 42: Reactance – Magnitude of Impedance
Capacitive Reactance: . Inductive Reactance: .
For circuits having series R and C or parallel R and C components, the frequency at which is a special frequency referred to as resonance.
Resulting impedance behavior depends upon whether capacitor and inductor are in series, i.e., series resonance, or in parallel, i.e., parallel resonance.

## Slide 43: Bode Plots
Bode magnitude plot utilize dB magnitude axis versus logarithmic frequency axis.
Bode phase plot utilizes linear phase axis in degrees versus logarithmic frequency axis.
Originally referred to a straight-line
approximation to the actual filter response, but
now also refers to exact calculated and/or
measured values.
Regarding the straight-line approximation to
the magnitude of the transfer function, the slope
increases by 20 dB/decade well beyond a pole
frequency. (The slope of the magnitude increases
by 20 dB/decade well beyond a zero frequency).
Regarding the straight-line approximation to
the phase shift of the transfer function, there is a
-45˚ phase shift at the pole frequency and a -90˚ phase shift well beyond the pole frequency. (The phase shifts by +45˚ at a zero frequency and +90˚ well beyond a zero frequency).
-3.01 dB gain on actual response at Break point or pole frequency
-45˚ phase shift at Break point or pole frequency.
Straight-line approximations to transfer function magnitude.
Actual transfer function magnitude.
Straight-line approximations to transfer function phase.
Actual transfer function phase.
Slope of 0 dB/decade.
Slope of -20 dB/decade after break point or pole frequency.
0˚ phase shift.
-90˚ phase shift.

## Slide 44
Logarithmic Scale
Logarithmic Scale  Increase is linear in the exponent, rather than the overall value.
100.5 = 3.16. So 3.16 is ½ way between 100 = 1 and 101 = 10 on a base 10 logarithmic scale.
101.5 = 31.6. So 31.6 is ½ way between 101 = 10 and 102 = 100 on a base 10 logarithmic scale.

## Slide 45
Since (Any Base)0 = 1, x = log(Any Base)(1) = 0.
Negative x = logb(a) values occur for argument a ranging between 0 to 1.
log10(0.1) = -1.0, i.e., 10-1 = 1/10 = 0.1.
Exponential form
Logarithmic form
base
exponent
a = bx x = logba
The logarithm of a reciprocal of a quantity is simply the negative logarithm of that quantity.
For example, log10(10) = 1.0, whereas log10(1/10) = -1.0. (Reciprocals)
Exponents and Logarithms (Continued)