## Slide 1: ECEN 150 Circuit Analysis I
Nodal and Mesh Analysis

## Slide 2: Barnyard Example
A farmer counts heads and feet of pigs and chickens in his barnyard, and get 17 heads and 40 feet. How many chickens and pigs does the farmer have?
Two Equations  Two Unknowns
pigs + chickens = 17. (Number of heads).
4pigs + 2chickens = 40. (Number of feet).
Can Solve by Substitution
chickens = 17 – pigs. (Substitute this expression into 4pigs + 2chickens = 40.)
4pigs + 2(17 – pigs) = 40. 4pigs - 2pigs + 34 = 40. 2pigs = 6. pigs = 3.
chickens = 17 – 3 = 14. chickens = 14.
Solution  (3 pigs, 14 chickens.)

## Slide 3: Barnyard Example (Continued)
A farmer counts heads and feet of pigs and chickens in his barnyard, and get 17 heads and 40 feet. How many chickens and pigs does the farmer have?
chickens = 17 – pigs.
Graphical Approach: chickens = 20 - 2pigs.
Solution  (3 pigs, 14 chickens.)

## Slide 4: Barnyard Example (Continued)
A farmer counts heads and feet of pigs and chickens in his barnyard, and get 17 heads and 40 feet. How many chickens and pigs does the farmer have?
Formal Approach Using Linear Algebra
Pigs + Chickens = 17. (Number of heads). x1 + x2 = 17.
4Pigs + 2Chickens = 40. (Number of feet). 4x1 + 2x2 = 40.
(1)x1 + (1)x2 = 17.
(4)x1 + (2)x2 = 40. Two unknowns are x1 and x2.
Define coefficient matrix A = , vector x = , and vector b =
Matrix multiplication, multiplies rows by columns. For example, given A = and x = , Ax =
Therefore, for A = , x = , and b = , the following are all equivalent:
x1 + x2 = 17.
4x1 + 2x2 = 40.
Ax = b
A
x
b

## Slide 5: Barnyard Example (Continued) (Continued)
A farmer counts heads and feet of pigs and chickens in his barnyard, and get 17 heads and 40 feet. How many chickens and pigs does the farmer have?
Formal Approach Using Linear Algebra
Pigs + Chickens = 17. (Number of heads). x1 + x2 = 17.
4Pigs + 2Chickens = 40. (Number of feet). 4x1 + 2x2 = 40.
Matrix form of the above equations: Ax = b, . Solve for the vector x: x = A-1b.
MATLAB Command Window:
              A^-1 denotes matrix inverse in MATLAB.
            x =
A
x
b

## Slide 6: Nodal Analysis
Algorithmic approach to solve for node voltages.
Choose the node connected to the most elements as the
reference node. All voltages are then with respect to the
reference node.
Why don’t we need to write equations for the nodes
labeled v1 and v4?
Because those voltages are already known.
Use KCL to write current equations at nodes labeled v2 and v3.
Positive conventional current flows through a resistor from the higher to lower voltage.
KCL at v2: i1 = i2 + i3, Using Ohm’s Law, .
KCL at v3: i3 = i4 + i5,
2 equations to solve for two unknown node voltages v2 and v3 in the above circuit.
Nodal analysis uses KCL to arrive at node voltages.
iR1
vhigher
R1
vlower
+
_
i1
i3
i3
i5
i2
i4

## Slide 7: Nodal Analysis Example 1
Determine the node voltages v1 and v2 in adjacent circuit
using nodal analysis.
Choose node v3 as reference node. So now node voltages
v1 and v2 are with respect to reference node v3.
Need two independent equations to solve for the two
unknown node voltages v1 and v2.
Assign current directions for i2, i3 and i4 and apply KCL.
i2
i3
i3
i4

## Slide 8: Nodal Analysis Example 1 (Continued)
Determine the node voltages v1 and v2 in adjacent circuit
using nodal analysis.
From the previous slide:
Equation 1:
Equation 2:
Since all terms include a factor of 10-3, I will multiply both sides of each equation by 1000, to simplify the coefficients.
(Equation 1 after scaling by 1000): 15.8v1 – 9.09v2 = 50.
(Equation 2 after scaling by 1000): 9.09v1 – 12.8v2 = 4.5.
Matrix form: Ax = b.
. x = A-1b.
i2
i3
i3
i4
MATLAB Command Window
v1 = 5.01 V. v2 = 3.20 V.
Poll Questions

## Slide 9: Nodal Analysis Example 2
Determine current in resistor R1, i.e. iR1,
in adjacent circuit using nodal analysis.
Choose node v5 as reference node.
Already know voltages for nodes labeled
v1 andv4.
Node v2: i1 = i2 + i3.
(Equation 1 after scaling by 1000): 20.8v2 – 10.0v3 = 107.
Node v3 : i3 + i5 = i4.
(Equation 2 after scaling by 1000): -10.0v2 + 20.5v3 = 83.3.

## Slide 10: Nodal Analysis Example 2 (Continued)
To demonstrate that chosen node current
directions don’t affect the solution, let’s
re-calculate node v3 with i5 current chosen
to flow into the battery vs2 instead of out of
the battery as we previously chose.
Then i3 = i4 + i5 and i5 = (v3 – v4)/R5.
Node v3: . i3 = i4 + i5.
Previously obtained
the same algebraically.
(Equation 2 after scaling by 1000): -10.0v2 + 20.5v3 = 83.3.
Same equation as before with i5 flowing the opposite direction. Why?
Because the relationship between node voltages and resistances does not change by our choice of current direction, which is often just a guess in many nodal analysis circuits.

## Slide 11: Nodal Analysis Example 2 (Continued)
(Equation 1): 20.85v2 – 10.00v3 = 107.14.
(Equation 2): -10.00v2 + 20.46v3 = 83.33.
Matrix form: Ax = b.
. x = A-1b.
v2 = 9.27 V. v3 = 8.59 V. iR1 = (15 – 9.27)V/(140 Ω) = 40.9 mA. iR1 = 40.9 mA.
MATLAB Command Window

## Slide 12: Nodal Analysis Using MATLAB Symbolic Capability
(Equation 1): .
(Equation 2):
% MATLAB Symbolic Nodal Analysis Example 1.
clear all, close all;
R1 = 140;
R2 = 270;
R3 = 100;
R4 = 470;
R5 = 120;
sympref('FloatingPointOutput', true) % Set Symbolic Preferences.
syms v2 v3 % Define symbolic variables.
eq1 = (1/R1 + 1/R2 + 1/R3)*v2 - (1/R3)*v3 - 15/R1;
eq2 = (-1/R3)*v2 + (1/R3 + 1/R4 + 1/R5)*v3 - 10/R5;
solution = solve(eq1, eq2, v2, v3);
v2 = 9.27 V. v3 = 8.60 V.
iR1 = (15 – 9.27)V/(140 Ω) = 40.9 mA.
iR1 = 40.9 mA.

## Slide 13: Nodal Analysis Example 3
Determine current in resistor R3, i.e. iR3,
in adjacent circuit using nodal analysis.
Choose node v4 as reference node.
Already know voltages for nodes labeled
v1 and v3.
Node v2: i1 + i2 = i3.
The current through resistor R3, i.e. , happens to also equal branch current in this example, but they could be different in the general case.
i1
i3
i2

## Slide 14: Circuit Terminology
Circuit comes from Latin, meaning to “go around”.
Open Circuit indicates that there is a gap or opening in the circuit so that no current flows. The gap or opening may be an open switch.
Closed circuit indicates that there is a complete path for current to flow around the circuit. Any switches in the circuit must be closed to form a closed circuit.
Short Circuit indicates that a very low resistance path is connected across an element, resulting in the current bypassing the element that is shorted, since current flows through the path of least resistance.
Branch – A single element, such as a voltage source or resistor.
Node – A electrical connection between two or more elements, having negligible resistance. Low-resistance wires form nodes in practical circuits
Loop – Any closed path in a circuit.
Mesh – A loop that does not contain any other loop within it. (Window pane).
Series connected elements exclusively share a single node, and therefore carry the same current. End-to-end series connected elements have the same current flowing through them.
Parallel connected elements are connected across the same two nodes. Therefore parallel connected elements have the same voltage across them.
Notes: Image by instructor

## Slide 15: Mesh (Loop) Analysis
Another algorithmic approach.
The adjacent circuit has two meshes, i.e. Mesh 1 and Mesh 2.
Resistor R2 is common to both meshes with
iR2 being algebraic sum of i1 and i2 mesh currents.
Convention is to define clockwise mesh currents. If actual
current flow is in the opposite direction of a clockwise then the
solved for mesh current will have a negative sign.
Mesh current i1 also equals branch current iR1, and mesh current i2 also equals branch current iR3. Branch current iR2 equals algebraic sum of i1 and i2 mesh currents.
Use KVL to write voltage equations for meshes 1 and 2.
Mesh 1: -vs1 + i1R1 + i1R2 – i2R2 = 0, (R1 + R2)i1 – R2i2 = vs1.
Mesh 2: i2R2 - i1R2 + i2R3 + vs2 = 0, -R2i1 + (R2 + R3)i2 = -vs2.
Solve for mesh currents i1 and i2.
Mesh analysis uses KVL to arrive at mesh currents.

## Slide 16: Mesh (Loop) Analysis Example 1
Determine voltage v2 with respect to circuit ground along with the
current in resistor R2, i.e. iR2, in adjacent circuit using mesh analysis.
Mesh 1: -vs1 + i1R1 + i1R2 – i2R2 = 0.
(R1 + R2)i1 – R2i2 = 6 V.
320i1 - 200i2 = 6.
Mesh 2: i2R2 – i1R2 + i2R3 + vs2 = 0.
-R2i1 + (R2 + R3)i2 = -12 V.
-200i1 + 440i2 = -12.
Matrix form: Ax = b, . x = A-1b.
Engineering notation in MATLAB: Home  Preferences  Command Window  Numeric Format  short eng.
    i1 = 2.38 mA. i2 = -26.2 mA. i2 current flows in the opposite direction illustrated above.
    iR2 = i1 – i2 = 2.38 mA - -26.2 mA = 28.6 mA flowing from v2 to ground.
    v2 = (28.6 mA)(200 Ω) = 5.72 V. v2 = 5.72 V.

## Slide 17: Mesh (Loop) Analysis Example 2
Determine voltage v2 with respect to circuit ground along with the
current in resistor R2, i.e. iR2, in adjacent circuit using mesh analysis.
Mesh 1: -vs1 + i1R1 + i1R2 – i2R2 + vs2 = 0.
(R1 + R2)i1 – R2i2 = 4 V.
320i1 - 220i2 = 4.
Mesh 2: -vs2 + i2R2 – i1R2 + i2R3 + vs3 = 0.
-R2i1 + (R2 + R3)i2 = 2 V, -220i1 + 660i2 = 2.
Matrix form: Ax = b, . x = A-1b.
i1 = 18.9 mA. i2 = 9.30 mA. v2 = vs1 - i1R1
v2 = 10V – (18.9 mA)(100 Ω) = 8.11 V. v2 = 8.11 V.
So conventional current iR2 flows from v2 to vs2.
iR2 = i1 – i2 = 18.9 mA – 9.34 mA = 9.56 mA, from v2 to vs2.
Mesh
Current
i1
Mesh
Current
i2
5 Poll Questions

## Slide 18: Mesh (Loop) Analysis Example 2 (Continued)
Determine voltage v2 with respect to circuit
ground along with the current in resistor R2,
i.e. iR2, in adjacent circuit using mesh analysis.
Mesh 1: (R1 + R2)i1 – R2i2 = 4 V.
Mesh 2: -R2i1 + (R2 + R3)i2 = 2 V.
% MATLAB Symbolic Mesh Analysis Example 1.
clear all, close all;
R1 = 100;
R2 = 220;
R3 = 440;
sympref('FloatingPointOutput', true) % Set Symbolic Preferences.
syms i1 i2 % Define symbolic variables.
eq1 = (R1 + R2)*i1 - R2*i2 - 4;
eq2 = -R2*i1 + (R2 + R3)*i2 - 2;
solution = solve(eq1, eq2, i1, i2);
        sympref(), i.e. symbolic preferences doesn’t have an engineering notation output option.
  i1 = 18.9 mA. i2 = 9.30 mA. v2 = vs1 - i1R1
v2 = 10V – (18.9 mA)(100 Ω) = 8.11 V. v2 = 8.11 V.
So conventional current iR2 flows from v2 to vs2.
iR2 = i1 – i2 = 9.6 mA.
            iR2 = 9.6 mA.
Mesh
Current
i1
Mesh
Current
i2

## Slide 19: Mesh (Loop) Analysis Example 3
Determine current in resistor R1,i.e. iR1, in adjacent circuit
Using mesh analysis.
Mesh 1: -vs1 + i1R1 + i1R2 – i2R2 = 0.
(R1 + R2)i1 – R2i2 = 15 V.
410i1 - 270i2 + 0i3 = 15.
Mesh 2: i2R2 – i1R2 + i2R3 + i2R4 – i3R4 = 0.
-R2i1 + (R2 + R3 + R4)i2 – R4i3 = 0,
-270i1 + 840i2 – 470i3 = 0.
Mesh 3: i3R4 – i2R4 + i3R5 + vs2 = 0, -R4i2 + (R4 + R5)i3 = -10 V,
0i1 - 470i2 + 590i3 = -10.
Matrix form: Ax = b, . x = A-1b.

## Slide 20: Mesh (Loop) Analysis Example 3 (Continued)
Determine current in resistor R1, i.e. iR1, in the circuit below using mesh analysis.
Matrix form: Ax = b,
.
x = A-1b.
i1 = 41.0 mA.
i2 = 6.60 mA.
i3 = -11.7 mA. What does this mean for the direction of i3?
Conventional i3 current flows from out of the positive terminal of vs2.
Using nodal analysis, we previously determined i1 = 40.9 mA, which is the same result using mesh analysis, accounting for some round off error in the calculations.
Nodal analysis is easier in this case as there are only two unknown node voltages, i.e. v2 and v3, whereas there are three unknown mesh currents, i.e. i1, i2 and i3.

## Slide 21: Series Circuit Application – Christmas Tree Lights
Common Christmas Tree lights use series
strings of 50 bulbs, so that each bulb has less
than 5 V across it.
Obvious problem with series string is that a
broken filament in one bulb takes out the entire
string and is hard to find.
Engineering to the rescue.
Standard mini-light bulb with insulated shunt
wire in case the filament breaks.
Broken filament results in entire string voltage
across one bulb, which heats the insulated shunt
wire, melting off the insulation and then shorting
across the two leads.
Result is broken filament does not take out entire
series string and bad bulb can easily be found.
Shunt Wire
Filament
Notes: Image by instructor

## Slide 22: Parallel Circuit Application – Terminal Strip
On/off switch and surge protection often included in terminal strips.
Several parallel high-current loads can exceed home circuit breakers.
Notes: Image by instructor

## Slide 23: Electrical Power Supplies
Power supplies provide electrical energy.
2 Major Types of Electrical Power Supplies:
  Voltage Sources.
  Current Sources.
Ideal voltage source provides constant voltage at the terminals for any load current.
Electrochemical batteries are good examples of a voltage source.
Ideal current source provides constant current at the terminals for any load voltage.
Solar panels are good examples of a current source.
How Do Batteries Work (4:19)
Notes: Image by instructor

## Slide 24: Series and Parallel Voltage Sources
Series Voltage Sources  Good idea.
Batteries with voltages > 4 V are usually strings of series connected cells.
Parallel Voltage Sources  Beware!
Voltage differences between parallel voltage sources can result in large currents!
Problems can arise when replacing just one of multiple parallel connected batteries because fresh battery will have a larger voltage, resulting in hard work for the fresh battery.
Common parallel battery example is jump starting a car with a dead battery.
Meter leads used in STC 215 would likely be damaged if used to jump start a car.
Jumper cables are designed to handle > 100 A.
Notes: Image by instructor

## Slide 25: Series Voltage Sources
Series Voltage Sources  Good idea.
Batteries with voltages > 4 V are usually strings of series connected cells.
Notes: Image by instructor

## Slide 26
The End

## Slide 27: Test Time – Just for Fun. No Points.

## Slide 28: Nodal and Mesh Analysis Quiz (1:4)
Which of the following is the best answer for a node in circuit analysis?
    1. The voltage is 0 V across a node.
    2. The voltage is the same across a node.
    3. The current is 0 A across a node.
    4. The current is the same across a node.
The voltage is the same across a node.
In circuit analysis, which of the following is the best definition of a mesh?
    1. A loop that does not contain any other loops within it.
    2. An equipotential surface.
    3. A loop with equal current.
    4. A loop that is a mess to solve.
A loop that does not contain any other loop within it. (Independent loop)

## Slide 29: Nodal and Mesh Analysis Quiz (2:4)
How many nodes are in the adjacent circuit?
    2.
    3.
    4.
    5.
5.
Which node would be the best reference node for nodal analysis?
v5, because it has the most elements connected to it.
How many unknown node voltages are in the above circuit?
    2.
    3.
    4.
    5.
2. v2 and v3
v1
v2
v3
v4
v5

## Slide 30: Nodal and Mesh Analysis Quiz (3:4)
Nodal analysis solves for which of the following?
    1. Voltages.
    2. Currents.
    3. Resistances.
    4. Power.
Nodal analysis solves for node voltages.
Nodal analysis uses which of the following of Kirchhoff’s laws?
    1. KVL.
    2. KCL.
KCL. Nodal analysis uses KCL to arrive at node voltages.

## Slide 31: Nodal and Mesh Analysis Quiz (4:4)
Mesh analysis solves for which of the following?
    1. Voltages.
    2. Currents.
    3. Resistances.
    4. Power.
Mesh analysis solves for mesh currents.
Mesh analysis uses which of the following of Kirchhoff’s laws?
    1. KVL.
    2. KCL.
KVL. Mesh analysis uses KVL to arrive at mesh currents.

## Slide 32
Extra

## Slide 33: Supernodes
Nodal analysis relies on Kirchhoff’s Current Law, i.e. KCL, to arrive at independent equations in order to solve for unknown node voltages.
An ideal voltage source provides the necessary current to maintain the desired voltage. Hence, the current provided by a voltage source is not known in advance.
Voltage sources not connected to the circuit reference node, actually simplify nodal analysis, since an ideal voltage source forces a known voltage difference between nodes.
A voltage source connected between two non-reference nodes forms what is referred to as a supernode, which is actually two nodes with a known voltage difference between them.
Kirchhoff’s Current Law, i.e. KCL, applies to closed boundaries, so can draw a boundary around a supernode and apply KCL to that boundary.
Supernodes actually simplify nodal analysis by reduce the number of necessary node equations.

## Slide 34: Supernode Example 1
Solve for the node voltages in the adjacent circuit.
Nodes v2 and v3 have a constant 2V between
them because of vs3, so treat them as a supernode,
using the equation v2 – v3 = 2V, v2 = 2V + v3.
Any elements connected in parallel with a
supernode, such as R3, are to be considered part
of the supernode.
Now only have to write one KCL equation at the
supernode. Also v1 = vs1 = 6V, and v4 = vs2 = 3V.
KCL at supernode: i1 + i5 = i2 + i4, .

## Slide 35: Supermeshes
Mesh analysis relies on Kirchhoff’s Voltage Law, i.e. KVL, to arrive at independent equations in order to solve for unknown mesh currents.
An ideal current source provides the necessary voltage to maintain the desired current. Hence, the voltage across a current source is not known in advance.
Current sources common between meshes, actually simplify mesh analysis, since an ideal current source forces a known branch current, reducing the number of unknown currents.
A current source common between meshes forms what is referred to as a supermesh, which is actually two or more meshes combined, each with a possibly different mesh current.
Kirchhoff’s Voltage Law, i.e. KVL, can be applied to a resulting supermesh in order to solve for unknown mesh currents.
Supermeshes actually simplify mesh analysis by reducing the number of necessary mesh equations.

## Slide 36: Supermesh Example 1
Solve for the mesh currents in the circuit below: Current source is1
results in a supermesh consisting of mesh currents i1 and i2. Because of
current source is1,we have a known relationship between i1 and i2. The
current source results in i1 - i2 = is1. i1 = 0.1 A + i2.
Supermesh is vs1 → R1 → R3 → R5.
Only other mesh is mesh for i3, i.e. R1 → R4 → R3.
Super Mesh: -vs1 + i1R1 – i3R1 + i2R3 – i3R3 + i2R5 = 0.
Also, i1 = 0.1 + i2. R1(0.1 + i2) +(R3 + R5)i2 - (R1 + R3)i3 = vs1.
(R1 + R3 + R5)i2 - (R1 + R3)i3 = vs1 – 0.1R1, 375i2 -175i3 = 16.5.
Mesh for i3: -i1R1 + i3R1 + i3R4 + i3R3 – i2R3 = 0,
-R1(0.1 + i2) – R3i2 + (R1 + R3 + R4)i3 = 0, –(R1 + R3)i2 + (R1 + R3 + R4)i3 = 0.1R1.
-175i2 + 505i3 = 7.5.
Matrix form: Ax = b, . x = A-1b.
i2 = 60.8 mA, i3 = 35.9 mA, ii = 0.1 + i2 = 161 mA.
i1
i2
i3

## Slide 37: Nodal and Mesh Analysis Summary
Node – A point of connection between two or more elements.
Nodal Analysis is based on KCL with unknowns being unknown node voltages.
Choosing a convenient reference node simplifies equations as all node voltages are then with respect to the reference node.
A voltage source connected between two non-reference nodes forms what is referred to as a supernode. Supernode contains more than one node.
Supernodes actually simplify nodal analysis by reduce the number of necessary node equations.
Mesh – A loop that does not contain any other loop within it. (Independent loop)
Mesh Analysis is based on KVL with unknowns being unknown mesh currents.
Convention assumes clockwise mesh currents.
A current source common between meshes forms what is referred to as a supermesh. A Supermesh contains inner loops.
Supermeshes actually simplify mesh analysis by reducing the number of necessary mesh equations.