## Slide 1: ECEN 150 Circuit Analysis I
Phasors and Impedance

## Slide 2
For AC steady-state at a given frequency, the
amplitude and phase angle difference between Vs
and Vc is a constant in the above circuit.
A complex number, referred to as a phasor,
is used to denote this constant peak amplitude
(magnitude) and phase angle difference between
Vs and Vc at the given frequency.
Phasors are not a function of time, since for
steady-state the constant peak amplitude (magnitude)
and phase angle difference between Vs and Vc is not a function of time.
Need Euler’s formula to arrive at a mathematical expression for phasors.
AC Steady-State and Phasors

## Slide 3
Series Expansion for eθ
  Imaginary Operator j:
    j2n = (-1)n, alternating between ±1. j2n+1 alternates between ∓j.

## Slide 4
Euler’s Formula
Complex exponentials and sinusoids are related.
Angle of cos(θ) + jsin(θ) = tan-1(tan(θ)) = θ. Therefore, the angle of cos(θ) + jsin(θ)= θ.

## Slide 5: Euler’s Formula and Signal Representation
.
Counter-Clockwise Rotating Vector for increasing .
Magnitude of () = 1 for all . Angle of () = .
Magnitude of () = r for all . Angle of () = .
Rotating Phasor Animation

## Slide 6: Phasor Signal Representation
Referred to as a phasor, i.e., phase vector.
Phasors are complex quantities that are not a function of time.
Phasors are used in ac steady-state analysis having a single common frequency.
↔
Where phasor .

## Slide 7: Phasor – (Phase Vector)
Phasor – amplitude and phase of a given
sinusoidal waveform.
Different spelling that Star Trek Phaser.
Phasors referred to as Sinors by some authors,
although the term sinor is considered outdated.
Phasor is a complex number representing
magnitude (amplitude) and phase of a cosine
waveform with respect to a reference cosine
waveform.
Can add, subtract, multiply and divide phasors
when they are all of the same frequency.
Assign an angle of zero to a reference cosine waveform, which is usually the AC power source of the circuit.
Ohm’s law applies for AC circuits with L’s and C’s if phasors are used to keep track of phase differences.
Real
Imaginary
Leading phase angle
Lagging phase angle corresponds to time delay.
Leading phase angle corresponds to time advance.
Lagging phase angle

## Slide 8: Phasor Relationships
Multiply by jω for differentiation.
Divide by jω for integration.
Phasors turn differential equations in the time domain into algebraic equations in the phasor domain.

## Slide 9: Phasor Examples
Ex. 1: Find the phasor representations of the following time function:
v(t) = 10cos(ωt + 15) V.
10cos(ωt + 15) V ↔ V = 105 V.
Ex. 2: Find the phasor representations of the following time function:
v(t) = 12sin(ωt) V.
12sin(ωt) V ↔ V = 12 V.

## Slide 10: Phasor Examples (Continued)
Ex. 3: Find the phasor representations of the following time function:
v(t) = v1(t) + v2(t), where v1(t) =10cos(ωt - 25) V and v2(t) = 4sin(ωt + 35) .
v1(t) = 10cos(ωt - 25
v2(t) = 4sin(ωt + 35) = 4cos(ωt - 55
= 11.35 - j7.51 V. (Quadrant IV).

## Slide 11: Sinusoid-Phasor Transformation
Time domain Representation | Phasor domain Representation
Time domain Representation | Phasor domain Representation
Trig Identities
Poll Questions

## Slide 12: Phasor Relationship for Resistors
For a resistor: . For
In terms of phasors,
Real
Imaginary
IR
VR
Voltage and Current are Always in-phase for pure resistance.

## Slide 13: Phasor Relationship for Inductors
Inductors oppose a change in current, i.e., current inertia.
For an inductor: In terms of phasors,
= 0 + j = j. So .
Multiplying by j results in +90˚ phase shift, meaning by 90˚.
Real
Imaginary
IL
VL
Inductor Voltage Always Leads Inductor Current
by 90˚.
-90˚

## Slide 14: Phasor Relationship for Capacitors
Capacitors oppose a change in voltage, i.e., voltage inertia.
For a capacitor: . In terms of phasors,
= 0 + j = j. So .
Multiplying by j results in +90˚ phase shift, meaning by 90˚.
Real
Imaginary
IC
VC
90˚
Capacitor Current Always Leads
Capacitor Voltage by 90˚.

## Slide 15: Time Derivatives and Phasors
Adjacent blue cosine wave changes most rapidly at zero crossings,
and has zero change at positive and negative peak values.
Resulting time derivative of the cosine wave leads the original
cosine wave by π/2 or 90˚, and also has larger peak magnitude by
the factor of 2πf.
Derivative of a sine wave leads the sine wave by π/2 or 90˚ also,
and also has larger peak magnitude by the factor of 2πf.
The associated amplitude of the time derivative of a sinusoid
increases with increasing frequency.
Capacitor current leads capacitor voltage in adjacent circuit
Inductor voltage leads inductor current in adjacent circuit
because . .

## Slide 16: Phasors (Continued)
For pure resistive circuits, the current and
voltage are in phase, and v(t)/i(t) = R.
Adjacent graph shows the ratio of v(t)/i(t)
for v(t) and i(t) that are 30˚ out of phase.
The instantaneous resistance, i.e., R(t) = v(t)/i(t), for the
out-of-phase waveforms varies from -∞ to +∞, which isn’t
very useful.
Need another way besides R(t) = v(t)/i(t) to
characterize opposition to current flow for
circuit with inductors and capacitors.
Inductor and capacitor opposition to current flow is also frequency dependent.
Impedance Z is the term used to describe the frequency dependent opposition to current flow relationships for circuits with capacitors and/or inductors.
For a pure resistance, ZR = R.

## Slide 17: Impedance  Ratio of Phasors
For an inductor: . In terms of phasors,
Define inductor impedance ZL as phasor voltage divided by phasor current.
For a capacitor: . In terms of phasors,
Define capacitor impedance ZC as phasor voltage divided by phasor current.
Impedance Z is a complex number, but Z is not a phasor because it does not describe a time varying quantity as do phasors, i.e., it is not multiplied by ejωt.

## Slide 18: Reactance – Magnitude of Impedance
Capacitors look like an open at DC, and a short
at high-frequency AC.
Inductors look like a short at DC, and an open
at high-frequency AC.

## Slide 19: Impedance for Series RC and RL Circuits
Z of a purely resistive AC circuit equals .
Z of an ideal capacitor equals:
Z of an ideal inductor equals:
Z is a complex number consisting of resistive (real) and reactive (imaginary) components for series RC and RL circuits.
. (Quadrant IV). Series RL →
Real
θ
Imaginary
R
XC
Real
θ
Imaginary
R
XL
Poll Questions

## Slide 20: Phasor RC Example 1
A series-connected RC circuit with R = 1.2 kΩ and
C = 0.47 µF is connected to a 5 V peak, sinusoidal
200 Hz source. Determine the overall impedance,
i.e., Zeq, along with the phasor circuit current I, the
phasor resistor voltage VR, and the phasor capacitor
voltage VC.
XC = 1/(2πfC) = 1/[2π(200 Hz)(0.47 µF)] = 1.69 kΩ. XC = 1.69 kΩ.
= 0 - j.
R – jXC = 1.2 kΩ - j.
. .
.
Zeq (Continued on next slide).

## Slide 21: Phasor RC Example 1 (Continued)
From previous slide.
.
mA.
V. V.
V.
Real
Imaginary
VS
90˚
VC
VR
Capacitor Current Always Leads Capacitor Voltage by 90˚. Therefore, VR leads VC by 90˚.
KVL and KCL also apply at each instant of time.

## Slide 22: Phasor RL Example 1
A series-connected RL circuit with R = 1.5 kΩ and
L = 680 mH is connected to a 5 V peak, sinusoidal
10 kHz source. Determine the overall impedance,
i.e., Zeq, along with the phasor circuit current I, the
phasor resistor voltage VR, and the phasor inductor
voltage VL.
XL = 2πfL = 2π(10 kHz)(68 mH) = 4.27 kΩ. XL = 4.27 kΩ.
= 0 + j.
R + jXL = 1.5 kΩ + j.
. .
.
Zeq (Continued on next slide).

## Slide 23: Phasor RL Example 1 (Continued)
From previous slide.
.
V. .
.
Real
Imaginary
VS
90˚
VL
VR
Inductor Voltage Always Leads Inductor Current by 90˚. Therefore, VL leads VR by 90˚.
KVL and KCL also apply at each instant of time.

## Slide 24: Phasor Signal Representation
Referred to as a phasor, i.e., phase vector.
Phasors are complex quantities that are not a function of time.
Phasors are used in ac steady-state analysis having a single common frequency.
↔
Where phasor .

## Slide 25: Time Derivatives and Phasors
Adjacent blue cosine wave changes most rapidly at zero crossings,
and has zero change at positive and negative peak values.
Resulting time derivative of the cosine wave leads the original
cosine wave by π/2 or 90˚, and also has larger peak magnitude by
the factor of 2πf.
Derivative of a sine wave leads the sine wave by π/2 or 90˚ also,
and also has larger peak magnitude by the factor of 2πf.
The associated amplitude of the time derivative of a sinusoid
increases with increasing frequency.
Capacitor current leads capacitor voltage in adjacent circuit
Inductor voltage leads inductor current in adjacent circuit
because . .

## Slide 26: Impedance for Series RC and RL Circuits
Z of a purely resistive AC circuit equals .
Z of an ideal capacitor equals:
Z of an ideal inductor equals:
Z is a complex number consisting of resistive (real) and reactive (imaginary) components for series RC and RL circuits.
. (Quadrant IV). Series RL →
Real
θ
Imaginary
R
XC
Real
θ
Imaginary
R
XL

## Slide 27: Impedance and Admittance
Impedance Z is a complex number with units of Ohms (Ω).
Impedance consists of resistance R (real) and reactance X ( imaginary) components.
Admittance Y is a complex number with unit of Siemens (S).
Admittance consists of conductance G (real) and susceptance B ( imaginary) components.
Admittance Y is the reciprocal of impedance Z. Y = 1/Z Siemens.
Conductance G is the reciprocal of resistance R. G = 1/R Siemens.
Susceptance B is the reciprocal of reactance X. B = 1/X Siemens.

## Slide 28: Impedance and Admittance (Continued)
Series impedances combine like series resistors: Zeq_series = Z1 + Z2 + …. Zn.
Series admittances combine like parallel resistors: Yeq_series =
Parallel impedances combine like parallel resistors: Zeq_parallel =
Parallel admittances combine like series resistors: Yeq_parallel = Y1 + Y2 + …. Yn
Why use admittances rather than impedances?
For parallel circuits the complex math is simpler using admittance rather than impedance. The equivalent admittance can then be inverted at the end to then arrive at equivalent impedance.

## Slide 29
Determine the equivalent admittance of the adjacent circuit,
at a frequency of 10 kHz.
Admittance Example 1

## Slide 30
Determine the equivalent impedance of the
adjacent parallel RLC circuit at f = 100 Hz.
Admittance Example 2

## Slide 31: Phasors and Impedance Review Quiz 1 of 6
Phasors vary with time.
  1. True.
  2. False.
2. False. Phasors corresponds to the amplitude and phase of a time varying sinusoids. So while the sinusoid varies with time, its amplitude and phase does not.
Phasor voltages and currents are not a function of frequency.
1. True.
2. False.
2. False. Phasor voltages and currents are a function of frequency. Consequently, numeric results from phasor analysis are only valid for a single frequency sinusoid.

## Slide 32: Phasors and Impedance Review Quiz 2 of 6
equals which of the following?
1. 0.
    2. .
3. .
4. 1.
  2. .
, equals which of the following for all values of ?
1. 0.0.
2. 0.5.
3. 0.71.
4. 1.0.
  1. 1.

## Slide 33: Phasors and Impedance Review Quiz 3 of 6
Choose the best answer below regarding impedance.
1. Impedance is the ratio of phasor voltage to phasor current.
2. The magnitude of impedance represents the opposition to current flow in a circuit for sinusoidal excitation.
3. Impedance is a complex number, but is not a phasor.
4. All of the above
  4. All of the above
The magnitude of the impedance of an inductor approaches which of the following for frequency  ∞?
1. 0.
2. 1/2πf.
3. 90˚.
4. ∞.
  4. ∞ XL = 2πfL.

## Slide 34: Phasors and Impedance Review Quiz 4 of 6
Choose the best answer below regarding admittance.
1. Admittance is the ratio of phasor voltage to phasor current.
2. The magnitude of admittance represent the opposition to current flow in a circuit for sinusoidal excitation.
3. Admittance is the reciprocal of impedance.
4. All of the above
  3. Admittance is the reciprocal of impedance and has units of siemens (S).
The magnitude of the impedance of a capacitor approaches which of the following for frequency  ∞?
1. 0.
2. 1/2πf.
3. 90˚.
4. ∞.
  1. 0 XC = 1/(2πfC).

## Slide 35: Phasors and Impedance Review Quiz 5 of 6
Choose the best answer below regarding capacitor impedance.
1.
2.
3. .
4. .
  1.
Choose the best answer below regarding inductor impedance.
1.
2.
3. .
4. .
  3.

## Slide 36: Phasors and Impedance Review Quiz 6 of 6
Choose the best answer below regarding capacitor admittance.
1.
2.
3. .
4. .
Choose the best answer below regarding why impedance, rather than just resistance, is employed for circuits involving inductors and capacitors.
1. Voltage and current can be out of phase, resulting in instantaneous
    resistance values ranging between ± ∞
    2. The opposition to current flow, i.e. reactance, of inductors and capacitors is a function of frequency.
3. Ohm’s law, KVL and KCL apply to ac steady state circuits when using phasors and impedance.
4. All of the above.
  4. All of the above

## Slide 37: Extra