## Slide 1: ECEN 350 Electronic Devices and Circuits
Bipolar Junction Transistors

## Slide 2
ECEN 350 – Topics
Semiconductor Physics
Diodes
BJTs
Rectifiers
MOSFETs
CMOS
Zeners
LEDs
Transistor Biasing
Small-Signal Analysis
Amplifier Gain Stages
Frequency Response
IC Op-Amps

## Slide 3: Transistor – Electronic Valve
A Transistor is an electronic valve controlling the flow of current.
We cover two different types of transistors in ECEN 350: 1. Bipolar Junction Transistors. 2. MOSFETs.
Bipolar Junction Transistors (BJTs) have three terminals:
  Base.
  Emitter.
  Collector.

## Slide 4: pn Junction Diode – Reverse Bias
With reverse bias, more work is required to move conduction
band electrons from the n-side to the p-side.
Reverse bias widens the depletion region and increases the
barrier potential between the n and p-side of the junction.
For a reverse biased pn junction, the depletion region inhibits
majority carriers from crossing the junction, while aiding minority
carriers to cross the junction.
A relatively small conventional current, referred to as reverse
saturation current Is, flows in a reversed biased pn junction diode.
Is consists mostly of minority carriers in the vicinity of the depletion
region crossing the junction. Saturation refers to the fact that Is
reaches a maximum value under reverse bias, only slightly increasing with increasing reverse voltage.
For a typical silicon pn junction diode at 25˚C , Is << 1 µA.

## Slide 5: pnp Diode Equivalent Circuit
For matched silicon pn junction diodes we expect IS2 to be much less than ID1.
How can we make IS2 larger than the typically negligible reverse saturation current?
Diode D1 is injecting holes, i.e., minority carriers, into n-type cathode region of D2. Remember that for a reverse biased pn junction, the depletion region inhibits majority carriers from crossing the junction, while aiding minority carriers to cross the junction.
By narrowing the width of the n-type region we inject minority carriers in the vicinity of the reverse biased pn junction of diode D2, which will increase IS. Also, utilizing a lightly doped n-type region widens the D2 depletion region extension into the n-type base region, further increasing IS.
The bias conditions shown with D1 forward biased and D2 reverse biased is referred to as the Active Region of operation.

## Slide 6: pnp Diode Equivalent Circuit (Continued)
Bipolar junction transistors utilize a very narrow and lightly doped base region in order to increase IS2, referred to as collector current IC. This works surprisingly well as IC >> IB for the standard bipolar junction transistors operating in the active region. Almost all of the holes from D1 injected into D2 cross the reversed D2 junction and end up as collector current, rather than base current.
The result of this non-intuitive approach is an electronic device in which the collector current IC is controlled by a much smaller base current IB, providing the desired goal of an electronically controlled current flow.
If the Base-Emitter diode, diode D1 in the above pictorial, is not forward biased, then the bipolar junction transistor simply behaves as an open switch between emitter and collector, which is also a useful function.
The p++ emitter region simply indicates heavy doping with respect to the other regions.

## Slide 7: pnp Bipolar Junction Transistor
p++ emitter region in above diagram indicated heavy doping with respect to the other regions
Bipolar meaning two pn junctions. Want the Base-Emitter junction in the above transistor forward biased to turn on transistor, else it behaves like an open switch between the emitter and collector.
Actual width of narrow base is < 1 % of overall transistor width.
pnp Schematic Symbol
pnp Diode Equivalent Circuit

## Slide 8: pnp Active Region Operation
For active region want Base-Emitter
junction forward biased with Collector-Base junction reverse biased.
Forward biased Base-Emitter junction results in a large number of holes injected into in the n-type base. Because of the Emitter and Base doping disparity, these holes can actually outnumber the conduction band (CB) electrons, yet since they are holes in an n-type region, they are still considered minority carriers.
pn junctions inhibit majority carriers from crossing, while aiding the crossing of minority carriers.
Almost all holes injected from Emitter to Base end up in the Collector.
pnp Energy Band Diagram in Active Region

## Slide 9: pnp Active Region Operation (Continued)
p++ simply denotes heavily doped p-type.
A few holes recombine with conduction band electrons in the narrow, lightly doped Base region, but most injected holes in the Base make it to the Collector.
For BJT active region operation, i.e. the Base-Emitter junction forward biased and Collector-Base junction reverse biased, most Emitter current ends up in the Collector due to narrow, lightly doped Base region.
Result by KCL is that IE = IB + IC, with IB << IC.
Ratio α IC/IE ≈ 1. Practical α values range from 0.9 to 0.998.
pnp Energy Band Diagram in Active Region

## Slide 10: npn Bipolar Junction Transistor
n++ emitter region in above diagram indicated heavy doping with respect to the other regions
Bipolar meaning two pn junctions. Want Base-Emitter junction in the above transistor forward biased to turn on transistor, else it behaves like an open switch between the collector and emitter.
Actual width of narrow base is < 1 % of overall transistor width.
npn Schematic Symbol
npn Diode Equivalent Circuit

## Slide 11: npn Active Region Operation
Use electron versus conventional current flow for above npn pictorial.
For active region want Base-Emitter junction forward biased with Collector-Base junction reverse biased.
Forward biased Base-Emitter junction results in a large number of CB electrons injected into in the p-type base. Because of the Emitter and Base doping disparity, these CB electrons can actually outnumber the valence band holes, yet since they are CB electrons in a p-type region, they are still considered minority carriers.
Almost all conduction band electrons injected from Emitter to the Base end up in the Collector.
npn Energy Band Diagram in Active Region

## Slide 12: npn Active Region Current Flow (Continued)
n++ simply denotes heavily doped n-type.
A few conduction band electrons recombine with holes in the narrow, lightly doped Base region, but most injected conduction band electrons in the Base make it to the Collector.
Result by KCL is that IE = IB + IC, with IB << IC.
Ratio β IC/IB >> 1. β describes the current gain of a bipolar transistor.
Practical BJT β values range from 50 to 400.
npn Energy Band Diagram in Active Region

## Slide 13: npn Active Region Current Flow (Continued)
Why do most injected conduction band electrons in the p-type Base region cross the reversed biased pn junction and end up in the Collector?
Because there is relatively little recombination in the lightly doped Base region, so the overwhelming number of “minority carrier” fall down the energy hill to the Collector.
Remember that for reverse biased pn junctions, the depletion region inhibits majority carriers from crossing the junction, while aiding minority carriers to cross the junction.
Conduction band electrons injected into the p-type Base are still considered minority carrier, even though they may outnumber the number of valence band holes (Majority Carriers) in the Base region.
npn Energy Band Diagram in Active Region

## Slide 14: npn Common-Emitter (CE) I-V Characteristics
Emitter is connected to ground or the common voltage, i.e.,
common emitter, (CE) configuration.
Base current IB versus Base-Emitter voltage VBE has a pn
junction diode characteristic.
Collector current IC is much larger than Base current IB,
because the overwhelming number of minority carriers
injected into the base region end up in the Collector.
Red trace in the above graph is the IC/IB ratio, i.e.,
the current gain β of the transistor, with axis on the far right.

## Slide 15: npn Common-Emitter (CE) I-V Characteristics (Continued)
Collector current IC versus increasing Collector-Emitter
voltage VCE has the adjacent characteristic, where each trace
represents a different base current IB.
Zero base current IB means that the Base-Emitter junction is not forward biased resulting in the transistor appearing as an open switch between the Collector and Emitter. This region of operation is referred to as cutoff.
The region of operation with near vertically increasing IC is referred to a saturation, and corresponds to small VCE voltages.
While transistor characteristic curves are shown as discrete traces, operating at any point between traces is a possible with appropriate bias conditions.

## Slide 16: npn Common-Emitter (CE) I-V Characteristics Summary
In the active region the Base current IB is fairly
independent of Collector-to-Emitter voltage as shown
in adjacent graph.
Hence, since IC = βIB, in the active region, Collector current is
also fairly independent of Collector-to-Emitter voltage.
Collector current versus Collector-to-Emitter voltage
for several different Base current values results in
the family of IC versus VCE curves shown below.
Three regions of operation, i.e. cutoff,
active and saturation, are illustrated in
the adjacent family of curves.
Saturation occurs when the Base-
Emitter junction is forward biased and the
Base-Collector junction becomes slightly
forward biased at VBC ≥ 0.4 V, corresponding
to VCE ≤ 0.3 V, for VBE = 0.7 V.

## Slide 17: pnp Common-Emitter (CE) I-V Characteristics
Emitter is connected to the positive dc supply
voltage, which is considered an ac ground for
ac amplifiers, i.e. common emitter (CE) configuration.
Base current IB versus Emitter-Base voltage VEB has a
pn junction diode characteristic.
Collector current magnitude |IC| is much larger than Base
current magnitude, because the overwhelming number of
minority carriers injected into the base region end up in the
Collector.
Red trace in the above graph is the IC/IB ratio, i.e. the current gain β of the transistor, with axis on the far right.
By convention, SPICE denotes conventional currents as negative when they flow out of a terminal. Hence, the Base current IB is a negative quantity in the plot because conventional IB flows out of the Base terminal .

## Slide 18: pnp Common-Emitter (CE) I-V Characteristics (Continued)
Collector current IC versus increasing Emitter-Collector
voltage VEC has the adjacent characteristic, where each trace
represents a different base current IB.
Zero base current IB means that the Emitter-Base junction is not forward biased resulting in the transistor appearing as an open switch between the Emitter and Collector. This region of operation is referred to as cutoff.
The region of operation before the leveling off of IC after the “knee” is referred to a saturation, and corresponds to small VEC voltages.
By convention, SPICE denotes conventional currents as negative when they flow out of a terminal. Hence, the Collector current IC is a negative quantity in the above family of curves because IC flows out of the Collector terminal to ground.

## Slide 19: Bipolar Junction Transistor Symbols
Arrowhead defines the direction of conventional current flow at the emitter terminal.
Need VBE ≈ 0.7 V for an npn and ≈ -0.7 V for a pnp, in order to forward bias the Base-Emitter junction, else the transistors are operating in the cutoff region.
For active region operation need Base-Emitter junctions forward biased and Collector-Base junctions reverse biased.
For Saturation need Base-Emitter junctions forward biased, with VCE ≤ 0.3 V for an npn with VEC ≤ 0.3 V for a pnp, i.e., slightly forward biased Collector-Base Junctions.

## Slide 20: BJT Active and Saturation Regions
The collector current in BJT active region is almost entirely determined by the transistor base current, with VCE having only a slight effect..
BJTs act like a current controlled current source in the active (Linear) region, i.e., IC = βIB.
The load lines below illustrate that
collector current is almost entirely
independent of VCE in the active region.
This results in IC = βIB, which is a
linear equation, resulting in the active
region also referred to as the linear
region of operation.
Since usually β > 50, a small change
in IB results in a much larger change in
IC, which can be utilized to produce
a large voltage gain in an amplifier
circuit.
BJT Saturation Region can
be approximated as a vertical
IC Line at VCE ≤ 0.3 V.
BJT Active or Linear Region can
be approximated as a horizontal
IC Line, acting as a Current Source.
Load Lines
Active
Region

## Slide 21: BJT Active and Saturation Regions (Continued)
The collector current in BJT saturation
is mostly determined by external
circuitry, as illustrated by load lines.
Our author refers to the maximum
load-line current as the saturation
current.
The maximum load-line current is
determined by external circuitry, and
not the transistor.
Hence, in the BJT Saturation Region,
the collector current approximately
equals the maximum load-line current.
We will refer to this as circuit
saturation, to be distinguished from
a region of operation of MOSFETs
termed saturation, which is a transistor
saturation of the current.
BJT Saturation Region can
be approximated as a vertical
IC Line at VCE ≤ 0.3 V.
BJT Active or Linear Region can
be approximated as a horizontal
IC Line, acting as a Current Source.
Active
Region
Load Lines

## Slide 22: BJT Saturation
Both junctions becoming forward biased, i.e. saturation, resulting in an increase in base current and decrease in β.
In the BJT Saturation Region,
the collector current approximately
equals the maximum load-line current,
i.e. circuit saturation.
β decreases in saturation compared
with active region value, with βmin = 10
being a conservative estimate, sometimes
referred to as hard saturation.
Operating a BJT in saturation is
common for digital applications and
undesirable for analog applications.
BJT Saturation Region can
be approximated as a vertical
IC Line at VCE ≤ 0.3 V.
npn Schematic Symbol
npn diode Equivalent Circuit
Active
Region
Load Lines
BJT Active or Linear Region can
be approximated as a horizontal
IC Line, acting as a Current Source.

## Slide 23: BJT Operating Regions
Cutoff Region
Base-Emitter junction not forward biased. Negligible Collector current flows.
Transistor behaves like an open switch between Collector and Emitter.
Active Region
Base-Emitter junction forward biased, Collector-Base junction reverse biased.
Transistor approximately behaves like a dependent current source with , i.e., IC
is linearly dependent upon IB. Useful operating region for transistor amplifiers.
Saturation Region
Saturation occurs when the Base-Emitter junction is forward biased, i.e., VBE ≈ 0.7 V for an npn and ≈ -0.7 V for a pnp, while the Collector-Base junction also becomes slightly forward biased. Both junctions becoming forward biased, i.e., saturation, implies that VCE ≤ 0.3 V for an npn and VEC ≤ 0.3 V for a pnp, which is sometimes approximated as a closed switch for hand calculations.
1st Approximation in saturation is a closed switch between Collector and Emitter.
IC_Sat is approximated as maximum load-line current.
Poll Questions.

## Slide 24: Common-Emitter (CE) Configuration
Common-emitter (CE) configuration refers to the emitter terminal being connected to the ground or common
terminal of the power supplies. The adjacent circuit is connected to a dc
ground, although CE configuration also results from emitter connected to
an ac ground for ac amplifiers, as will be discussed at a future time.
Subscript Notation:
Single subscripts are used for node voltages, i.e., VB, VC and VE.
Double subscripts are used to represent either sources of power,
such as VCC or VBB, and also the voltage between two different nodes
such as VCE = VC – VE.
Output voltage Vout also equals collector node voltage VC = VCE in the
adjacent schematic.
In the above circuit, 2nd approximation implies that Q1 is operating in cutoff
if VBE < 0.7 V.
Q1 is operating in the active region for VBE ≥ 0.7 V and VCE > 0.3 V.
Q1 is operating in the saturation region for VBE ≥ 0.7 V and VCE ≤ 0.3 V.

## Slide 25: β – BJT Current Gain
β represents the current gain of a bipolar
junction transistor (BJT).
BJTs are said to have both a dc and ac BJT β.
In bipolar transistor data sheets β is often
referred to as hfe for historical reasons.
Often , so in some contexts we will simply use β for BJT current gain, rather than distinguishing between whether it is dc or ac current gain.

## Slide 26: Transistor Approximations
Active or linear region is useful for analog applications
including amplifiers.
First approximation in the active region.
BJTs are considered current controlled devices.
The diamond symbol for dependent
sources is not universal, as the Malvino
text and LTspice don’t use that symbol.
So when referring to the Malvino text note
that the inclusion of the βdcIB control
equation along side the circle symbol for
an independent current source indicates
a dependent source, that depends upon IB.

## Slide 27: 2N3904 npn BJT Data Sheet

## Slide 28: 2N3904 npn BJT Data Sheet (Continued)

## Slide 29: 2N3904 npn BJT Data Sheet (Continued)

## Slide 30: 2N3904 npn BJT Data Sheet (Continued)

## Slide 31: 2N3904 npn BJT Data Sheet (Continued)

## Slide 32: 2N3906 pnp BJT Data Sheet

## Slide 33: 2N3906 pnp BJT Data Sheet (Continued)

## Slide 34: 2N3906 pnp BJT Data Sheet (Continued)

## Slide 35: 2N3906 pnp BJT Data Sheet (Continued)

## Slide 36: npn Common-Emitter (CE) Stage
Output is 5.0 V for transistor off, and within 0.3 V of ground for relatively low (< 20 mA) collector current.
Cutoff
Active
Saturation

## Slide 37: npn Common-Emitter (CE) Stage (Continued)
Notice that in circuit saturation that increasing base current does not dramatically increase the collector current, i.e., the collector current approaches a saturation value.
Cutoff
Active
Saturation

## Slide 38: pnp Common-Emitter (CE) Stage
Emitter is connected to the positive dc supply
voltage, which is considered an ac ground for
ac amplifiers, i.e., common emitter (CE) configuration.
Output is 0.0 V for transistor off, and within 0.3 V of 5.0 V for relatively low (< 20 mA) magnitude collector current.
Active
Saturation
Cutoff

## Slide 39: pnp Common-Emitter (CE) Stage (Continued)
Notice that in circuit saturation that increasing the magnitude of the base current does not dramatically increase the magnitude of the collector current, i.e., the collector current magnitude approaches a saturation value.
Cutoff
Active
Saturation

## Slide 40: Load Line for Common-Emitter (CE) Configuration
For hand calculations, the load line provides helpful approximations
for determining the saturation and cutoff points of a given circuit.
Look at end-point extremes for IC_Sat and VCE_Cutoff:
For Vout = VCE = 0 V, IC_Max, i.e. IC_Sat = VCC/RC = (10 V)/(400 Ω) = 25 mA.
For IC = 0 A, VCE = VCC = 10 V.
Superimpose the resulting load line over the
transistor characteristics.
The actual transistor operating point must lie on
the load line.
While discrete IC versus VCE lines are shown, IC
can take on any value between the discrete lines,
given the appropriate IB value.
Saturation
Point
Cutoff
Point

## Slide 41: npn Common-Emitter (CE) LED Driver
Design an npn common-emitter LED driver with base bias such as shown in the
adjacent 5 V powered circuit.
Based on lab measurements, a red LED takes ≈ 3 mA at 1.7 V for good brightness.
Want IC_Sat ≥ 3 mA. Choose
Choose
The above calculation assumed negligible VCE, implying saturation region.
From 2N3904 characteristics, βmin = 70 for 1 mA in active region, yet β is reduced in
saturation. So assume βmin = 10 for 3.3 mA in hard saturation, which is conservative
but provides a robust design.
So need IB ≥ (3.3 mA)/10 ≥ 330 µA. . Vi = 5 V max.
13.0 kΩ. Choose
For R1 = 13 kΩ and R2 = 1 kΩ, a 2N3904 npn transistor should be able to turn on a Red LED, like the one characterized in the Zener Diodes and LED lab, when powered by a 5 V supply.
You need to do similar calculations for the upcoming homework.
Poll Questions

## Slide 42: Ideal Voltage Follower
What is Vout and why in the adjacent circuit?
Vp = Vin. Vout = Vm.
Also, Vp = Vm. Therefore Vout = Vin.
Why does Vp = Vm?
Because of large open-loop voltage gain and negative feedback, Vout is always adjusts Vm towards Vp.
The only time that Vout is not adjusting Vm towards Vp, is when Vm = Vp, which implies
Vout = Vin. Hence, Vout follows Vin.
If Vout became < Vin, then Vp > Vm, resulting in Vout increasing until Vm again equals Vp.
If Vout became > Vin, then Vp < Vm, resulting in Vout decreasing until Vm again equals Vp.
Since Vout = Vin, the resulting voltage gain with feedback, i.e. closed-loop gain = 1 because of negative feedback, whereas open-loop gain >> 1.

## Slide 43: Buffered Op-Amp Using BJT Emitter Follower
For the adjacent circuit, what is Vout?
Because op-amp output adjusts the base-to-emitter
voltage of the BJT until the BJT collector current Ic multiplied
by Rload = Vin, i.e., the output voltage is regulated over a wide
range of load resistance values, termed a Voltage Regulator.
Voltage Regulators may need to provide more than 1 A of
output current.
BJT source-follower in above circuit increases output current well beyond the 10 to 20 mA possible from the op-amp output. The npn transistor boosts the current well beyond what the op-amp can provide.
One weakness of the above circuit occurs if/when the output is inadvertently shorted to ground, which is easy to do.
If VCC is a stiff voltage supply and Vout is inadvertently shorted to ground, then transistor Q1 will likely overheat and be destroyed.
Practical voltage regulators provide some method of limiting the output current so as to protect the output transistor.

## Slide 44: Output Protection for Stiff Voltage Sources
The adjacent practical voltage source can be
modeled as a Thevenin equivalent circuit.
Stiff Voltage Source: Rs < 0.01Rload.
Large and damaging currents can flow from
inadvertently shorted stiff voltage source without some type of current limiting.
For example, a healthy 12 V lead-acid battery can provide over 400 A for
several seconds, as needed to start cars. Inadvertently shorting across the
terminals of a 12 V lead-acid battery, i.e. a load fault, will damage or destroy
diodes and switching transistors, along with PCB traces.
A circuit that is easily destroyed by a simple load fault is not a good, robust design.
One-time blowable fuses protect the wiring and circuitry, and are commonly
employed in automobiles. Yet replacing fuses is considered too cumbersome
for many electronic applications, and so instead recoverable current limit
circuitry is often employed to protect wiring and circuitry.
A good, robust design can withstand common user errors and load faults.

## Slide 45: VBE Current Limit Circuit
The adjacent circuit is a 5 V voltage regulator, i.e.,
stiff 5 V voltage source, with VBE current limit.
Under normal load conditions, Vout = 5 V, with Q1 operating in
cutoff, having no effect on Vout.
Yet when (Iload)(Rcl) exceeds approximately 0.6 V, Q1 begins
turning on and diverts base current from transistor Q2, which
then limits the Q2 emitter current to approximately (0.66 V)/Rcl.
The 2nd approximation of VBE = 0.7 V for transistor turn on
results in a calculated current limit that is too large by more
than 10%, so we will be using VBE = 0.66 V for current limit
calculations for both npn and pnp VBE current limit circuits.
For example with Rcl = 4.3 Ω, Ilim ≈ (0.66 V)/(4.3 Ω) = 154 mA.
Whereas, maximum load current for the above circuit is
simulated at approximately 142 mA (-8% from calculated Ilim).
Output Transistor

## Slide 46: VBE Current Limit Circuit (Continued)
When in regulation the output of op-amp U1 controls the base current
of Q2 so as to maintain an output voltage of 5.0 V, over a wide range of
load currents.
The parts cost for the adjacent VBE current limit circuitry
is less than 10 cents in production quantities.
What is the output voltage Vout, when the current limit is activated?
Vout = (Ilim)Rlimit, which is less than the desired 5 V. We say that
the voltage regulator has come out of regulation when operating
in current limit, with the output voltage becoming a function of
load current.
Another point of view is that the voltage regulator, which is a
voltage source, turns into a current regulator, or current source,
upon entering current limit.
A current limit is much more convenient than a 1-time
blowable fuse for circuit protection.

## Slide 47: Transistor Approximations
Active or linear region is useful for analog applications
including amplifiers.
First approximation in the active region.
BJTs are considered current controlled devices.
The diamond symbol for dependent
sources is not universal, as the Malvino
text and LTspice don’t use that symbol.
So when referring to the Malvino text note
that the inclusion of the βdcIB control
equation along side the circle symbol for
an independent current source indicates
a dependent source, that depends upon IB.

## Slide 48: BJT Circuit Debug/Testing
With a DMM, verify that VBE is approximately |0.7 V| for active region operation.
Use portable DMM β (hfe) test socket.
May have to put pressure on BJT package for good
reading.

## Slide 49
ECEN 350 – Topics
Semiconductor Physics
Diodes
BJTs
Rectifiers
MOSFETs
CMOS
Zeners
LEDs
Transistor Biasing
Small-Signal Analysis
Amplifier Gain Stages
Frequency Response
IC Op-Amps

## Slide 50: The End

## Slide 51: Extra

## Slide 52: BJT Transistor Relationships
BJT analysis approach is to first find IB, the solve for IC, and IE.

## Slide 53: Test Time – Just for Fun. No Points.

## Slide 54: BJT Test
What is largest current in a bipolar transistor operating in the active region?
  1. Emitter Current.
  2. Base Current.
  3. Collector Current.
  Answer: 1. Emitter Current since IE = IC + IB.

## Slide 55: BJT Test (Continued)
The arrow in the transistor symbol defines the direction of conventional current flow for which of the following terminals?
  1. Emitter.
  2. Base.
  3. Collector.
  Answer: 1. Emitter, which then also defines the direction for base and collector currents since IE = IC + IB.

## Slide 56: BJT Test (Continued)
Choose the best answer for reasonable dc values for a bipolar junction transistor operating in the active region.
  1. 0.7.
  2. 0.96.
  3. 1.1.
  4. ≥ 10.
  Answer: 2. ≈ 1, but < 1.1.

## Slide 57: BJT Test (Continued)
In the active region of a bipolar transistor what are the bias conditions
for the Base-Emitter and Collector-Base junctions?
  1. Forward, Forward.
  2. Forward, Reverse.
  3. Reverse, Forward.
  4. Reverse, Reverse.
  Answer: 2. Base-Emitter forward biased and Collector-Base junction
  reverse biased for active region.

## Slide 58: BJT Test (Continued)
As a 2nd approximation for hand calculations, the base-to-emitter voltage of a bipolar junction transistors operating in the saturation or active regions can be assumed to be what voltage?
  1. 0.0 V.
  2. 0.3 V.
  3. 0.7 V.
  4. Not enough information.
  Answer: 3. 0.7 V.

## Slide 59: BJT Test (Continued)
Is the following transistor symbol for an npn or pnp transistor?
  1. npn.
  2. pnp.
  Answer: 2. pnp transistor since arrow is pointing in, whereas
  the arrow in an npn transistor is not pointing in.

## Slide 60: BJT Test (Continued)
What is smallest current in a bipolar transistor operating in the active region?
  1. Emitter Current.
  2. Base Current.
  3. Collector Current.
  Answer: 2. Base Current since IE ≈ IC and IB << IC.

## Slide 61: BJT Test (Continued)
Choose the best answer for reasonable βdc values for a bipolar junction transistor operating in the active region.
  1. 0.7.
  2. 0.9 to 1.0.
  3. 50 to 400.
  4. > 1000.
  Answer: 3.

## Slide 62: Buffer Stage Example (Continued)
DMM Measurement Details Lab provided a circuit with a large Thevenin Output impedance/resistance.
The portable DMM’s having 10 MΩ input
impedance/resistance is not high enough for a good
voltage measurement in this particular case.
Need a buffer stage. The VirtualBench High (10 GΩ) Input Impedance setting provided a measured result of approximately 10 V, accomplished by incorporating an internal buffer amplifier having very high input impedance (10 GΩ) so as to not load down the above Thevening Equivalent Circuit. A good buffer also has low output resistance/impedance so that reasonable resistive load does not affect the output voltage.

## Slide 63: Common-Emitter Configuration (Continued)
How can this circuit achieve voltage gain?
Small change in Ib results in β times larger change in Ic in active region.
Vo = Vcc – ICRc.
Output voltage Vo decreases for an increase in input voltage Vi.
Hence, common-emitter is an inverting stage.

## Slide 64: Common-Collector (Emitter-Follower) Configuration
Only the collector voltage is fixed in this configuration, and so referred to as Common-
Collector, even though collector is not necessarily
common between input and output.
Also referred to as emitter-follower since the
emitter terminal follows within approximately
0.7 V of the base terminal.
Large current gain possible although the
maximum voltage gain equals 1.
Emitter follower is a useful buffer stage.
A buffer stage interfaces between a voltage source with a relatively large Thevenin output resistance/impedance and a load requiring a small Thevenin output resistance/impedance.
A good buffer stage requires negligible input current while providing significant output current at the desired output voltage.
Output voltage Vo increases for increasing input voltage Vi.

## Slide 65: Buffer Stage Example
DMM Measurement Details Lab provided a circuit with a large Thevenin Output impedance/resistance.
The portable DMM’s having 10 MΩ input
impedance/resistance is not high enough for a good
voltage measurement in this particular case.
Need a buffer stage. An Emitter-Follower stage would help, although
there is still non-negligible base current along with approximately 0.7 V
drop from base-to-emitter.

## Slide 66: Common-Base Transistor Configuration
Both input and output terminals share the Base terminal, i.e. Common-Base.
Can achieve voltage gain.
Need to bias the emitter terminal to below ground for active region operation.
Not widely used because of the need of a negative supply voltage.