## Slide 1: ECEN 350 Electronic Devices and Circuits
Operational Amplifiers.

## Slide 2
ECEN 350 – Topics
Semiconductor Physics
Diodes
BJTs
Rectifiers
MOSFETs
CMOS
Zeners
LEDs
Transistor Biasing
Small-Signal Analysis
Amplifier Gain Stages
Frequency Response
IC Op-Amps

## Slide 3: Operational Amplifiers – Op-Amps
Op-amp – Active circuit element designed to
perform the mathematical operations of addition,
subtraction, multiplication, division,
differentiation and integration.
The output of an op-amp behaves as a
voltage-controlled voltage-source.
Op-amps have very large open-loop voltage gain
(AV_OL > 50,000 at low frequency), resulting in
output saturation for relatively small voltage
differences on the inputs.
Most op-amp applications incorporate
negative feedback, referred to as closed-loop
operation. This feedback usually results in a
closed-loop gain that is much smaller in
magnitude than the open-loop gain.
Op-amp output is governed by the voltage difference between the + and - inputs. Since Vd = 0 for common-mode input signals they are rejected.

## Slide 4
Logarithms and decibels (dB)
Some Important Logarithmic Properties:
  log(P1P2) = log(P1) + log(P2). Similarly, log(P1/P2) = log(P1) - log(P2).
  log(P)n = nlog(P).
  log(1) = 0.
The decibel (dB) scale defined as GdB = Dimensionless ratio assigned the unit dB.
Power gain in dB: GdB =
Voltage gain in dB: AV_dB for .
Power Gain: GdB =
For , AV_dB
  K, where K = . Often this K is ignored when .

## Slide 5
Ex. 1: An op-amp has an open loop gain of 1 million at low frequencies, i.e., . What is the open loop gain in dB?
Ex. 2: A signal is first amplified by a voltage amplifier having 36 dB voltage
gain, then amplified by another amplifier with 32 dB voltage gain. What is
the overall dB voltage gain for the signal?
Many amplifiers, including op-amps utilize multiple voltage gain stages.
Voltage (dB) Example

## Slide 6: Ideal Voltage Follower
What is Vout and why in the adjacent circuit?
Vp = Vin. Vout = Vm.
Also, Vp = Vm. Therefore Vout = Vin.
Why does Vp = Vm?
Because of large open-loop voltage gain and negative feedback, Vout is always adjusts Vm towards Vp.
The only time that Vout is not adjusting Vm towards Vp, is when Vm = Vp, which implies Vout = Vin. Hence, Vout follows Vin.
If Vout became < Vin, then Vp > Vm, resulting in Vout increasing until Vm again equals Vp.
If Vout became > Vin, then Vp < Vm, resulting in Vout decreasing until Vm again equals Vp.
Since Vout = Vin, the resulting voltage gain with feedback, i.e., closed-loop gain = 1 because of negative feedback, whereas open-loop gain >> 1, where >> means much greater than.

## Slide 7: Feedback Control
Feedback control: Inverted Pendelum
Feedback control is used to keep the bottom (-) end of the pendulum in vertical alignment with the top (+) end, with the controller constantly minimizing any difference. As a result, the bottom (-) end follows the vertical position of the top (+) end of the inverted pendulum. The horizontal corrective response of the controller has to be larger than any misalignment to keep the pendelum inverted, making large horizontal gain and quick response time desirable. The larger the vertical mis-alignment, the larger the corrective response to minimize the misallignment.
Feedback control: Voltage Follower
Feedback control is used to keep the minus (-) input of the op-amp equal to the plus (+) input, with the op-amp output constantly minimizing any difference. As a result, the minus (-) input follows the voltage of the plus (+) input of the op-amp when the output is connected to the minus (-) input, referred to as negative feedback. The corrective response of the op-amp has to be larger than any |vp - vm|, for the output to follow the input, making large open-loop voltage gain and quick response time desirable. The larger the magnitude of vp - vm,, i.e., |vp - vm|, the larger the corrective response to minimize |vp - vm|.

## Slide 8: Voltage Divider and Follower Application
Measure a nominal 12 V battery with a microcontroller having
a 0 to 5 V ADC input range.
The voltage divider relationship applies when the current
in the top resistor equals the current in the bottom resistor,
meaning that it applies only for series circuits. Hence, we want
to sense voltage Va without taking any current from node Va.
The adjacent voltage follower amplifier does just that, sensing
the voltage Va without requiring any input current, so IR1 = IR2.
The voltage follower is said to buffer the voltage divider output.
For the adjacent circuit assuming an ideal op-amp, calculate the
output voltage Vout.
.
The voltage follower op-amp buffers the voltage divider output Va, providing an output voltage equal to Va even when driving a modest load resistor.
Ideal op-amps have zero output resistance, i.e. are ideal voltage sources.
Practical op-amps have 10 to 100 Ω output resistance and can provide up to 10 to 20 mA output current.
Poll Questions

## Slide 9: Non-Inverting Op-Amp Configuration
Note: Unlike the AC coupled BJT amplifiers to be discussed, with negataive feedback op-amps can amplify AC or DC signals, along with small or large signals. Hence, we will express the following closed-loop voltage gain as Vout/Vin rather than vout_p/vin_p.
How can we analyze the closed-loop voltage gain, AV i.e. Av = Vout/Vin
for the adjacent op-amp circuit?
Also Vm = Vp = Vin because of infinite open-loop voltage gain and negative feedback, which implies:
The closed-loop gain equals , whereas the open-loop gain is ideally infinite.
What is the overall input impedance of this stage?
Ideally input impedance = Vin/Iin = Vin/0 = ∞.
Closed-loop gain for non-inverting configuration.

## Slide 10: Inverting Op-Amp Configuration
How can we analyze the voltage gain, AV i.e. Av = Vout/Vin
for the adjacent op-amp circuit?
Vm = Vp because of infinite open-loop voltage
gain and negative feedback, which also implies
Vm = 0.
The fact that Vm = 0, when not tied to ground
is referred to as a virtual ground. A virtual ground appears as a short for voltage, yet an open for currents.
What is the overall input impedance of this stage?
Ideally input impedance = Vin/Iin = R1, because of virtual ground.
Non-inverting amplifier has better (higher) input impedance than the inverting amplifier.
Closed-loop gain for inverting op-amp configuration.

## Slide 11: Single-Ended versus Double-Ended (Differential) Signals
Single-Ended (SE) Signal  Referenced to ground.
Differential (Diff) Signal  Referenced to opposite polarity terminal which is not necessarily ground.
Differential Signals are more immune to noise and ground bounce compared to single-ended, as noise and ground bounce are common-mode signals, i.e. common to both inputs, which are rejected by a differential input stage.
Examples of Single-Ended signals are ground referenced voltages, along with standard digital logic signals and RS-232.
Example of a Differential Signals are the output voltages of a Wheatstone bridge, along with digital RS-485, USB, and Ethernet signals.

## Slide 12: Single-Ended versus Double-Ended (Differential) Voltages
Single-Ended (SE) Signal  Referenced to ground.
Differential (Diff) Signal  Referenced to opposite polarity terminal which is not necessarily ground.
Differential Signals are more immune to noise and ground bounce compared to single-ended, as noise and ground bounce are common-mode signals, i.e. common to both inputs, which are rejected by a differential input stage.
Differential Voltage PRT Measurement
Single-Ended Voltage Thermistor Measurement

## Slide 13: Single-Ended Voltage Measurement with Ground Noise
Single-Ended (SE) Signal  Referenced to ground.
Ground noise adds as to Vout in the adjacent resistive
bridge circuit, since VS is an ac ground, resulting in Vout = + .
This is not a problem when VR2 = >> Vnoise.
Thermistors have large resistance changes with temperature,
resulting in relatively large Vout variations with temperature.
Hence, the adjacent single-ended measurement scheme is often
used to arrive at the thermistor resistance based on measured Vout
along with the known value of fixed resistance R1.
Yet the adacent single-ended measurement scheme is not a good
choice to measure the resistance of a Platinum Resistance
Thermometer (PRT), as PRTs have much smaller resistance change
with temperature, resulting in a small change in Vout with temperature.
A differential output Wheatstone bride is a better choice for an accurate resistance measurement of a PRT.
Single-Ended Voltage Thermistor Measurement

## Slide 14: Differential Voltage Measurement with Ground Noise
Differential (Diff) Signal  Referenced to opposite polarity terminal which is not necessarily ground.
The common-mode noise results in Vd = VR2 + - VR4 + .
For a balanced Wheatstone bridge , and Vd = VR2 - VR4 + ,
where is common to both inputs, i.e.
, resulting
in Vd ≈ VR2 - VR4 + i.e. Vd = VR2 - VR4 + .
An ideal differential amplifier will only amplify the desired differential
signal Vd, while completely rejecting the unwanted common-mode noise, i.e. Vcm.
Practical differential amplifiers can achieve high Common-Mode Rejection,
such that the unwanted voltage Vcm is mostly eliminated from the measurement.
In the above Wheatstone bride, resistors R1, R3 and R4 are known, whereas RPRT is to be determined from Vd.
Amplifying Vd while rejecting Vcm prior to the Analog to Digital Converter (ADC) is necessary to accurately determine RPRT and it’s corresponding temperature. A differential input amplifier with good (high) Common-Mode Rejection is necessary for this task.
Differential Voltage PRT Measurement

## Slide 15: Common-Mode Rejection
Differential (Diff) Signal  Referenced to opposite polarity terminal which is not
necessarily ground.
The adjacent Wheatstone bridge circuit produces a differential voltage to be measured,
that is a function of RPRT, the resistance of the PRT (Platinum Resistance Thermometer).
Want a differential amplifier that will amplify the relatively small differential
signal Vd, while rejecting the unwanted common-mode noise Vcm of the adjacent
Wheatstone bridge circuit.
A differential input amplifier with good (high) Common-Mode Rejection is
necessary for this task.
A standard op-amp incorporating negative feedback is not sufficient as a differential
amplifier for a Wheatstone bridge, as there is only 1 remaining input.
Special differential amplifier ICs, referred to as instrumentation amplifiers (IAs), provide
the desired differential mode gain, along with good (large) common-mode rejection.

## Slide 16: Practical Differential Amplifier Circuit (Continued)
The adjacent op-amp difference amplifier has too low of input impedance for
general purpose use, so need to add buffer amplifiers to the front-end.
Adding voltage follower op-amps as buffers for the differential amplifier results in
very high input impedance along with good common-mode rejection with AV_Diff = 1.
The front-end buffer amplifiers can be configured as non-inverting amplifiers so as
to provide the very high input impedance, along with voltage gain > 1.
For purely common-mode inputs, the op-amp output voltages are equal, meaning
that no current flows through the R1 and R2 resistors. Hence the voltage Va simply
equals the common-mode input voltage for purely common-mode inputs.
For the adjacent circuit, the voltage at Va stays balanced a 0 V for purely differential
inputs, i.e., Va is a virtual ground for purely differential inputs.
Assume ½ of differential mode signal applied to Vin+ and ½ to Vin-.

## Slide 17: Classic 3-Op-Amp Instrumentation Amplifier (IA)
The adjacent circuit is referred to as the classic 3 op-amp
Instrumentation Amplifier (IA), which has the following
Differential and common-mode gain equations:
The factor of 2 in the differential mode gain comes from the
fact that R1 = RG/2 from the previous slide. Don’t actually
need two separate R1 resistors as shown on the previous slide
for a practical IA.
Instrumentation Amplifiers (IAs) are widely used for
amplifying and measuring low level signals, as they provide very high input impedance,
along with large common-mode rejection.
Voltage gain can be set by means of the R2/RG resistor ratio, with RG an external
resistor chosen by the user for the desired voltage gain. Typical IA voltage gains range
from 1 to 1000.
The reference pin provides a convenient way to level shift the output voltage for
single-supply applications, such as a microcontroller powered from a 5 V supply.

## Slide 18: AD8221 IC Instrumentation Amplifier (IA)
The AD8221 IA has improved performance over the classic AD620 IA.
The output voltage of an instrumentation amplifier is with respect to the REF terminal,
which can be used to dc level shift the output for single-supply systems such as the 0 to 5 V
system shown below.
The adjacent circuit uses a Wheatstone bridge so
as to provide 2.5 V on the Vin- input, which then gets
subtracted from the Vin+ input by the AD8221 IA.
The voltage applied to the REF pin must be between
–VS and +VS, and needs to meet the criteria of a stiff
voltage source in order to maintain the desired
reference voltage.
For a 0 and 5 V microcontroller application, the IA
output voltage can be centered around 2.5 V by
connecting the REF terminal to a reasonably stiff
2.5 V supply.

## Slide 19: AD8221 IC Instrumentation Amplifier Example 1
For the adjacent circuit determine Vin-, Vin+, and Vout
using 4 significant figures.
Vin- = (5.000 V)R4/(R3 + R4) = (5.000 V)(0.5000) = 2.500 V.
Vin- = 2.500 V.
Vin+ = (5.000 V)R2/(R1 + R2) =(5.000 V)(1006 Ω)/(2006 Ω).
Vin+ = 2.508 V.
Vout = AV(Vin+ - Vin-) + Vref = (100.0)(2.508 – 2.500) + 2.500 = 0.8000 V + 2.5 V = 3.300 V. Vout = 3.300 V.
Notice that resistors R3 and R4 of the Wheatstone bridge, do not equal resistor R1. R3 must equal R4 to set Vin- = Vs/2, but R3 and R4 do not need to equal R1. Choosing R3 and R4 resistor values that are larger than R1 and R2 helps reduce the required current.
The IA output voltage in the above circuit could be measured by means of a microcontroller Analog-to-Digital Converter (ADC) having a 0 to 5 V input range.

## Slide 20: Instrumentation Amplifiers (IAs) versus Op-Amps
Why use an IA versus a regular op-amp, as op-amps offer differential inputs?
While op-amps offer differential inputs, the resulting voltage gain, i.e., open-loop voltage gain, is very large and not well controlled. Hence, op-amps cannot provide a well controlled voltage gain for differential inputs.
To get a well controlled, i.e., closed-loop, gain from an op-amp, negative feedback must be employed which then uses the minus input, leaving only a single input. Hence, op-amps can only amplify single-ended signals in closed-loop configurations.
Whereas Instrumentation Amplifiers (IAs) provide well-controlled gain for differential input signals.
Wheatstone bridges are commonly used to provide differential signals from sensors that have small ∆R/R changes to the quantity being sensed, such as PRT’s and Strain Gauges.
IAs are commonly used to buffer and amplify the low-level differential voltages from Wheatstone bridges associated with PRT’s and Strain Gauges.
IAs can also be used for single-ended inputs, by simply tying the minus input to the signal reference (ground).

## Slide 21: AD8221 IC Instrumentation Amplifier Example 2
The adjacent circuit includes an AD8221 Instrumentation Amplifier (IA)
to amplify the differential voltage from a Wheatstone Bridge. Resistor R2
models the possible resistance from a 350 Ω Strain Gauge sensor. For the
adjacent circuit use hand calculations to determine AV, Vin+, Vin-, and Vout
with respect to Vref, where Vref is considered the reference voltage, i.e.
output voltage associated with Vin+ - Vin- = 0 V, in this 0 to 5 V circuit.
The differential mode voltage gain of the AD8221 is as follows:
AV.
Vin+.
Vin+ = (5.0 V)R2/(R1 + R2) = (5.0 V)(355 Ω)/(350 Ω + 355 Ω) = 2.52 V. Vin+ = 2.52 V.
Vin-.
Vin- = (5.0 V)R4/(R3 + R4) = (5.0 V)(0.50) = 2.50 V. Vin- = 2.50 V.

## Slide 22: AD8221 IC IA Example 2 (Continued)
The adjacent circuit includes an AD8221 Instrumentation Amplifier (IA)
to amplify the differential voltage from a Wheatstone Bridge. Resistor R2
models the possible resistance from a 350 Ω Strain Gauge sensor. For the
adjacent circuit use hand calculations to determine AV, Vin+, Vin-, and Vout
with respect to Vref, where Vref is considered the reference voltage, i.e.,
output voltage associated with Vin+ - Vin- = 0 V, in this 0 to 5 V circuit.
From the previous slide: Vin+ = 2.52 V. Vin- = 2.50 V.
Vout.
Vout = AV(Vin+ - Vin-) + Vref = (10.0)(2.52 – 2.50) + 2.50 = 0.20 V + 2.5 V = 2.70 V.

## Slide 23: Instrumentation Amplifier as a Buffer
DMM Measurement Details Lab Circuit.
10 MΩ output (Thevenin) resistance equals
10 MΩ input resistance of a standard DMM.
Result is a voltage divider with a standard DMM
measuring approximately 2.5 V instead of 5.0 V. (-50%).
Need a buffer stage, i.e. very high input impedance, followed by relatively low output impedance to fix this measurement problem.
Instrumentation Amplifier does the job well.
For the buffer output, the 10 MΩ input resistance of a
standard DMM is no problem because of the relatively low
output-impedance of the IA.
Ideally hand-held DMMs report a measured voltage
equal to Vth with buffer circuit.

## Slide 24: Practical Differential Amplifier Circuit
The adjacent op-amp based amplifier is referred to as a differential or difference
amplifier as the output voltage is proportional to the difference Vin+ – Vin-.
Superposition can be used to determine the differential voltage gain AV.
Superposition Part a: Set Vin+ = 0. This results in an inverting amplifier configuration.
Superposition Part b: Set Vin- = 0. This results in a non-inverting amplifier configuration.

## Slide 25: Practical Differential Amplifier Circuit (Continued)
The resulting circuit amplifies differential voltages while rejecting
common-mode voltages, i.e. voltages common to both the Vin+ and Vin- inputs.
Ideally R1 = R1’ and R2 = R2’, i.e. R1 and R1’ are matched resistors.
Practically, R1’ is slightly different that R1, and R2’ is slightly different than R2.
Non-ideal resistor matching results in non-zero common-mode gain.
For R1 = R2, AV_CM = ±2∆R/R. For example with ±0.1% resistor matching = 0.1/100 =0.001.

## Slide 26: Practical Differential Amplifier Circuit (Continued)
For R1 = R2, Vout = Vin+ - Vin-.
LT5400A offers 4 matched resistors with ±0.01% matching with
0.2 ppm/˚C, i.e. 0.2 x 10-6 per ˚C, temperature coefficient (TC) matching.
The following circuit illustrates a difference amplifier
circuit implemented with an LT5400.
The adjacent circuit provides a differential mode gain of 1,
along with good rejection of Common-Mode Signals.

## Slide 27: Practical Voltage Follower
For an ideal op-amp Vp = Vm, and for Vin = 1.00 V, Vout = 1.00 V for the
voltage follower configuration.
Yet if Vp = Vm, and Vp – Vm = 0 V, then doesn’t Vout = AV(Vp – Vm ) = 0?
Mathematically, Vout = (∞)(0 V) is indeterminate for an ideal op-amp.
Practical op-amps have open-loop gains < ∞, resulting in the voltage follower output approximately equal to Vin.
For example, given an open loop gain AV = 1 x 106, and Vp = Vin = 1.00 V, Vout = Vm ≈ 1.00 V.
In the above circuit, since Vout = AV(Vp – Vm ) = (1 x 106)(Vp – Vm ) ≈ 1.00 V, with (1 x 106)(1 µV) = 1.00 V.
Therefore, Vp - Vm ≈ 1 µV, meaning Vm = Vout = 1.00 V - 1 µV = 0.999999 V instead of 1.00 V.
So for the above voltage follower with an open loop gain AV = 1 x 106, and Vp = Vin = 1.00 V, Vout = Vm = 1.00 V - 1 µV = 0.999999 V, which is close enough to 1.00 V for practical applications.
A large open-loop gain and negative feedback associated with op-amps result in Vp ≈ Vm , which for hand calculations is well approximated as Vp = Vm.

## Slide 28
ECEN 350 – Topics
Semiconductor Physics
Diodes
BJTs
Rectifiers
MOSFETs
CMOS
Zeners
LEDs
Transistor Biasing
Small-Signal Analysis
Amplifier Gain Stages
Frequency Response
IC Op-Amps

## Slide 29
The End

## Slide 30
Extra

## Slide 31: Current Source Circuit
This current source works by forcing a constant
voltage, Vcc – Vref, across a known resistor, Rsense,
resulting in a constant current flowing through
Rsense.
The approximation IE = IC is utilized.

## Slide 32: Peak Detector Circuit
Diode D1 results in maximum or peak voltage remaining on capacitor C1.
Vout = Vin_max.

## Slide 33: Operational Amplifiers – Op-Amps
Op-amp – Active circuit element designed to perform the mathematical operations of addition, subtraction, multiplication, division, differentiation and integration.
Name “Operational” comes from analog computer days in which op-amps and other components were used to implement mathematical operations.
The output of an op-amp behaves as a voltage source controlled by the voltage difference between the Vp and Vm inputs, and Ro fairly small, ideally zero.
Op-amp outputs behave like a voltage-controlled voltage-sources.
Op-amp output is governed by the voltage difference between the + and - inputs. Since Vd = 0 for common-mode input signals they are rejected.

## Slide 34: Operational Amplifiers – Op-Amps
Op-amp – Active circuit element designed to perform the mathematical operations of addition, subtraction, multiplication, division, differentiation and integration.
Name “Operational” comes from analog computer days in which op-amps and other components were used to implement mathematical operations.
The output of an op-amp behaves as a voltage source controlled by the voltage difference between the Vp and Vm inputs, and Ro fairly small, ideally zero.
Op-amp outputs behave like a voltage-controlled voltage-sources.
Op-amp output is governed by the voltage difference between the + and - inputs. Since Vd = 0 for common-mode input signals they are rejected.

## Slide 35: Open-Loop Op-Amp Transfer Function
Op-amps have very large open-loop voltage gain (AV_OL > 50,000 at low frequency), resulting in output saturation for relatively small voltage differences on the inputs.
An op-amp operating without negative feedback, i.e. a connection between the output and the inverting input, is said to be operating open-loop, with the output usually saturated, i.e. maxed out at one of the power supply rails.
Most op-amp applications incorporate negative feedback, referred to as closed-loop operation. This feedback usually results in a closed-loop gain that is much smaller in magnitude than the open-loop gain.

## Slide 36: Feedback Control
Feedback control: Inverted Pendelum
Feedback control is used to keep the bottom (-) end of the pendulum in vertical alignment with the top (+) end, with the controller constantly minimizing any difference. As a result, the bottom (-) end follows the vertical position of the top (+) end of the inverted pendulum. The horizontal corrective response of the controller has to be larger than any misalignment to keep the pendelum inverted, making large horizontal gain and quick response time desirable. The larger the vertical mis-alignment, the larger the corrective response to minimize the misallignment.
vp
vm
Feedback control: Voltage Follower
Feedback control is used to keep the minus (-) input of the op-amp equal to the plus (+) input, with the op-amp output constantly minimizing any difference. As a result, the minus (-) input follows the voltage of the plus (+) input of the op-amp when the output is connected to the minus (-) input, referred to as negative feedback. The corrective response of the op-amp has to be larger than any |vp - vm|, for the output to follow the input, making large open-loop voltage gain and quick response time desirable. The larger the magnitude of vp - vm,, i.e., |vp - vm|, the larger the corrective response to minimize |vp - vm|.
Poll Questions.

## Slide 37: Feedback Control
Hot
Cold
Feedback control:
Use negative (balancing) feedback to minimize the difference between the desired water temperature and the actual water temperature.
Feedback control:
Use negative feedback (negative because output is connected to minus input) to minimize the difference between the desired output voltage and the actual output voltage.

## Slide 38: Operational Amplifiers  Op-Amps
What is needed for a modern Integrated Circuit (IC) op-amp?
  Differential input stage.
  Single-ended output.
  Very large open-loop voltage gain.
  Very small input current into the + and – inputs.
  Differential input stage is fundamental to op-amp construction in order to attenuate amplify voltage differences between the + and – inputs while attenuating voltages common to both inputs.
  Additional gain stages used to provide overall open-loop voltage gain.
  For integrated Circuits (ICs), need to build op-amps out of mostly transistors and diodes, with resistors as needed along with small value (< 100 pf) capacitors as needed.
  Hence coupling and bypass capacitors are not an option, rather dc coupling is utilized.

## Slide 39: Op-Amps (Continued)
Because of the large open-loop voltage gain, if the voltage on
the non-inverting input is slightly greater than the voltage on
the inverting input, then the output will increase in voltage
towards VCC.
Likewise, if the voltage on the inverting input is slightly
greater than the voltage on the non-inverting input, then
the output will decrease in voltage towards VEE.
Op-amp output is governed by the voltage difference between the + and - inputs. Since Vd = 0 for common-mode input signals they are rejected.

## Slide 40: Ideal Op-Amps
An ideal op-amp utilizes the following three assumptions, commonly used for hand calculations:
1. Infinite open-loop gain, i.e. AV = ∞.
2. Infinite input resistance, meaning current into the two input terminals equals 0.00 µA.
3. Zero output resistance, which is the assumption made for an ideal voltage source.
Parameter | Typical Range | Ideal Values
Open-Loop Voltage Gain, AV | 105 to 108 | ∞
Input Resistance, Ri | 105 to 1013 Ω | ∞ Ω
Output Resistance, Ro | 10 to 100 Ω | 0 Ω
Supply Voltage Range (VCC – VEE) | 5 V to 30 V | Any Value

## Slide 41: Op-Amps (Continued)
Why can we assume the current into the minus and plus inputs is zero?
Because a differential amplifier input stage is used,
along with high β transistors for low input currents.
Input bias currents into differential pair input transistors usually in the range of pA to nA,
which is often negligible.

## Slide 42: Voltage Follower with Buffer Transistor
What is Vout and why?
Vp = Vi. Vo = Vm.
Also Vm = Vp. Therefore Vo = Vi.
Why does Vm = Vp?
Because of large open-loop voltage gain and negative feedback.
The resulting voltage gain with feedback, i.e. closed-loop gain = 1 because of negative feedback, whereas open-loop gain >> 1.
Why would you add Q1?
Because Q1 can provide much more current to Rload than the op-amp output.

## Slide 43: Voltage Follower as a Buffer
DMM Measurement Details Lab Circuit.
10 MΩ output (Thevenin) resistance equals
10 MΩ input resistance of a standard DMM.
Result is a voltage divider with a standard DMM
measuring approximately 5.0 V instead of 10 V. (-50%).
Need a buffer stage, i.e. very high input impedance, followed by relatively low output impedance to fix this measurement problem.
Voltage follower configuration does the job well.
For the buffer output, the 10 MΩ input
resistance of a standard DMM is no problem
because of the relatively low
output-impedance of the voltage-follower
op-amp.
Ideally hand-held DMM reports a measured voltage equal to Vth with buffer circuit.

## Slide 44: Voltage Follower Application
The voltage divider relationship applies when IR1 = IR2, meaning
that it only applies for series circuits. The adjacent voltage follower
amplifier buffers the output of the voltage divider, sensing the
voltage Va without requiring any input current, so IR1 = IR2. Hence, the
voltage divider relationship applies, resulting in an output voltage Vout
that equals Va from the voltage divider. For the adjacent circuit assuming
an ideal op-amp, calculate the output voltage Vout.
.
The voltage follower op-amp buffers the voltage divider output Va, providing an output voltage equal to Va even when the op-amp output drives a modest load resistor.
Ideal op-amps have zero output resistance, i.e. are ideal voltage sources.
Practical op-amps have 10 to 100 Ω output resistance and can provide 10 to 20 mA output current.

## Slide 45: Buffered Op-Amp Using BJT Emitter Follower
For the adjacent circuit, what is Vout?
Because op-amp output adjusts the base-to-emitter voltage of the BJT until the BJT collector current Ic multiplied by Rload = Vin, i.e. the output voltage is regulated over a wide range of load resistance values, termed a Voltage Regulator.
Voltage Regulators may need to provide more than 1 A of output current.
BJT source-follower in above circuit increases output current well beyond the 10 to 20 mA possible from the op-amp output.

## Slide 46: Buffered Op-Amp Using MOSFET Source Follower
Ideal op-amps have zero output resistance, i.e. are ideal
voltage sources.
Practical op-amps have 10 to 100 Ω output resistance and
can only provide 10 to 20 mA output current.
Voltage Regulators may need to provide more than 1 A
of output current.
MOSFET source-follower in above circuit increases output
current well beyond the 10 to 20 mA possible from the op-amp
output.
For the above circuit, Vout = Vref. Why?
Because op-amp output adjusts the gate-to-source voltage of the MOSFET until the MOSFET drain current ID multiplied by Rload = Vref, i.e. Voltage Regulator.

## Slide 47: Voltage Regulator with Current Limit
When Q1 is in cutoff, Vout = Vref.
Yet when Q1 turns on, Iout_max = Ilim.
How do we calculate Ilim?
Ilim ≈ (0.66 V)/(4.2 Ω) = 157 mA. Why?
When Q1 turns on it limits the gate-to-source
voltage of M1, even when the op-amp is tries to increase
the gate-to-source voltage. Hence, the gate-to-source voltage of M1 equals the voltage necessary for ID = Ilim in current limit.
In current limit Vout, no longer equals Vref, and instead equals (Ilim)Rload.
This effective and simple current limit is much more convenient than a 1-time blowable fuse for circuit protection.
For the above circuit, what is the maximum power dissipation of M1 assuming Vout = Vref?
PM1 = [VDD - Vout - ILimit(4.2 Ω)](Ilimit). The maximum output current is often limited by power dissipation of M1.

## Slide 48: Classic 741 Op-Amp
A component-level diagram of the common 741 op-amp. Dotted lines outline: current mirrors (red); differential amplifier (blue); output gain stage (magenta); voltage level shifter (green); emitter-follower output stage (cyan).
VBE Current Limit.
Emitter Follower
Emitter Follower

## Slide 49: AD8221 IC Instrumentation Amplifier Example 2
Platinum Resistance Thermometers (PRTs) provide
accurate temperature measurements based on the
positive temperature coefficient of resistance of platinum
metal.
A 100 Ω PRT has a nominal resistance of 100 Ω @ 0˚C.
One type of 100 Ω PRTs offers a TCR of 0.3851 Ω/˚C.
This 100 Ω PRT resistance versus temperature can be modeled mathematically as follows for a 1st approximation:
    R(T) = (100 Ω)[1 + 0.003851(T)], for T in ˚C.
The Wheatstone bridge provides a differential signal that is nominally 0.0 mV, when the PRT resistance equals 100 Ω.
Notice that resistors R3 and R4 of the Wheatstone bridge, do not equal resistor R1 and RPRT at 0˚C. Resistor values larger than 100 Ω are chosen for R3 and R4 in order to reduce the required current.
The IA output voltage is to be measured by means of a microcontroller Analog-to-Digital Converter (ADC), and then PRT temperature determined by the appropriate output voltage to temperature conversion equation.